| 24-451 | Feedback Control Systems | Fall 2000 |
| --- | --- | --- |

Homework #1

Due Tuesday 12 September at 3 pm

- (5 points.) Use the defining integral of the Laplace transform and elementary properties of integrals to show the linearity of the Laplace transform, i.e., for functions f(t) and g(t) and real scalars a and b, one has

- (5 points.) Use the defining integral of the Laplace transform to prove the differentiation theorem of the Laplace transform, i.e., if F(s)=L[f(t)], then

Hint: In general, given a function g(t) with a step discontinuity at t=0, one has

- (10 points.) Use the defining integral of the Laplace transform to derive the Laplace transform of .

- (16 points.) Use the differentiation and time delay theorems of the Laplace transform to respectively show the following:

# (24 points.) Assuming zero initial conditions, solve the following differential equations using the Laplace transform:

Use the MATLAB function residue to verify the partial fraction expansion in each case.