## Slide 1: 14-736 Distributed Systems
Lecture 26:
Internet Routing as a DS Problem

## Slide 2: Outline
Intro
Distance Vector
Link State

## Slide 3: Graph Model
Represent each router as node
Direct link between routers represented by edge
  Symmetric links  undirected graph
Edge “cost” c(x,y) denotes measure of difficulty of using link
  delay, $ cost, or congestion level
Task
  Determine least cost path from every node to every other node
    Path cost d(x,y) = sum of link costs
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 4: Routes from Node A
Properties
  Some set of shortest paths forms tree
    Shortest path spanning tree
  Solution not unique
    E.g., A-E-F-C-D also has cost 7
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Forwarding Table for A |  | 
Dest | Cost | Next Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E

## Slide 5: Key Challenges
This would be easy if the graph didn’t change
But, what happens as links are removed and are added?
  Links fail
  Links heal
Internet routing is basically a big distributed agreement problem
  If routers agree on the graph, they can make consistent decisions
  If routers disagree on the graph, badness can happen
    Cycles are a notable problem
    Lost packets are another (time out)

## Slide 6: Ways to Compute Shortest Paths
Centralized
  Collect graph structure in one place
  Use standard graph algorithm
  Disseminate routing tables
Link-state
  Every node collects complete graph structure
  Each computes shortest paths from it
  Each generates own routing table
Distance-vector
  No one has copy of graph
  Nodes construct their own tables iteratively
  Each sends information about its table to neighbors

## Slide 7: Outline
Intro
Distance Vector
Link State

## Slide 8: Distance-Vector Method
Idea
  At any time, have cost/next hop of best known path to destination
  Use cost  when no path known
Initially
  Only have entries for directly connected nodes
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Initial Table for A |  | 
Dest | Cost | Next Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F

## Slide 9: Distance-Vector Update
Update(x,y,z)
  d  c(x,z) + d(z,y) # Cost of path from x to y with first hop z
  if d < d(x,y)
    # Found better path
    return d,z # Updated cost / next hop
  else
    return d(x,y), nexthop(x,y) # Existing cost / next hop
x
z
y
c(x,z)
d(z,y)
d(x,y)

## Slide 10: Algorithm
Bellman-Ford algorithm
Repeat
  For every node x
  For every neighbor z
  For every destination y
  d(x,y)  Update(x,y,z)
Until converge

## Slide 11: Start
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C |  | –
D | 3 | D
E |  | –
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A |  | –
B |  | –
C | 0 | C
D | 1 | D
E |  | –
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A |  | –
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F |  | –
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B |  | –
C |  | –
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 6 | A
B | 1 | B
C | 1 | C
D |  | –
E | 3 | E
F | 0 | F
Optimum 1-hop paths

## Slide 12: Iteration #1
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 7 | F
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 7 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 2-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 13: Iteration #2
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 6 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E | 5 | C
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D | 5 | F
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 3-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 14: Distance Vector: Link Cost Changes
Link cost changes:
Node detects local link cost change
Updates distance table
If cost change in least cost path, notify neighbors
X
Z
1
4
50
Y
1
algorithm
terminates
“good
news
travels
fast”

## Slide 15: Distance Vector: Link Cost Changes
Link cost changes:
Good news travels fast
Bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 16: Distance Vector: Split Horizon
If Z routes through Y to get to X :
Z does not advertise its route to X back to Y
algorithm
terminates
X
Z
1
4
50
Y
60
?
?
?

## Slide 17: Distance Vector: Poison Reverse
If Z routes through Y to get to X :
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
Immediate notification of unreachability, rather than split horizon timeout waiting for advertisement
Will this completely solve count to infinity problem?
X
Z
1
4
50
Y
60
algorithm
terminates

## Slide 18: Poison Reverse Failures
Iterations don’t converge
“Count to infinity”
Solution
  Make “infinity” smaller
  What is upper bound on maximum path length?
Table for A |  | 
Dst | Cst | Hop
C | 7 | F
Table for B |  | 
Dst | Cst | Hop
C | 8 | A
Table for F |  | 
Dst | Cst | Hop
C | 1 | C
Table for F |  | 
Dst | Cst | Hop
C |  | –
Table for A |  | 
Dst | Cst | Hop
C |  | –
Forced
Update
Table for B |  | 
Dst | Cst | Hop
C | 14 | A
Forced
Update
F
C
6
1
1
1
B
D
A
4

Table for D |  | 
Dst | Cst | Hop
C | 9 | B
Forced
Update
Table for A |  | 
Dst | Cst | Hop
C | 13 | D
Better
Route
Table for D |  | 
Dst | Cst | Hop
C | 15 | B
Table for A |  | 
Dst | Cst | Hop
C | 19 | D
Forced
Update
•
•
•
Forced
Update

## Slide 19: Routing Information Protocol (RIP)
Earliest IP routing protocol (1982 BSD)
  Current standard is version 2 (RFC 1723)
Features
  Every link has cost 1
  “Infinity” = 16
    Limits to networks where everything reachable within 15 hops
Sending Updates
  Every router listens for updates on UDP port 520
  RIP message can contain entries for up to 25 table entries

## Slide 20: RIP Updates
Initial
  When router first starts, asks for copy of table for every neighbor
  Uses it to iteratively generate own table
Periodic
  Every 30 seconds, router sends copy of its table to each neighbor
  Neighbors use it to iteratively update their tables
Triggered
  When every entry changes, send copy of entry to neighbors
    Except for one causing update (split horizon rule)
  Neighbors use it to update their tables

## Slide 21: RIP Staleness / Oscillation Control
Small Infinity
  Count to infinity doesnt take very long
Route Timer
  Every route has timeout limit of 180 seconds
    Reached when haven’t received update from next hop for 6 periods
  If not updated, set to infinity
  Soft-state refresh  important concept!
Behavior
  When router or link fails, can take minutes to stabilize
Notes:   Lots of subtlety to get good implementation (RFC 1058).

## Slide 22: Outline
Intro
Distance Vector
Link State

## Slide 23: Link State Protocol Concept
Every node gets complete copy of graph
  Every node “floods” network with data about its outgoing links
Every node computes routes to every other node
  Using single-source, shortest-path algorithm
Process performed whenever needed
  When connections die / reappear

## Slide 24: Sending Link States by Flooding
X Wants to Send Information
  Sends on all outgoing links
When Node Y Receives Information from Z
  Send on all links other than Z
X
A
C
B
D
(a)
X
A
C
B
D
(b)
X
A
C
B
D
(c)
X
A
C
B
D
(d)

## Slide 25: Dijkstra’s Algorithm
Given
  Graph with source node s and edge costs c(u,v)
  Determine least cost path from s to every node v
Shortest Path First Algorithm
  Traverse graph in order of least cost from source

## Slide 26: Dijkstra’s Algorithm: Concept
Node Sets
  Done
    Already have least cost path to it
  Horizon:
    Reachable in 1 hop from node in Done
  Unseen:
    Cannot reach directly from node in Done
Label
  d(v) = path cost from s to v
Path
  Keep track of last link in path
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
5
3


Current Path Costs

## Slide 27: Dijkstra’s Algorithm: Initially
No nodes done
Source in horizon
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0





Current Path Costs

## Slide 28: Dijkstra’s Algorithm: Initially
d(v) to node A shown in red
  Only consider links from done nodes
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
6
3


Current Path Costs

## Slide 29: Dijkstra’s Algorithm
Select node v in horizon with minimum d(v)
Add link used to add node to shortest path tree
Update d(v) information
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
3


Current Path Costs
6
5

## Slide 30: Dijkstra’s Algorithm
Repeat…
A
C
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
5
3


Current Path Costs
F
B
D
E

## Slide 31: Dijkstra’s Algorithm
Update d(v) values
  Can cause addition of new nodes to horizon
2
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
4
3

6
Current Path Costs
A
C
3
D
B
E
F

## Slide 32: Dijkstra’s Algorithm
Final tree shown in green
2
6
3
1
1
2
3
Source
Node
0
2
4
3
5
6
A
C
3
D
B
E
F

## Slide 33: Link State Characteristics
With consistent LSDBs*, all nodes compute consistent loop-free paths
Can still have transient loops
A
B
C
D
1
3
5
2
1
Packet from CA
may loop around BDC
if B knows about failure
and C & D do not
X
Link State Data Base

## Slide 34: OSPF Routing Protocol
Open
  Open standard created by IETF
Shortest-path first
  Another name for Dijkstra’s algorithm
More prevalent than RIP

## Slide 35: OSPF Reliable Flooding
Transmit link state advertisements
  Originating router
    Typically, minimum IP address for router
  Link ID
    ID of router at other end of link
  Metric
    Cost of link
  Link-state age
    Incremented each second
    Packet expires when reaches 3600
  Sequence number
    Incremented each time sending new link information

## Slide 36: OSPF Flooding Operation
Node X Receives LSA from Node Y
  With Sequence Number q
  Looks for entry with same origin/link ID
Cases
  No entry present
    Add entry, propagate to all neighbors other than Y
  Entry present with sequence number p < q
    Update entry, propagate to all neighbors other than Y
  Entry present with sequence number p > q
    Send entry back to Y
    To tell Y that it has out-of-date information
  Entry present with sequence number p = q
    Ignore it

## Slide 37: Flooding Issues
When should it be performed
  Periodically
  When status of link changes
    Detected by connected node
What happens when router goes down & back up
  Sequence number reset to 0
    Other routers may have entries with higher sequence numbers
  Router will send out LSAs with number 0
  Will get back LSAs with last valid sequence number p
  Router sets sequence number to p+1 & resends

## Slide 38: Adoption of OSPF
RIP viewed as outmoded
  Good when networks small and routers had limited memory & computational power
OSPF Advantages
  Fast convergence when configuration changes

## Slide 39: Comparison of LS and DV Algorithms
Message complexity
LS: with n nodes, E links, O(nE) messages
DV: exchange between neighbors only
Speed of Convergence
LS: Relatively fast
  Complex computation, but can forward before computation
  may have transient loops
DV: convergence time varies
  may have routing loops
  count-to-infinity problem
  faster with triggered updates
Space requirements:
  LS maintains entire topology
  DV maintains only neighbor state
Robustness: router malfunctions
LS: Node can advertise incorrect link cost
  Each node computes its own table
DV: Node can advertise incorrect path cost
  Each node’s table used by others (error propagates)

## Slide 40: Outline
Distance Vector
Link State
Routing Hierarchy

## Slide 41: EXTRA SLIDES
The rest of the slides are FYI

## Slide 42: RIP Table Processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated

## Slide 43: Dijsktra’s Algorithm
1 Initialization:
2 N = {A}
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v)
6 else D(v) = infinity
7
8 Loop
9 find w not in N such that D(w) is a minimum
10 add w to N
11 update D(v) for all v adjacent to w and not in N:
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N

## Slide 44: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
start N
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
2,A
2,A
D(C),p(C)
5,A
4,D
3,E
3,E
D(D),p(D)
1,A
D(E),p(E)
infinity
2,D
D(F),p(F)
infinity
infinity
4,E
4,E
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5