## Slide 1
14-513
18-613

## Slide 2: Floating Point 14-513/18-613: Introduction to Computer Systems 3rd Lecture, May 21, 2020

## Slide 3: Recall the “Number Line Challenge”
Given a specific bit-width, we get only a specific number of points on our number line. We can assign them whatever meaning we like, but that’s all we get.
Consider some examples for a 3-bit number line:
  000 001 010 011 100 101 110 111
  -2 -1.5 -1 -0.5 0 0.5 1 1.5
  A B C D E F G H

## Slide 4: So, Where Do Fractions Fit In?
For some applications range is important – things are large and details don’t matter
  Think telescope
For some applications resolution is important and nothing is large
  Thing microscope
We could solve this problem by using different types, e.g. one for large things and one for small things
  But, then what happens when math involved both?
We want a unified numbering system where we have more resolution for small things and more range for large things.

## Slide 5: IEEE’s Answer
Notice how the distribution gets denser toward zero.
8 values

## Slide 6: Distribution of Values (close-up view)
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 7: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
  Some CPUs don’t implement IEEE 754 in full e.g., early GPUs, Cell BE processor
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard

## Slide 8: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 9: Fractional Binary Numbers: Examples
Value Representation
5 3/4 = 23/4 101.112 = 4 + 1 + 1/2 + 1/4
2 7/8 = 23/8 010.1112 = 2 + 1/2 + 1/4 + 1/8
1 7/16 = 23/16 001.01112 = 1 + 1/4 + 1/8 + 1/16
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 10: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
    Limited range of numbers (very small values? very large?)

## Slide 11: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac
  Example: 1521310 = (-1)0 x 1.11011011011012 x 213

## Slide 12: Precision options
Single precision: 32 bits  7 decimal digits, 10±38
Double precision: 64 bits  16 decimal digits, 10±308
Other formats: half precision, quad precision
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits

## Slide 13: Three “kinds” of floating point numbers
s | exp | frac
1 | e-bits | f-bits
00…00
exp ≠ 0 and exp ≠ 11…11
11…11
denormalized
normalized
special

## Slide 14: Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 15: “Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = exp – Bias
  exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (exp: 1…254, E: -126…127)
    Double precision: 1023 (exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E

## Slide 16: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac
v = (–1)s M 2E
E = exp – Bias
Bias = 2k-1 - 1

## Slide 17: Denormalized Values
Condition: exp = 000…0
Bias is the same as for normalized numbers
  Bias = 2k-1 - 1, where k is number of exponent bits
Exponent value: E = 1 – Bias (instead of exp – Bias) (why?)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced
v = (–1)s M 2E
E = 1 – Bias
Bias = 2k-1 - 1

## Slide 18: Denormalized Encoding Example
s
exp
frac
v = (–1)s M 2E
E = 1 – Bias
Bias = 2k-1 - 1
Value: float F = 0.5;
Base 2 Scientific Notation
  0.510 = 1.0 x 2-1
Converting to a leading 0
  1.0 x 2-1 = 0.1 x 20
Exponent
  Bias = 2k-1 - 1 = 22-1 – 1 = 2 – 1 = 1
  E = 1 – Bias = 1 – 1 = 0
  Exp = 00
  Frac = 0.12
Result: 0 00 100

## Slide 19: Special Values
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0

## Slide 20: C float Decoding Example
float: 0xC0A00000
binary:
1 | 8-bits | 23-bits
E = 129
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E =
  Bias = 2k-1 – 1 = 127

## Slide 21: C float Decoding Example #1
E = 129
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E =
float: 0xC0A00000
binary: 1100 0000 1010 0000 0000 0000 0000 0000
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 | 8-bits | 23-bits

## Slide 22: C float Decoding Example #1
float: 0xC0A00000
binary: 1100 0000 1010 0000 0000 0000 0000 0000
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 | 8-bits | 23-bits
E = exp – Bias = 129 – 127 = 2 (decimal)
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E = (-1)1 * 1.25 * 22 = -5
  Bias = 2k-1 – 1 = 127

## Slide 23: C float Decoding Example #2
E = 129
S = 1 -> negative number
M = 0.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = 1 – Bias
v = (–1)s M 2E =
float: 0x001C0000
binary: 0000 0000 0001 1100 0000 0000 0000 0000
0 | 0000 0000 | 001 1100 0000 0000 0000 0000
1 | 8-bits | 23-bits

## Slide 24: C float Decoding Example #2
float: 0x001C0000
E = 1 – Bias = 1 – 127 = –126 (decimal)
S = 0 -> positive number
M = 0.001 1100 0000 0000 0000 0000
M = 1/8 + 1/16 + 1/32 = 7/32 = 7*2–5
v = (–1)s M 2E
E = 1 – Bias
v = (–1)s M 2E = (-1)0 * 7*2–5 * 2–126 = 7*2–131
  Bias = 2k-1 – 1 = 127
binary: 0000 0000 0001 1100 0000 0000 0000 0000
0 | 0000 0000 | 001 1100 0000 0000 0000 0000
1 | 8-bits | 23-bits
v ≈ 2.571393892 X 10–39

## Slide 25: Tiny Floating Point Example
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exp, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 26: Dynamic Range (s=0 only)
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
norm: E = exp – Bias
denorm: E = 1 – Bias
(-1)0(0+1/4)*2-6
(-1)0(1+1/8)*2-6

## Slide 27: Special Properties of the IEEE Encoding
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield? The answer is complicated.
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 28: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 29: Floating Point Operations: Basic Idea
x +f y = Round(x + y)
x f y = Round(x  y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac

## Slide 30: Rounding
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−) $1 $1 $1 $2 –$2
  Round up (+) $2 $2 $2 $3 –$1
  Nearest Even* (default) $1 $2 $2 $2 –$2
*Round to nearest, but if half-way in-between then round to nearest even

## Slide 31: Closer Look at Round-To-Even
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
    C99 has support for rounding mode management
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    7.8949999 7.89 (Less than half way)
    7.8950001 7.90 (Greater than half way)
    7.8950000 7.90 (Half way—round up)
    7.8850000 7.88 (Half way—round down)

## Slide 32: Rounding Binary Numbers
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 33: Rounding
Round up conditions
  Round = 1, Sticky = 1 ➙ > 0.5
  Guard = 1, Round = 1, Sticky = 0 ➙ Round to even
  Fraction GRS Incr? Rounded
  1.0000000 000 N 1.000
  1.1010000 100 N 1.101
  1.0001000 010 N 1.000
  1.0011000 110 Y 1.010
  1.0001010 011 Y 1.001
  1.1111100 111 Y 10.000
1.BBGRXXX
Guard bit: LSB of result
Round bit: 1st bit removed
Sticky bit: OR of remaining bits

## Slide 34: FP Multiplication
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands
4 bit significand: 1.010*22 x 1.110*23 = 10.0011*25
= 1.00011*26 = 1.001*26

## Slide 35: Floating Point Addition
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up
1.010*22 + 1.110*23 = (0.1010 + 1.1100)*23
= 10.0110 * 23 = 1.00110 * 24 = 1.010 * 24

## Slide 36: Mathematical Properties of FP Add
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
Yes
No
Almost
Almost

## Slide 37: Mathematical Properties of FP Mult
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 38: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 39: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 40: Floating Point Puzzles
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN

## Slide 41: Summary
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers