## Slide 1
14-513
18-613

## Slide 2: Machine-Level Programming I: Basics 14-513/18-613: Introduction to Computer Systems 5th Lecture, May 27, 2020

## Slide 3: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 4: Levels of Abstraction
C programmer
Assembly programmer
Computer Designer
#include <stdio.h>
int main(){
int i, n = 10, t1 = 0, t2 = 1, nxt;
for (i = 1; i <= n; ++i){
printf("%d, ", t1);
nxt = t1 + t2;
t1 = t2;
t2 = nxt; }
return 0; }
Gates, clocks, circuit layout, …
Nice clean layers, but beware…

## Slide 5: Definitions
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand for writing correct machine/assembly code
  Examples: instruction set specification, registers
  Machine Code: The byte-level programs that a processor executes
  Assembly Code: A text representation of machine code
Microarchitecture: Implementation of the architecture
  Examples: cache sizes and core frequency
Example ISAs:
  Intel: x86, IA32, Itanium, x86-64
  ARM: Used in almost all mobile phones
  RISC V: New open-source ISA

## Slide 6: Assembly/Machine Code View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 7: Assembly Characteristics: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
(SIMD vector data types of 8, 16, 32 or 64 bytes)
Code: Byte sequences encoding series of instructions
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 8: x86-64 Integer Registers
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
  Not part of memory (or cache)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 9: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches
  Indirect branches

## Slide 10: Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 11: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 12: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 13: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “addressing modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN
Warning: Intel docs use mov Dest, Source

## Slide 14: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 15: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 16: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 17: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 18: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 19: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 20: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 21: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 22: Address Computation Instruction
leaq Src, Dst
  Src is address mode expression
  Set Dst to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t = x+2*x
salq $2, %rax # return t<<2
Converted to ASM by compiler:

## Slide 23: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    shlq Src,Dest Dest = Dest << Src Synonym: salq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order! Src,Dest (Warning: Intel docs use “op Dest,Src”)
No distinction between signed and unsigned int (why?)

## Slide 24: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions
  Depending how you count, there are 2,034 total x86 instructions
  (If you count all addr modes, op widths, flags, it’s actually 3,683)

## Slide 25: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    Curious: only used once…
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret
Notes: (rsi,rsi,2) = 3y; 3y << 4 == 3y * 16 = 48y

## Slide 26: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z, t4
%rax | t1, t2, rval
%rcx | t5

## Slide 27: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 28: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –Og p1.c p2.c -o p
    Use basic optimizations (-Og) [New to recent versions of GCC]
    Put resulting binary in file p

## Slide 29: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on shark machine) with command
  gcc –Og –S sum.c
Produces file sum.s
Warning: Will get very different results on non-Shark machines (Andrew Linux, Mac OS-X, …) due to different versions of gcc and different compiler settings.

## Slide 30: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore
Things that look weird and are preceded by a ‘.’ are generally directives.
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret

## Slide 31: Assembly Characteristics: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
(SIMD vector data types of 8, 16, 32 or 64 bytes)
Code: Byte sequences encoding series of instructions
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 32: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches

## Slide 33: Object Code
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595

## Slide 34: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 35: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 36: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore

## Slide 37: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore
  Examine the 14 bytes starting at sumstore
  x/14xb sumstore
Object Code
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 38: Machine Programming I: Summary
History of Intel processors and architectures
  Evolutionary design leads to many quirks and artifacts
C, assembly, machine code
  New forms of visible state: program counter, registers, ...
  Compiler must transform statements, expressions, procedures into low-level instruction sequences
Assembly Basics: Registers, operands, move
  The x86-64 move instructions cover wide range of data movement forms
Arithmetic
  C compiler will figure out different instruction combinations to carry out computation