## Slide 1
14-513
18-613

## Slide 2: Machine-Level Programming III: Procedures 14-513/18-613: Introduction to Computer Systems 7th Lecture, June 2, 2020

## Slide 3: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 4: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 5: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 6: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 7: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 8: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}
Machine instructions implement the mechanisms, but the choices are determined by designers. These choices make up the Application Binary Interface (ABI).

## Slide 9: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 10: x86-64 Stack
Carnegie Mellon
Region of memory managed with stack discipline
Memory viewed as array of bytes.
Different regions have different purposes.
(Like ABI, a policy decision)
code
stack
memory

## Slide 11: x86-64 Stack
Carnegie Mellon
Region of memory managed with stack discipline
Stack Pointer: %rsp
Stack “Top”
Stack “Bottom”
code
stack

## Slide 12: x86-64 Stack
Region of memory managed with stack discipline
Grows toward lower addresses
Register %rsp contains lowest stack address
  address of “top” element
Stack Pointer: %rsp
Stack Grows
Down
(toward lower addresses)
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 13: x86-64 Stack: Push
pushq Src
  Fetch operand at Src
  Decrement %rsp by 8
  Write operand at address given by %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”
val

## Slide 14: x86-64 Stack: Push
pushq Src
  Fetch operand at Src
  Decrement %rsp by 8
  Write operand at address given by %rsp
-8
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”
val

## Slide 15: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Carnegie Mellon
val
Stack “Bottom”

## Slide 16: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
+8
val
Stack “Bottom”

## Slide 17: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
val
(The memory doesn’t change, only the value of %rsp)
Stack “Bottom”
Stack “Top”

## Slide 18: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 19: Code Examples
long mult2(long a, long b)
{
long s = a * b;
return s;
}
void multstore(long x, long y, long *dest)
{
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
400557: retq # Return
0000000000400540 <multstore>:
400540: push %rbx # Save %rbx
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
400549: mov %rax,(%rbx) # Save at dest
40054c: pop %rbx # Restore %rbx
40054d: retq # Return

## Slide 20: Procedure Control Flow
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
  Jump to label
Return address:
  Address of the next instruction right after call
  Example from disassembly
Procedure return: ret
  Pop address from stack
  Jump to address

## Slide 21: Control Flow Example #1
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400544
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 22: Control Flow Example #2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400550
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip
Notes: 0x120-0x118 = 8

## Slide 23: Control Flow Example #3
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400557
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 24: Control Flow Example #4
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 25: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustrations of Recursion & Pointers

## Slide 26: Procedure Data Flow
Registers
First 6 arguments
Return value
Stack
Only allocate stack space when needed
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •

## Slide 27: Data Flow Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore
(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
# a in %rdi, b in %rsi
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
# s in %rax
400557: retq # Return
0000000000400540 <multstore>:
# x in %rdi, y in %rsi, dest in %rdx
• • •
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
# t in %rax
400549: mov %rax,(%rbx) # Save at dest
• • •
Notes: Rdi, rsi outer => x,y; rdi,rsi inner => a,b. Change names without moving data.
Mov rdx, rbx => defer until caller/callee save

## Slide 28: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 29: Stack-Based Languages
Languages that support recursion
  e.g., C, Pascal, Java
  Code must be “Reentrant”
    Multiple simultaneous instantiations of single procedure
  Need some place to store state of each instantiation
    Arguments
    Local variables
    Return address
Stack discipline
  State for given procedure needed for limited time
    From when called to when return
  Callee returns before caller does
Stack allocated in Frames
  state for single procedure instantiation

## Slide 30: Call Chain Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
yoo
who
amI
amI
amI
Example
Call Chain
amI
Procedure amI() is recursive

## Slide 31: Stack Frames
Frame Pointer: %rbp
Contents
  Return information
  Local storage (if needed)
  Temporary space (if needed)
Management
  Space allocated when enter procedure
    “Set-up” code
    Includes push by call instruction
  Deallocated when return
    “Tear-down” code
    Includes pop by ret instruction
Stack Pointer: %rsp
Stack “Top”
Previous Frame
Frame for proc
(Optional) x
Notes: When rbp not optional? Variable arity argument passing – need to track extents of args on stack to allow deallocation during tear-down

## Slide 32: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 33: Example
yoo(…)
{
•
•
who();
•
•
}
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 34: Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI(…)
{
•
•
amI();
•
•
}

## Slide 35: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 36: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 37: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 38: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 39: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 40: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 41: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 42: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 43: x86-64/Linux Stack Frame
Current Stack Frame (“Top” to Bottom)
  “Argument build:” Parameters for function about to call
  Local variables If can’t keep in registers
  Saved register context
  Old frame pointer (optional)
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
(Optional)
Old %rbp
Arguments
7+
Caller
Frame
Frame pointer %rbp
Stack pointer
%rsp
(Optional)

## Slide 44: Example: incr
long incr(long *p, long val) {
long x = *p;
long y = x + val;
*p = y;
return x;
}
incr:
movq (%rdi), %rax
addq %rax, %rsi
movq %rsi, (%rdi)
ret
Register | Use(s)
%rdi | Argument p
%rsi | Argument val, y
%rax | x, Return value

## Slide 45: Example: Calling incr #1
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Notes: Why the unused bytes? Could be alignment. Or space to spill something later.

## Slide 46: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Notes: Leaq: stash known address of “15213” for use in function. Will be safely there until return to call_incr

## Slide 47: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Aside 1: movl $3000, %esi
Note: movl -> %exx zeros out high order 32 bits.
Why use movl instead of movq? 1 byte shorter.

## Slide 48: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Aside 2: leaq 8(%rsp), %rdi
Computes %rsp+8
Actually, used for what it is meant!

## Slide 49: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 50: Example: Calling incr #3
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 51: Example: Calling incr #4
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rax | Return value
Notes: Rsp+8 still contains 15213 which is v1.

## Slide 52: Example: Calling incr #5a
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address

## Slide 53: Example: Calling incr #5b
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address
%rsp
Final Stack Structure
. . .

## Slide 54: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can a register be used for temporary storage?
  Contents of register %rdx overwritten by who
  If a callee clobbers your register, its value is lost!
    Need coordination between caller/callee
yoo:
• • •
movq $15213, %rdx
call who
addq %rdx, %rax
• • •
ret
who:
• • •
subq $18213, %rdx
• • •
ret

## Slide 55: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can register be used for temporary storage?
Conventions
  “Caller Saved”
    Caller must save values in its stack frame before call
  “Callee Saved”
    Callee saves values in its frame before using
    Callee restores values before returning

## Slide 56: x86-64 Linux Register Usage #1
%rax
  Return value
  Also caller-saved
  Can be modified by procedure
%rdi, ..., %r9
  Arguments
  Also caller-saved
  Can be modified by procedure
%r10, %r11
  Caller-saved
  Can be modified by procedure
%rax
%rdx
%rcx
Caller-saved
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Caller-saved
Arguments
Caller-saved
Temporaries

## Slide 57: x86-64 Linux Register Usage #2
%rbx, %r12, %r13, %r14
  Callee-saved
  Callee must save & restore
%rbp
  Callee-saved
  Callee must save & restore
  May be used as frame pointer
  Compiler decides use of rbp
%rsp
  Special form of callee save
  Restored to original value upon exit from procedure
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14

## Slide 58: Quiz Time!
Check out:
https://canvas.cmu.edu/courses/10968

## Slide 59: Callee-Saved Example #1
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
X comes in register %rdi.
We need %rdi for the call to incr.
Where should be put x, so we can use it after the call to incr?

## Slide 60: Callee-Saved Example #2
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
%rsp
Resulting Stack Structure
. . .
Rtn address
Saved %rbx
Notes: We are a callee, must save %rbx (to stack)

## Slide 61: Callee-Saved Example #3
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
Initial Stack Structure
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
%rsp
. . .
Rtn address
Saved %rbx

## Slide 62: Callee-Saved Example #4
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
x is saved in %rbx, a callee saved register
Notes: Rdi is x;

## Slide 63: Callee-Saved Example #5
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
x is saved in %rbx, a callee saved register

## Slide 64: Callee-Saved Example #6
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
Upon return from incr:
x safe in %rbx
Return val v2 in %rax
Compute x+v2: addq %rbx, %rax
Notes: If incr() used rbx, it had to restore call_incr2()’s rbx value before returning

## Slide 65: Callee-Saved Example #7
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
Saved %rbx
Return result in %rax

## Slide 66: Callee-Saved Example #8
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Initial Stack Structure
. . .
Rtn address
Saved %rbx
18213
Unused
%rsp
. . .
Rtn address
Saved %rbx
final Stack Structure
Notes: Remember: we saved %rbx onto stack earlier. Need to restore.

## Slide 67: Callee-Saved Example #2
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Pre-return Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx

## Slide 68: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 69: Recursive Function
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret

## Slide 70: Recursive Function Terminal Case
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rax | Return value | Return value
Notes: Load up 0 return, test rdi for 0, jump to L6. rep;ret -> no-op padding that is more efficient than actual nop.

## Slide 71: Recursive Function Register Save
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rsp
. . .
Rtn address
Saved %rbx

## Slide 72: Recursive Function Call Setup
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x >> 1 | Recursive argument
%rbx | x & 1 | Callee-saved
Notes: Put x into rbx; (safe – caller-saved) and with 1 to get addend, shift rdi to make new arg.

## Slide 73: Recursive Function Call
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Recursive call return value | 

## Slide 74: Recursive Function Result
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Return value | 
Notes: Remember rbx is save because the callee had to restore it before returning.

## Slide 75: Recursive Function Completion
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rax | Return value | Return value
%rsp
. . .

## Slide 76: Observations About Recursion
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
    Unless the C code explicitly does so (e.g., buffer overflow in Lecture 9)
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 77: x86-64 Procedure Summary
Important Points
  Stack is the right data structure for procedure call/return
    If P calls Q, then Q returns before P
Recursion (& mutual recursion) handled by normal calling conventions
  Can safely store values in local stack frame and in callee-saved registers
  Put function arguments at top of stack
  Result return in %rax
Pointers are addresses of values
  On stack or global
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %rbp
Arguments
7+
Caller
Frame
%rbp
(Optional)
%rsp

## Slide 78: Small Exercise
long add5(long b0, long b1, long b2, long b3, long b4) {
return b0+b1+b2+b3+b4;
}
long add10(long a0, long a1, long a2, long a3, long a4, long a5,
long a6, long a7, long a8, long a9) {
return add5(a0, a1, a2, a3, a4)+
add5(a5, a6, a7, a8, a9);
}
Where are a0,…, a9 passed?
Where are b0,…, b4 passed?
rdi, rsi, rdx, rcx, r8, r9, stack
rdi, rsi, rdx, rcx, r8
Which registers do we need to save?
Ill-posed question. Need assembly.
Notes: 1)Rdi, rsi, rdx, rcx, r8, r9, stack
2)rdi,rsi,rdx,rcx,r8, r9

## Slide 79: Small Exercise
long add5(long b0, long b1, long b2, long b3, long b4) {
return b0+b1+b2+b3+b4;
}
long add10(long a0, long a1, long a2, long a3, long a4, long a5,
long a6, long a7, long a8, long a9) {
return add5(a0, a1, a2, a3, a4)+
add5(a5, a6, a7, a8, a9);
}
add5:
addq %rsi, %rdi
addq %rdi, %rdx
addq %rdx, %rcx
leaq (%rcx,%r8), %rax
ret
add10:
pushq %rbp
pushq %rbx
movq %r9, %rbp
call add5
movq %rax, %rbx
movq 48(%rsp), %r8
movq 40(%rsp), %rcx
movq 32(%rsp), %rdx
movq 24(%rsp), %rsi
movq %rbp, %rdi
call add5
addq %rbx, %rax
popq %rbx
popq %rbp
ret