## Slide 1: Desktop Publishing Carnegie-Mellon University Spring 2001
Dave Watterson Art Director, GATF
wttrsn@aol.com
dwatterson@gatf.org

## Slide 2: Binding and Finishing

## Slide 3: What is Binding and Finishing
This category of the process includes everything from simple folding to complex die cutting and case binding

## Slide 4: Design for Limitations
Binding and finishing equipment is usually acurate to within 1/32 of an inch whereas presses are accurate to within .010 of an inch.
Take the tolerances into account when creating artwork for complex finishing work.

## Slide 5: Imaging in the Bindery
Die cutting
Kiss Die cutting
Embossing and Debossing
Foil Stamping
Holography

## Slide 6: Cutting and Trimming
We run jobs on paper larger than the TRIM size to accommodate bleeds, color bars, multiple-up images
Waste must be trimmed away and items cut apart from each other

## Slide 7: Drilling and Punching
Holes for three-ring binders are drilled
Diameters range from 1/8 in. to 1/4 in.
Holes that are not round must be punched

## Slide 8: Scoring and Perforating
Scoring means to crease the printed piece to allow it to fold more easily
This is necessary when paper is thicker than .005 in.
Coated stock that is printed with large solids of ink requires scoring to prevent cracking

## Slide 9: Folding
The options seem almost endless
Most printers do basic folding
More complex jobs need to go to trade binderies
Accuracy of the folds is compounded with the number of folds

## Slide 10: Grain Direction
Paper folds better when folded WITH the grain rather than against it.
Plan the final fold grain long so that the piece lies fat and opens easily
Grain direction affects perfect binding also, causing pages to pucker in the binding edge

## Slide 11: Four Page

## Slide 12: 6-page letter

## Slide 13: 6-page accordion

## Slide 14: 8-page parallel

## Slide 15: 8-page French

## Slide 16: 8-page map

## Slide 17: 8-page gate

## Slide 18: 8-page accordion

## Slide 19: 10-page accordion

## Slide 20: 8-page roll

## Slide 21: 10-page parallel

## Slide 22: 12-page roll

## Slide 23: 12-page broadsheet

## Slide 24: 16-page broadsheet

## Slide 25: 16-page signature

## Slide 26: 12-page signature

## Slide 27: A signature

## Slide 28: Collating
Collating machines have specific tolerances and capabilities
If your job has more sheets than pockets in the equipment, or the sheet size is too heavy it may require more than one pass through the machine

## Slide 29: Laminating
Relatively simple but costly operation
Book jackets, maps, menus, cookbooks, counter displays, name tags
Used to prevent moisture from reaching the final piece
Watch curling

## Slide 30: Adhesive Bindings
There are several ways to glue loose folded sheets or signatures to each other.
Each method offers a different mix of aesthetics, performance, convenience and cost.

## Slide 31: Padding
Almost every printer can glue a stack of paper into a pad
One of the most simple of binding operations
Can be a hand operation with a brush and glue pot

## Slide 32: Gluing
Binderies and envelope makers can apply adhesive strips for individual sealing by the user
Remoistenable glue strips are inexpensive and can be wet sealed automatically

## Slide 33: Perfect Binding
Perfect-bound books are made from gathered signatures
The left-side of the stack is trimmed to get rid of the folds
The edges are roughed and notched for maximum surface adhesion

## Slide 34: Perfect Binding
Glue is applied to the spine of the publication and the pages are inserted
When the glue is set-up the other three sides of the assembled book are trimmed

## Slide 35: Perfect Binding

## Slide 36: Lie-Flat Perfect Binding

## Slide 37: Burst Perfect Binding

## Slide 38: Case Bound Book

## Slide 39: Side Stitch Binding

## Slide 40: Saddle Stitch Binding

## Slide 41: Screw and Post Binding

## Slide 42: Plastic Grip Binding

## Slide 43: Comb Binding

## Slide 44: Spiral Bound

## Slide 45: Double-loop wire bound

## Slide 46: Three-ring bindery

## Slide 47: Converting
A printed sheet changed into a substantially new product—a box, point-of-purchase display, or envelope—has been converted

## Slide 48: Converting companies
Usually specialize in one area of the process, envelope creation, boxes, display houses
Usually have specific tolerances and requirements

## Slide 49: Final Considerations
Packing
Final Counts
Shipping
Storage

## Slide 50: Contacting me
I don’t have an office on campus and really work all day
Please e-mail me and I will set up a meeting time as quickly as possible

## Slide 51: Thanks for your attention! Now let’s head over to the lab (CFA Room 318)