## Slide 1
18-100 Introduction to Electrical and Computer Engineering
Lecture 04
Binary Numbers, Boolean Logic, and Logic Gates

## Slide 2
Today’s Digital World: “0” and “1”
“10011011110001…1000100010…0100101111001...”
Digital music
Data Center
“100…11011110001…1000100010…01001011110”
Everything is stored as
Communications
Everything is transmitted as
“100…11011110001…1000100010…01001011110”
Binary Number

## Slide 3
Quiz
1. The first general purpose computer, ENIAC, was built at Univ. of Pennsylvania in 1946 and was in operation until 1956. It contains 20,000 vacuum tubes. It used 10-digit decimal numbers for computation. Can you guess what is the clock speed of ENIAC?
3.5 GHz
25 kHz.
50 Hz.

## Slide 4
Quiz
1. The first general purpose computer, ENIAC, was built at Univ. of Pennsylvania in 1946 and was in operation until 1956. It contains 20,000 vacuum tubes. It used 10-digit decimal numbers for computation. Can you guess what is the clock speed of ENIAC?
3.5 GHz
25 kHz.
50 Hz.
Intel CORE i7 Microprocessor.
Frequency of ac power from wall outlet.

## Slide 5
Learning Objectives for This Lecture
Why today’s computer using binary numbers.
How computer uses binary numbers to control “things”.
What is Boolean logic and what are logic gates.
How to use logic gates to build logic functions.
How computer uses logic gates to do “computation”.

## Slide 6
“1” and “0” : Inside a Microprocessor
8.5 billion transistors
1.2V
0V
“HIGH”
“LOW”
“1”
“0”
1.2V
“1”
“0”
Transistor pairs: Switches
“0”
“1”
…
Output
input
A13

## Slide 7
The Logic Levels Used Here
5V
0V
“HIGH”
“LOW”
“1”
“0”
5V
“1”
“0”
Logic Gates
“0”
“1”
…
Output
input
+
-
Logic Value | Logic Value | Logic Value | Voltage Value
0 | False | LOW | 0 (V)
1 | True | HIGH | 5 (V)

## Slide 8
Why “1” and “0”
Black (“0”) and White (“1”)
No Gray
Ensure No Mistakes: It is not so easy to “confuse” black and “white”

## Slide 9
Why “1” and “0” Resilient to Noise
Ensure No Mistakes: It is not so easy to “confuse” black and “white”
1.0
0.3
0.8
0.0
0.6
0.3
1.0
0.1
0.8
0.3
0.8
0.1
0.8
0.1
1.0
0.2
0.8
0.1
0.8
0.0
0.8
0.0
0.8
0.2
0.8
0.3
1.0
0.2
0.8
0.3
0.8
0.1
0.7
0.1
0.8
0.0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
Threshold = 0.5

## Slide 10
Binary Minimize the Impact of Noise
2 GHz
1 GHz

## Slide 11
Decimal Number System
n-digit
…
1982

## Slide 12
Binary Number System
n-digit
(n-bit )
…
Conversion to decimal:
A n-bit binary number has number of possible values, ranging from
10101011

## Slide 13
Decimal to Binary
139
1
2
2
2
2
2
8
4
2
1
1
0
0
0
2
2
Decimal
Binary
Each digit will only have two values
0
1
(bit)
139
6
9
1
3
4
1
17
0
1
0
0
1
1
0
0

## Slide 14
Decimal to Binary
13
1101
2
2
2
13
6
3
1
1
0
1
Decimal
Binary

## Slide 15
Addition
1101
Decimal
Binary
139 + 13 =
10001011 + 1101 =
10001011
+
0
1
0
1
0
1
1
1
1
0
0
1
binary operation
binary operation
10011000
carry

## Slide 16
Binary to Decimal
Decimal
Binary
139 + 13 =
10001011 + 1101 = 10011000
10011000
7 6 5 4 3 2 1 0
Digit number
152
10011000
Least significant bit (LSB)
Most significant bit (MSB)

## Slide 17
Negative Number:
1 0 0 1 0 1 0 0
bit-wise complement:
0 1 1 0 1 0 1 1
1 0 0 1 0 1 0 0
Add the above two numbers:
+
1 1 1 1 1 1 1 1
+
0 0 0 0 0 0 0 1
Add 1:
0 0 0 0 0 0 0 0
If x = 01101011
–x = 10010101
bit-wise-complement + 1
Negative Number 8-bit Number
0 1 1 0 1 0 1 1
Take any 8-bit binary number:
Two’s Complement
( 2’s Complement )
1
bit-wise complement:
8-bit

## Slide 18
For a 8-bit number with both positive and negative integers:
0 1 1 1 1 1 1 1
Largest positive number
1 0 0 0 0 0 0 1
Smallest (negative) number
0 0 0 0 0 0 0 1
1 1 1 1 1 1 1 1
1000001, 10000010, 10000011, …,11111111,00000000, 00000001, 00000010,…,01111111
8-bit Adder
8-bit Adder
Use adder for subtracting:
2’s complement

## Slide 19
Binary Number System
2-bit binary number
3-bit binary number
Binary | Decimal
00 | 0
01 | 1
10 | 2
11 | 3
Binary | Decimal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Binary | Decimal
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
1000 | 8
1001 | 9
1010 | 10
1011 | 11
1100 | 12
1101 | 13
1110 | 14
1111 | 15
4-bit binary number
values
values
values

## Slide 20
Hexadecimal Number
A Hexadecimal number is a base 16 number: Each digit has 16 values:
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
16 values
2E
=
Decimal
2 E
Hexadecimal to Binary
Each bit in Hex is 4 bit in Binary!
Hexadecimal to Decimal
Hex
10
11
12
13
14
15
0x2E = 46
0x21 = 33
0x
The number to follow is hexadecimal.
Decimal
Hex

## Slide 21
Taking More Digits
1-bit gray
256 levels
…
black
White
00000000
00000001
11111111
…
…
256 numbers
8-bit gray
0
1
2 levels
8-digit binary number
1-digit binary number
01011001

## Slide 22
Binary to Represent Analog
16,777,216 color variations
24-bit Color
1-bit gray
8-bit gray
256 levels
8-bit Red
8-bit Green
8-bit Blue
…

## Slide 23
A Simple Truth of “1” and “0”
Each transistor only controls a “1” and a “0”, however,
8,500,000,000 Transistors can carry out very complex functions!

## Slide 24
Binary Logic:
“True” = “1”
“False” = “0”
Binary bit operation: Simplest decision making

## Slide 25
NOT Gate: Inverter
Input
Output
“1”
“0”
“0”
“1”
Input | Output
1 | 0
0 | 1
Truth Table

## Slide 26
AND Gate
Input A
Input B
Output P
“0”
“0”
“0”
“0”
“1”
“0”
“0”
“1”
“1”
“1”
“0”
“1”
Input A | Input B | Output P
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
Truth Table

## Slide 27
Using Logic Gates to Control Action: The Use of “1” and “0”
Input A
Input B

## Slide 28
Using Logic Gates to Control Action: The Use of “1” and “0”
Input A
Input B
0
0
1
1
1
0
1
0
0
1
0

## Slide 29
Using Logic Gates to Control Action: The Use of “1” and “0”
Input A
Input B
1
0
0
1
0
1
1
1
0
0
0

## Slide 30
Using Logic Gates to Control Action: The Use of “1” and “0”
Input A
Input B
0
1
1
0
0
0
0
0
1
1
1

## Slide 31
Using Logic Gates to Control Action: The Use of “1” and “0”
Input A
Input B
A
B
0 0
1 0
0 1

## Slide 32
n-bit Input Controlling/Selecting 2n Different Actions
A n-bit number has 2n different values: Can be used to control 2n different actions!
Example: 4-bit number controlling/selecting 16 lines
……
1111
0111
0000
0001
16 Lines
Corresponding input number
……

## Slide 33
n-bit Input Controlling/Selecting 2n Different Actions
4-bit Decode
4-bit binary number
Controlling 24 = 16 lines
This is how machine(computer) uses binary numbers to perform different actions!

## Slide 34
n-bit Input Controlling/Selecting 2n Different Actions
4-bit Decode
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
4-bit binary number: 1011
A 4-bit binary number selects a single line (out of the 16 lines) to be “HIGH”.
(The rest all remain “LOW”)
4-bit Decode

## Slide 35
4-bit Input Controlling/Selecting 24 Different Actions
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
4-bit binary number
A 4-bit binary number selects a single line (out of the 16 lines) to be “HIGH”.
(The rest all remain “LOW”)
0111
4-bit Decode

## Slide 36
OR Gate
Input A | Input B | Output C
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
Truth Table
Input A
Input B
Output C
“0”
“0”
“0”
“1”
“1”
“0”
“0”
“1”
“1”
“1”
“1”
“1”

## Slide 37
Exclusive OR Gate: XOR
Input A
Input B
Output C
Input A | Input B | Output C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table
“0”
“0”
“0”
“1”
“0”
“1”
“1”
“0”
“1”
“1”
“1”
“0”

## Slide 38
Computing Using Logic Gates: Addition
0
0
+
0
1
0
+
1
0
1
+
1
1
1
+
0
1
Adding Binary Numbers for the Rightest Digit (No Input Carry)
Half Adder (no input carry)
A
B
+

## Slide 39
Computing Using Logic Gates: Addition
0
0
+
0
1
0
+
1
0
1
+
1
1
1
+
0
1
Adding Binary Numbers for the Rightest Digit (No Input Carry)
Half Adder (no input carry)
A
B
+
0
0
0
0

## Slide 40
Computing Using Logic Gates: Addition
0
0
+
0
1
0
+
1
0
1
+
1
1
1
+
0
1
Adding Binary Numbers for the Rightest Digit (No Input Carry)
Half Adder (no input carry)
A
B
+
1
0
1
0

## Slide 41
Computing Using Logic Gates: Addition
0
0
+
0
1
0
+
1
0
1
+
1
1
1
+
0
1
Adding Binary Numbers for the Rightest Digit (No Input Carry)
Half Adder (no input carry)
A
B
+
0
1
1
0

## Slide 42
Computing Using Logic Gates: Addition
0
0
+
0
1
0
+
1
0
1
+
1
1
1
+
0
1
Adding Binary Numbers for the Rightest Digit (No Input Carry)
Half Adder (no input carry)
A
B
+
1
1
0
1

## Slide 43
Addition
Full Adder (with input carry)
0
0
+
1
1
1
0
+
0
1
1
0
1
+
0
1
1
1
1
+
1
Addition with input carry:
1
1
A
B
S
COut
S
A
B
S
COut
Cout
CIN
A
B
Full Adder
Half Adder
Half Adder

## Slide 44
8-bit Adder
A1
CIN
S1
S0
A0
full
adder
A2
CIN
A3
CIN
A4
CIN
A5
CIN
Overflow
full
adder
full
adder
A6
CIN
A7
B1
B0
B2
B3
B4
B5
B6
B7
CIN
full
adder
full
adder
full
adder
full
adder
half
adder
S2
S3
S4
S5
S6
S7
COUT
COUT
COUT
COUT
COUT
COUT
COUT

## Slide 45
Arithmetic Logic Unit (ALU)
Integer A
Integer B
Output Result
Operation Code
Status

## Slide 46
NAND Gate :
AND gate + NOT gate
Input A | Input B | Output P
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
Truth Table
“0”
“0”
“1”
“0”
“0”
“1”
“1”
“1”
A
B
P
NAND gate
A
B
P
“1”
“1”
“1”
“0”

## Slide 47
Boolean Algebra
and are complements
Rules

## Slide 48
Boolean Algebra

## Slide 49
Boolean Algebra Example
Fail-Safe Autopilot Logic
Prior to takeoff or landing maneuver, a commercial aircraft requires the following check:
2 of the possible 3 pilots must be available: the pilot, the copilot and the autopilot
X - State of the pilot: 1= Present, 0=Absent
Y - State of the copilot: 1= Present, 0=Absent
Z - State of the autopilot: 1= Functioning, 0=Not Functioning
Logic function corresponding to “System Ready” is
or
or
Set Logic Variables:
: System Ready ;
: System Not Ready

## Slide 50
Rules for Boolean Algebra
Commutative Law
Commutative Law
Distributive Law
Absorption Law

## Slide 51
Rules for Boolean Algebra
Commutative Law
Commutative Law
Distributive Law
Absorption Law

## Slide 52
De Morgan’s Laws
Any logic function can be implemented using only OR and NOT gates.
Any logic function can be implemented using only AND and NOT gates.

## Slide 53
Boolean Algebra Example
Fail-Safe Autopilot Logic
or
Positive check
sum-of-product
System Not Ready Condition: