## Slide 1
Digital Video

## Slide 2
Video
Video comes from a camera, which records what it sees as a sequence of images
Image frames comprise the video
  Frame rate = presentation of successive frames
  minimal image change between frames
  Frequency of frames is measured in frames per second [fps].
Sequencing of still images creates the illusion of movement
  > 16 fps is “smooth”
  Standards: 29.97 is NTSC, 24 for movies, 25 is PAL, 60 is HDTV
Standard Definition Broadcast TV, NTSC,
  15 bits/pixel of color depth, and
  525 lines of resolution
  with 4:3 aspect ratio.
  Scanning practices leave a smaller safe region.
Display scan rate is different
  monitor refresh rate
  60 - 70 Hz (= 1/s)
  Interlacing: half the scan lines at a time (-> flicker)

## Slide 3: The Video Data Firehose
To play one SECOND of uncompressed 16-bit color, 640 X 480 resolution, digital video requires approximately 18 MB of storage.
One minute would require about 1 GB.
A CD-ROM can only hold about 600MB and a single-speed (1x) player can only transfer 150KB per second.
Data storage and transfer problems increase proportionally with 24-bit color playback.
Without compression, digital video would not be possible with current storage technology.

## Slide 4: Storage/Transmission Issues
The storage/transmission requirements for video is determined by:
  Video Source Data * Compression = Storage
The amount of required storage is determined by
  how much and what type of video data is in the uncompressed signal and
  how much the data can be compressed.
In other words, the original video source and the desired playback parameters dramatically affect the final storage/transmission needs.

## Slide 5: Video Compression
The person recording video to be digitized can drastically affect the later compression steps.
Video in which backgrounds are stable (or change slowly), for a period of time will yield a high compression rate.
Scenes in which only a person's face from the shoulders upward is captured against a solid background will result in excellent compression.
  This type of video is often referred to as a 'talking head'.

## Slide 6: Filtering
A filtering step does not achieve compression, but may be necessary to minimize artifacts of compression.
Filtering is a preprocessing step performed on video frame images before compression. Essentially it smoothes the sharp edges in an image where a sudden shift in color or luminance has occurred.
The smoothing is performed by averaging adjacent groups of pixel values. Without filtering, decompressed video exhibits aliasing (jagged edges), and moiré patterns.

## Slide 7: Data Reduction through Scaling
The easiest way to save memory is to store less, e.g. through size scaling. Original digital video standards only stored a video window of 160 X 120 pixels. A reduction of 1/16th the size of a 640 X 480 window. A 320 X 240 digital video window size is currently about standard, yielding a 4 to 1 data reduction.
A further scaling application involves time instead of space. In temporal scaling the number of frames per second (fps), is reduced from 30 to 24. If the fps is reduced below 24 the reduction becomes noticeable in the form of jerky movement.

## Slide 8: Compression through Transformation
Codecs (COmpression/DECompression algorithms) transform a two-dimensional spatial representation of an image into another dimension space (usually frequency).
Since most natural images are composed of low frequency information, the high frequency components can be discarded.
  [What are high frequency components?]
  This results in a softer picture in terms of contrast.
Most commonly, the frequency information is represented as 64 coefficients due to the underlying DCT (Discrete Cosine Transform), algorithm which operates upon 8 X 8 pixel grids. Low frequency terms occur in one corner of the grid, with high frequency terms occurring in the opposite corner of the grid.

## Slide 9: Compression through Quantization
The lossy quantization step of digital video uses fewer bits to represent larger quantities. The 64 frequency coefficients of the DCT transformation are treated as real numbers. These are quantified into 16 different levels. The high frequency components (sparse in real-world images), are represented with only 0, 1 or 2 bits. The zero mapped frequencies drop out and are lost.

## Slide 10: Frame Compaction
The last step in compressing individual frames (intraframe compression) is a sequence of three standard text file compression schemes. Run-length encoding (RLE), Huffman coding, and arithmetic coding.
  RLE replaces sequences of identical values with the number of times the value occurs followed by the value (e.g., 11111000011111100000 ==>> 51406150).
  Huffman coding replaces the most frequently occurring values|strings with the smallest codes.
  Arithmetic coding, similar to Huffman coding, codes the commonly occurring values|strings using fractional bit codes.

## Slide 11: Interframe Compression (MPEG style)
Interframe compression takes advantage of minimal changes from one frame to the next to achieve dramatic compression. Instead of storing complete information about each frame only the difference information between frames is stored.
MPEG stores three types of frames:
  The first type I-frame, stores all of the interframe compression information using no frame differencing.
  The second type P-frame is a predicted frame two or four frames in the future. This is compared with the corresponding actual future frame and the differences are stored (error signal).
  The third type B-frames, are bidirectional interpolative predicted frames that fill in the jumped frames.

## Slide 12
Streaming Video
  Access disk fast enough
    RAIDs
  Don’t download everything first
    Play as you start to download
  Keep a buffer for variable network speed
    equivalent to sampling a CD’s faster and filling a buffer
  Drop frames/packets when you fall behind (not TCP)
  Adjust the bandwidth dynamically
    need multiple encoding formats
RTSP, QT, MS ASF, H.323 (video conferencing)

## Slide 13
Webcasting
  LIVE
  Encode fast enough
  Stream to multiple users connected at the same time
  Only time-synchronous viewing

## Slide 14: Video Data Rates
Quality | Format (example) | Transfer Rate | Disk Space 1 hour | Disk Space 100,000 hours
Netcasting | VDOLive | 0.06 Mbit/s | 26.4MByte | 2.6 TByte
Preview (ISDN) | RealVideo | 0.1 Mbit/s | 43.9 MByte | 4.4 TByte
Preview (LAN) | MPEG-1 | 1.5 Mbit/s | 675 MByte | 67.6 TByte
Broadcast | MPEG-2 (MP @ ML) | 8 Mbit/s | 3.5 GByte | 350 TByte
Editing | MPEG-2 (4:2:2P@ML ) DVCPro50 | 18 Mbit/s 50 Mbit/s | 7.9 GByte 22 GByte | 790 TByte 2.2 PByte
Archive | MJPEG Lossless | 100 Mbit/s | 43.9 GByte | 4.4 PByte
Uncompressed | ITU-R BT.601-5 | 270 Mbit/s | 118.7 GByte | 11.9 PByte

## Slide 15
MPEG: Motion Picture Experts Group
  MPEG-1 (1992)
    Compression for Storage
    1.5Mbps
    Frame-based Compression
  MPEG-2 (1994)
    Digital TV
    6.0 Mbps
    Frame-based Compression
  MPEG-4 (1998)
    Multimedia Applications, digital TV, synthetic graphics
    Lower bit rate
    Object based compression
  MPEG-7
    Multimedia Content Description Interface, XML-based
  MPEG-21
    Digital identification, IP rights management

## Slide 16
MPEG-1 System Layer
  Combines one or more data streams from the video and audio parts with timing information to form a single stream suited to digital storage or transmission.

## Slide 17
MPEG-1 Video Layer
a coded representation that can be used for compressing video sequences - both 625-line and 525-lines - to bitrates around 1.5 Mbit/s.
Developed to operate from storage media offering a continuous transfer rate of about 1.5 Mbit/s.
Different techniques for video compression:
  Select an appropriate spatial resolution for the signal. Use block-based motion compensation to reduce the temporal redundancy. Motion compensation is used for causal prediction of the current picture from a previous picture, for non-causal prediction of the current picture from a future picture, or for interpolative prediction from past and future pictures.
  The difference signal, the prediction error, is further compressed using the discrete cosine transform (DCT) to remove spatial correlation and is then quantised.
  Finally, the motion vectors are combined with the DCT information, and coded using variable length codes.
  When storing differences MPEG actually compares a block of pixels (macroblock) and if a difference is found it searches for the block in nearby regions. This can be used to alleviate slight camera movement to stabilize an image. It is also used to efficiently represent motion by storing the movement information (motion vector), for the block.

## Slide 18
MPEG-1 Video Layer

## Slide 19
MPEG-1
  I,B,P Frames
  Choice of audio encoding
  Picture size, bitrate is variable
  No closed-captions, etc.
  Group of Pictures
    one I frame in every group
    10-15 frames per group
    P depends only on I, B depends on both I and P
    B and P are random within GoP

## Slide 20
MPEG-1 Audio Layer
Compress audio sequences in mono or stereo.
Encoding creates a filtered and subsampled representation of the input audio stream.
A psychoacoustic model creates data to control the quantiser and coding.
The quantiser and coding block creates coding symbols from the mapped input samples.
The block 'frame packing' assembles the actual bitstream from the output data of the other blocks and adds other information (e.g. error correction) if necessary.

## Slide 21
MPEG-1 Audio Layer

## Slide 22: MPEG Streaming in variable networks
Problem: available bandwidth
  Slightly too low, varying
  Shared by other users/applications
Target application: Informedia
  MPEG movie database (terabytes)
http://www.cineflo.com
  CMU spinoff startup company for adaptive MPEG-1 video transmission
Notes: Informedia needs to transfer movies to clients with different BW requirements
Research in network awareness

## Slide 23: System Overview
Filter / Transcoder
Client
Data-Base
Video server
Application-aware network
Network-aware application
Notes: Streaming with TCP too slow over congested lines
Streaming with UDP results in random packet losses
impact of losses on quality depends on format of video stream
Emphasize filter IN network : intelligent network vs intelligent server

## Slide 24: Architecture
Maintain two connections
  control connection: TCP
  data connection: UDP
Fits with the JAVA security model
Server
Filter
Client
Control
Control
Data
Data
Notes: 3 tier architecture
Java security:
Filter needs to be able to talk to server on behalf of client
setup connection
transmit reliable data
exchange control information
Cascadable operation.

## Slide 25: Congestion Analysis and Feedback
Client notices changes in loss rate and notifies filter ...
  Variable-size sliding window and two thresholds
Filter modifies rate by clever manipulation of data stream
Client is less aggressive in recapturing bandwidth
Server
Filter
Client
Control
Control
Data
Data
Notes: TCP-like friendly
Rate change is not absolute (depends on filtering) so no need for rate prediction

## Slide 26: Filter
Acts as mediator between client and upstream
MPEG Video format dependent
  Performs on-the-fly low-cost computational modifications to data stream
  Paces data stream
Server
Filter
Client
Control
Control
Data
Data
Notes: Filter has 2 tasks: mediator and filtering.
Mediator 4 way
The filtering is format dependant.
A different filter is required for a different movie format
up until now we did not mention the format (intentionally)
Now ---> MPEG-1

## Slide 27: MPEG-1 Systems Stream
Network layer
Padding
Audio[0]
Audio[0]
Audio[1]
Audio[1]
Video[0]
Video[0]
Video[0]
Video[0]
Video[0]
Video[0]
Video[0]
Video[0]
Audio[0]
Audio[1]
Pack layer
Packet layer
Notes: Impact of loss in system streams is worse than video streams

## Slide 28: MPEG Sensitivity to Network Losses

## Slide 29: MPEG Video Filtering
I
B
B
P
B
B
P
B
B
P
B
B
P
B
B
I
I
B
P
B
P
B
P
B
P
B
I
I
P
P
P
P
I
I
P
P
P
I
I
P
P
I
I
I
Notes: ideally: remove frame with largest amount of data
practically: remove frame with smallest amount of data

## Slide 30: MPEG System Sensitive Video Filtering
Reduce network traffic by filtering frames
  on-the-fly & low-cost !
Maintain smoothness
Maintain synchronization data
  Adjust Packet Layer
Padding
Audio[0]
Audio[1]
Padding
Audio[0]
Audio[1]
-----------B frame--------------
Notes: Every video packet data remains in its original packet to maintain DTS and PTS so no need to recalculate
Also all headers remain so that correct pacing of data can be done
if we have time at the end I will show a filtered video example

## Slide 31: Evaluation
Constant heavy competing load
Notes: WORST case

## Slide 32: Streaming based on estimated need
Smarter Streaming for interactivity
Break apart I, P, B frames
Client decides which are more likely to be needed and requests those from server for the client cache
  Differential weights on frames based on need
  Also weighting based on type of frame (I,P,B) since you can’t decode a B frame without the I and P.
Can only achieve savings of ~ 30% over raw MPEG-1

## Slide 33
MPEG-2
  Digital Television (4 - 9 Mb/s)
  Satellite dishes, digital cable video
  Larger data size
  includes CC
  More complex encoding (“long time”)
  almost HDTV

## Slide 34
HDTV
  2x horizontal and vertical resolution
  SDTV: 480 line, 720 pixels per line, 29.97 frames per second
  x 16 bits/pixel = 168 Mbits/sec uncompressed
  MPEG-1 brings this to 1.5Mbits/sec at VHS quality
  HDTV: expanded to 1080 lines, 1920 pixels per line, 60 fps
  x 16 bits/pixel = 1990 Mbits/sec uncompressed
  MPEG-II like encoding, different audio encoding
  HDTV Audio Compression is based on the Dolby AC-3 system with sampling rate 48kHz and perceptually coded

## Slide 35: Why HDTV?
Higher-resolution picture
Wider picture
Digital surround sound.
Additional data
Easy to interface with computers

## Slide 36: Current TV Standards
NTSC: National Television Systems Committee
PAL: Phase Alternation Line
SECAM: Séquential Couleur Avec Mèmoire

## Slide 37: HDTV and NTSC Specifications

## Slide 38: Analog bandwidth of HDTV signals?
HDTV image size of 1050 by 600 at 30 frames per sec, the bandwidth required to carry that image quality using the analog transmission system is 18MHz. However, it will require more bandwidth to transmit it in digital format.
With the MPEG-2 compression, the bit rate is compressed from more than 1 Gbps to about 20 Mbps, which transmit digitally only require bandwidth 6MHz

## Slide 39: Architecture of HDTV Receivers
Display
Processor
Audio
Decoder
Image
Decoder
Demodulator
Demultiplexer
Decoded
video
signals
Decoded
audio
signals
Display
format
video
signals
audio
signals
digital
signals
analog
carrier
+
digital
signals

## Slide 40: Aspect ratio of movies vs. HDTV?
Aspect ratio of HDTV is 16:9
However, movies have many different aspect ratios:
  “Movies are always shot so they can be displayed in several aspect ratios at different types of movie theaters, from the shoebox-sized foreign movie houses to the ultra big screen Star Wars jobs.” ----- Franco Vitaliano
  http://www.vxm.com/21R.107.html

## Slide 41: Original Timeline of HDTV
First began in 60’s at NHK, the Japan Broadcasting Corporation.
In 1993, FCC suggested an alliance that could create the best possible system
November 1998: HDTV transmissions begin at 27 stations in the top 10 markets
May 1999: network affiliates in the top 10 markets must show at least 50% digital programming
November 1999: digital broadcasts in the next 20 largest markets
May 2002: remaining commercial stations must convert
2003: public stations must convert to digital broadcasts
2004: stations must simulcast at least 75% of their analog programming on HDTV
2005: stations must simulcast 100% of their analog programming
2006: stations relinquish their current analog spectrum
  NTSC TV sets will no longer be able to pick up broadcast signals

## Slide 42: Spring 2001 Status
18 digital TV formats are approved by FCC
More than 27 digital channels being broadcast by ABC, CBS, FOX, NBC
DirecTV has one HDTV channel
Cox is broadcasting two HDTV channels

## Slide 43: Hardware Requirements
Digital Decoder
  converts digital signals to analog
  allow current TV set to work
Digital-Ready TV set
  Wide-screen format
  progressive scanning
HDTV set
  Wide-screen format
  can receive 18 digital input format

## Slide 44: Comparison
Current TV
HDTV

## Slide 45: Comparison (current TV)

## Slide 46: Comparison (HDTV)

## Slide 47
Video vs. computer (ROM) formats
Single (R) and multiple (RAM) recordings possible
Up to 17 GB of data
12 cm optical disc format data storage medium
Replaces optical media such as
  the laserdisc
  audio CD,
  and CD-ROM.
Will also replace VHS tape as a distribution format for movies
MPEG-2 encoding
Digital Video Disc (DVD)

## Slide 48
DVD Features
Language choice (for automatic selection of video scenes, audio tracks, subtitle tracks, and menus). Optional
Special effects playback: freeze, step, slow, fast, and scan (no reverse play or reverse step).
Parental lock (for denying playback of discs or scenes with objectionable material). Optional
Programmability (playback of selected sections in a desired sequence).
Random play and repeat play.
Digital audio output (PCM stereo and Dolby Digital).
Compatibility with audio CDs
Digital Zoom
Six channel audio

## Slide 49
MPEG-4
  MPEG 2 plus
    Interactive Graphics Applications
    Interactive multimedia (WWW), networked distribution

## Slide 50
MPEG-4
  Bitrates from 5kb/s to 10Mb/s
  Several extension “profiles”
  Very high quality video
  Better compression than MPEG-1
  Low delay audio and error resilience
  Support for “objects”
    Face Animation
  Support for efficient streaming
  Limited industry activity at this point

## Slide 51
MPEG-4 from: http://mpeg.telecomitalialab.com/standards/mpeg-4/mpeg-4.htm

## Slide 52
MPEG-4

## Slide 53
MPEG-4 Example
  Difficulty is in separating foreground from background automatically
  http://www.dbvision.net
  Object Vision codec by Diamondback Vision (startup .com)

## Slide 54
MPEG-7
  Data + Multimedia Content Description Scheme
    Description Definition Language (XML-based)
  Still not ‘final’, but close
  Does not deal with data, but meta-data transmission
  Description Scheme + Content Description, e.g:
    Table of content
    Still Images
    Summaries
    links
    etc.
  How does the Description data get generated? How is it used?

## Slide 55: Mpeg-7 Examples
<VideoText id="VideoText1" textType="Superimposed">
<MediaTime>
<MediaTimePoint> T0:0:0:0 </MediaTimePoint>
<MediaDuration> PT6S </MediaDuration>
</MediaTime>
<Text xml:lang="en-us">CNN World News</Text>
</VideoText>
<TextProperty>
<FreeText xml:lang="en"> World Today </FreeText>
<SyncTime>
<MediaRelTimePoint>PT01N30F </MediaRelTimePoint>
<MediaDuration> PT2S </MediaDuration>
</SyncTime>
</TextProperty>
<Place>

## Slide 56: Mpeg-7 Examples Cont’d
<Name xml:lang="en">Kabul</Name>
<GPSCoordinates type="latlon">69.137E 34.531N </GPSCoordinates>
<Country>Afghanistan</Country>
<Region>Velayat</Region>
<AdministrativeUnit type="city"> Kabul </AdministrativeUnit>
</Place>

## Slide 57
MPEG-7

## Slide 58: MPEG-21 (Draft) http://mpeg.telecomitalialab.com/standards/mpeg-21/mpeg-21.htm

## Slide 59: Video Compression Styles
Symmetric codecs require inverse operations to decompress the format.
Asymmetric codecs use different compression|decompression methods. More processing time is spent in compressing to achieve low storage to allow for shorter decompression time.

## Slide 60: Other Compression Schemes
Quicktime (Apple), Video for Windows
  Open architecture allowing different codecs
Motion JPEG – no interframe compression
Cinepak is an asymmetric codec designed for 24-bit video in a 320 X 240 window for single-speed CD-ROM drives. Compression typically takes 300 times longer than decompression.
Indeo asymmetric codec (Intel). Playback can take place on a Intel 486 processor without any hardware assistance. Less efficient than Cinepak
DVI Digital Video Interactive requires off-line supercomputer processing power for the compression.

## Slide 61
QuickTime
An ISO standard for digital media
Created by Apple Computer Inc., 1993
Audio, animation, video, and interactive capabilities for PC
Allows integration of MPEG technology into QuickTime.
QuickTime is available for MS Windows/NT as well
QuickTime movies have file extension .qt and .mov.
Description: http://www.apple.com/quicktime/specifications.html
ftp://ftp.intel.com/pub/IAL/multimedia/indeo/utilities/smartv.exe
converts quicktime to avi and back

## Slide 62
Video Players for your PC
To play a movie on your computer, you need a multimedia player
  e.g. an MPEG player, WindowsMediaPlayer, RealPlayer or QuickTime player.
These players are also called decoders because they decode the MPEG or QuickTime, RealNetworks, etc. compressed codes.
Some software allows you to both encode and decode multimedia files, e.g. to make and play the files.
  You’ll use both for your digital video homework assignment.
Some software only allows you to play back multimedia files.
When digitizing from a VCR, then the quality of the videotape recording and playback process limits the quality the digital video capturing system can achieve. Consumer grade recorders used should at least be SVHS, or Hi-8, to give adequate quality of the computer representation.

## Slide 63: References
http://www.cato.org/pubs/regulation/reg16n4b.html
http://web-star.com/hdtv/faq.html
http://web-star.com/hdtv/perspective.html
http://bock.bushwick.com/hdtv_ppt/
http://web-star.com/hdtv/history.html
http://www.cnn.com/TECH/computing/9910/26/pc.hdtv.idg/
http://money.cnn.com/services/tickerheadlines/bw/222470357.htm

## Slide 64: References
MPEG-1 System Layer
MPEG-1 Video Layer
MPEG-1 Audio Layer
Definition of Video Terms

## Slide 65
Digital Video
That’s all for today