## Slide 2
Sound Compression

## Slide 3: Compression of Sound

## Slide 4: Motivation for Sound Compression
need to minimize transmission costs or provide cost efficient storage
demand to transmit over channels of limited capacity such as mobile radio channels
need to share capacity for different services (voice, audio, data, graphics, images) in integrated service network

## Slide 5: Compression Approaches
Delta coding
  Encode differences only
Predictive coding
  Predict the next sample
Linear Predictive Coding (LPC) - mostly for speech
  Describe fundamental frequencies + ‘error’
  CELP, RPE, cell-phone standards
Variable Rate Encoding
  Don’t encode silences
  regular signal=few bits, variable signal=many bits
Subband coding
  Split into frequency bands each encoded separately + efficiently
Psycho-acoustical coding
  drop bits where you can’t hear it

## Slide 6
Many (!) Compression Standards
PCM (Pulse Code Modulation)
u-LAW (Mu-law – logarithmic coding)
LPC-10E (Linear Predictive Coding 2.4kb/s)
CELP 4.8Kb/s – code excited LPC builds on LPC
GSM (European Cell Phones, RPE-LPC)
1650 bytes/sec (at 8000 samples/sec)
ADPCM (adaptive, delta PCM, 24/32/40 kbps)
MPEG Audio Layers (builds on ADPCM)
Layer-2: From 32 kbps to 384 kbps - target bit rate of 128 kbps
Layer-3: From 32 kbps to 320 kbps - target bit rate of 64 kbps
Complex compression, using perceptual models
RealAudio, Windows Media Formats (builds on above, proprietary)

## Slide 7: MPEG Audio Encoding
MPEG encoding

## Slide 8: MPEG Audio Encoding
Motion Picture Experts Group Audio Encoding
  Mpeg-1 layer 1 - 384 kbit/s
  Mpeg-1 layer 2 - 192 kbit/s
  Mpeg-1 layer 3 - 1128 kbit/s
  Mpeg-2

## Slide 9: MPEG 1 layer 1 Audio
Mapping the audio input into 32 subbands via equally spaced bandpass filters
Fixed block lengths (8 ms at 48 kHz sampling frequency) compressed into 12 samples each
Quantization providing very large dynamic range of more than 120 dB.
Bit allocation algorithm selects a quantizer (out of 15) for bit rate requirement and best coding noise masking.
In the official ISO/MPEG subjective tests Layer I codec showed an excellent performance at a stereo bit rate of 384 kbit/s.

## Slide 10: MPEG 1 layer 2 Audio
Similar to the Layer I coder but better performance through three modifications.
  The input to the psychoacoustic model is a 1024-point FFT leading to a finer frequency resolution for the calculation of the global masking thresholds.
  Exploiting redundancies between three adjacent 12-sample blocks.
  A finer quantization is provided.
In the official ISO/MPEG subjective tests Layer II codec showed an excellent performance at a stereo bit rate of 256 kbit/s, and when using joint stereo, at 192 kbit/s.

## Slide 11: MPEG 1 layer 3 Audio (MP3)
Hybrid (subband/transform) coding
Variable bit rate coding
Layer III has improved:
  frequency mapping
  an analysis-by-synthesis approach for the bit allocation
  an advanced pre-echo control
Layer III employs nonuniform quantization with entropy coding.
In order to achieve a higher frequency resolution closer to critical band partitions:
  the 32 subband signals are subdivided in frequency content by applying a six-point or 18-point modified DCT (MDCT) with 50% overlap to each of the subbands.
  the six-point MDCT is applied in case of expected pre-echoes.
  the maximum number of frequency components is 32*18=576 each representing a bandwidth of only 24000/576 = 41.67 Hz.
At a stereo bit rate of 1128 kbit/s the ISO/MPEG subjective tests gave an increase in impairment score of around 0.6 over Layer II.

## Slide 12: MPEG 2 Audio
2 multichannel audio coding standards, one of which will be forward- and backwards-compatible with MPEG-1.
Forwards-compatible with MPEG-1: The multichannel decoder can properly decode MPEG-1 mono or stereo signals.
Backwards-compatible with MPEG-1: An MPEG-1 stereo decoder can deliver a correct (front left and front right) stereo signal when decoding a future MPEG-2 multichannel bit stream i.e., the decoder will reproduce a meaningful down-mix of the original five channel.
Nonbackwards-compatible (NBC) MPEG-2 coding
The NBC multichannel coding mode will have the sampling rates, audio bandwidth, and channel configurations of MPEG-2 audio, but shall be capable to operate at bit rates from 32 kbit/s up to a bit rate sufficient for high quality audio.

## Slide 13: Audio Encoding Issues
Bitrate vs fidelity tradeoff
Computational effort (time) in encoding/decoding
Delay and window size
Recovery from lossy transmission, packet errors
Noisy environments (for speech, music encoders)

## Slide 14
Sound Editing
GoldWave (www.goldwave.com)-
  requires a sound card.
  digital audio sound player, recorder and editor
  can load, play and edit many different file formats
    .wav, .au, .voc, .snd, …
  displays separate graphics for the left and right channels
  very easy to use
  good sound quality
CoolEdit (http://www.syntrillium.com/cooledit )
SonicFoundry SoundForge,
SOX conversion tool
Winamp
MS SoundRecorder, Windows Media encoder

## Slide 15
Tips for Audio on the Web
There is no generic audio standard on the Web
Listening to 16-bit sounds on an 8-bit system results in strange effects
Users will be annoyed if they spend a lot of time downloading a sound and they can’t play it
Distribute only 8-bit sounds on your Web page
Or, provide different sound files in both 8- and 16-bits
Record in the highest sampling rate and size you can, and then process down to 8-bit
Keep file size small
  downsampling to 8-bit
  use a lower sampling rate
  use mono sounds
Describe what format those sounds are in
  WAVE, AIFF, or other format
  Providing the file size in the description is a politeness to help estimate download times
If you need high sound quality and have large audio files:
  Use a smaller sound clip in downsampled format as a preview
  or for those who can’t to listen to the higher-quality sample.
Check out http://music.acu.edu/www/iawm/articles/june96/techtips.html

## Slide 16: Audio Encoding Reference Links
Sub-Band Coding
MPEG Audio
http://www.realnetworks.com
  esp. resources and tutorials

## Slide 17
Speech Compression
That’s all for today