## Slide 1: Wireless Technologies Wireless Andrew
Chuck Bartel
Director of Operations
Computing Services
Carnegie Mellon University
crb@cmu.edu

## Slide 2: Introduction To Wireless Data Technology
The RF Spectrum
Components of an RF System
Overview of Options

## Slide 3
The RF Spectrum

## Slide 4: ELECTROMAGNETIC SPECTRUM
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Frequency Bands- ISM
Extremely
Low
Very
Low
Low
Medium
High
Very
High
Ultra
High
Super
High
Infrared
Visible
Light
Ultra-
violet
X-Rays
Audio
AM Broadcast
Short Wave Radio
FM Broadcast
Television
Infrared wireless LAN
902 - 928 MHz
26 MHz
Cellular (840MHz)
NPCS (1.9GHz)
2.4 - 2.4835 GHz
83.5 MHz
(IEEE 802.11)
5 GHz
(IEEE 802.11)
HyperLAN
HyperLAN2
Industrial, Scientific, and Medical (ISM) bands
Unlicensed, 22 MHz channel bandwidth
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Frequency Bands - MMDS
Multichannel Multipoint Distribution System (MMDS) 2.500 to 2.690 GHz
  Licensed Spectrum
  33 Channels at 6 Mhz
  Key Owners: CAI Wireless (MCI Worldcom), PCTV (Sprint), ATI (Sprint), CS Wireless, Heartland Wireless. Wireless One
  Originally envisioned as wireless CATV, DirectTV has already captured this market in the US
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Frequency Bands- LMDS
Local Multipoint Distribution System (LMDS) 27.5-28.35, 29.10-29.25, 31.00- 31.30 GHz
Licensed Spectrum-1150 MHz in the A block, 150 MHz in the B block
Propagation limitations require good quality line-of-sight
Key Owners: Nextlink (now holds 95% of top 30 LMDS markets), Winstar
Uses: Local loop wire replacement (voice & data)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8
Components of an RF
Communications System

## Slide 9: Communications 101 Simplified Communication System
Transmitter
Wireless
Digital Information
Antenna
Subsystem
Analog
Information
or
Digital Information
Analog
Information
or
Receiver
Transmitter
Wired System
Digital Information
Analog
Information
or
Digital Information
Analog
Information
or
Receiver
Notes: <number>
<footer>
<header>
<date/time>
Transmitters and Receivers are used to source and sink information in an electronic communications system. A number of technical challenges arise from building transmitters and receivers; these devices must interface with sources of information (human) that are stochastic in nature. The issue is that receivers must ‘synchronize’ to the frequencies being transmitted by the transmitter. This means that the receivers must have a priori knowledge of the information being transmitted. This, of course, is impossible due to the heuristic nature of the signals (information) being generated.
To solve this problem as well as other technical issues posed by the channel (either wired or wireless), communications systems generate a ‘carrier’ frequency preset (a priori) and tuned by the transmitter and receiver. The information to be transmitted is then modulated onto this carrier by a variety of methods.
Analog signals may be modulated onto a carrier using Amplitude Modulation (AM), Frequency Modulation (FM), or Phase or Frequency Shift Keying (PSK/FSK).
Digital signals may be modulated onto the carrier by variations of Phase Shift Keying.
Receivers perform the reverse operation of the transmitter.

## Slide 10: Antenna Concepts Omni Directional Antenna
High gain omnidirectional antennas will create more coverage area in far distances, but the energy level directly below the antenna will become lower, and coverage here may be poor
Poor coverage area underneath antenna (null)
Side View
(vertical pattern)
Polar View
(horizontal coverage area)
beamwidth
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Antenna Concepts Directional Antenna
For directional antennas the lobes are pushed in a certain direction, causing the energy to move be condensed in a particular area.
Very little energy is in the back side of a directional antenna.
Directional antennae include parabolic dish, yagi, planars, and many more
Poor coverage area underneath antenna (null)
Side View
(vertical pattern)
Polar View
(horizontal coverage area)
beamwidth
Notes: <number>
<footer>
<header>
<date/time>
Effective Isotropic Radiated Power (EIRP) = Ptranmit + Antenna Gain; where Ptranmit is the transmit power in db.
Antenna directional gain is the ratio of the power required to produce a given field strength at a given location using a reference antenna (isotrope), compared to the power required to produce the same field strength with a directional antenna.
Additional antenna gain may be obtained by using combinations of two or more antenna elements to form an antenna array. Depending on the method used to excite the additional elements, antenna systems are classified as parasitic or driven arrays.

## Slide 12: Line-of-Sight
Signals travel in a straight line but they spread as they travel
The required beam clearance is called the Fresnel Zone
The antennas must be high enough to allow the first Fresnel zone to clear the hills, earth bulge, buildings or trees
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Building-to-Building-Fresnel Zone
Antenna Height
  Line-of-Site is really ellipse
  Clear of all obstacles year round
Fresnel
Earth Curvature
Antenna
Height
Obstacle Free
Notes: <number>
<footer>
<header>
<date/time>
A main consideration in a building-to-building design is the fresnel zone which we think of as line-of-site. Line-of-sight however does not exist as a line between the two antennas but more as an ellipse a which should be clear of obstacles year round. Because of the ellipse, we must ensure that the antennas are mounted high enough to provide for clearance at the mid-point of the fresnel zone. As the distance increases an additional concern becomes the curvature of the earth where line of sight disappears at 16 miles. Therefore we must take into consideration curvature of the earth when determining your antenna mounting height. The upcoming slides will provide you with rules of thumb for antenna mounting heights for distances in increments of 5 miles up to 25 miles links.

## Slide 14: Overview of Options

## Slide 15: Wireless Data Options
WAP
CDPD (Wide Area Network- WAN)
Ricochette (WAN)
Wireless LANs (802.11)
Bluetooth

## Slide 16: WAP (Wireless Application Protocol)
Set of specs developed by WAP Forum
Uses WML (Wireless Markup Language)
Designed for handheld devices with limited memory/CPU/screen size (Cell phones, pagers, PDAs)
Allows for mixed OS, mixed media
Assumes low bandwidth and erratic connections
Defacto standard-200+vendors

## Slide 18: Cellular Data Packet Distribution - CDPD
CDPD - Analog Cellular Transmission Technology :
Uses the “dead space” between cellular phone calls for bandwidth
Limited Bandwidth – 28Kbps

## Slide 19: Metricom-Ricochet-Wireless WAN
ISM Band – 900Mhz, Frequency Hopping
Currently in limited number of cities:
San Francisco, Washington DC
Limited bit rate –now 28.8Kbps
Recent FCC approval allows higher bit rates up to 128Kbps
Uses an external wireless modem

## Slide 20: Ricochet-Wireless WAN (Cont.)

## Slide 21: Wireless LAN Solutions
Spread Spectrum Techniques
802.11 Overview

## Slide 22
Spread Spectrum Techniques

## Slide 23: Spread Spectrum
Originally intented for military use as a way to prevent jamming of communications
Concept is to spread the communications over a wide range of the radio spectrum making jamming difficult.
2 main approaches –Direct Signaling and Frequency Hopping.
Co-developed by actress Hedy Lamar (WWII)

## Slide 24: Spread Spectrum Techniques Direct Sequence
2 Mbps data rate without complex modulation scheme
3 Access Points can occupy same area
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Spread Spectrum Techniques Frequency Hopping
79 Channels, 1 MHz Each
Changes frequency (Hops) at least every 0.4 seconds
Synchronized hopping required
Frequency
2.400 GHz
2.483 GHz
1
2
3
4
5
6
7
8
9
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Which is best- DSSS vs. FHSS?
Depends on your application:
Pros/ FH: Cheaper to design & develop
Cons/FH: May not scale to higher speeds
Pros/DS: Better scaling to higher speeds
Cons/DS:More complex to design
Who’s winning – Direct Sequence

## Slide 27: IEEE 802.11
Specification For Over The Air Interface Between Wireless Clients and Base Stations (Access Points)
Specifies MAC and PHY Layer Like 802.3 Ethernet and 802.5 Token Ring
Conceived in 1990. Final Draft Ratified June 26, 1997

## Slide 28: IEEE 802.11 Architecture
Wireless Nodes
  Clients
  Access Points (AP) - interfaces to a wired network
Basic Service Set (BSS)
  two or more wireless nodes that have recognized each other and established communications
Extended Service Set (ESS)
  a series of overlapping BSSs’ each containing an AP connected via a Distribution System (DS). The DS is typically Ethernet

## Slide 29: IEEE 802.11 Architecture
Two Connection Options:
  Infrastructure Network
  Ad Hoc Network
Infrastructure Network
  Contains at least two nodes one of which is an AP
  client to access point (to wired network)
  all nodes communicate through the access point
Ad Hoc Network
  client to client (no access to the wired network)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Wireless LAN LAN Topology
Notes: <number>
<footer>
<header>
<date/time>
The Basic Service Area or microcell can consist of nothing more than two or more wireless PC’s with a wireless network card.
Operating systems such as Windows 95 or Windows NT has made this type of network very easy to setup.
This can be used for a small office (or home office) to allows a laptop to be connected to the main PC, or for several people to simply share files.
This type of network has one drawback- Coverage limitation. Everyone must be able to hear everyone.

## Slide 31: Wireless LAN Typical Single Cell Coverage
Wireless Clients
LAN Backbone
Notes: <number>
<footer>
<header>
<date/time>
To extend the Basic Service Area, or to simply add wireless devices and extend range of an existing wired system, an Access Point can be added to the BSA.
The Term Access Point indicates it is the point at which the wireless clients can ACCESS the backbone.
The Access Point attaches to the backbone (usually Ethernet), and communicates with all the wireless devices in the cell area. The AP is the master for the cell, and controls traffic flow to the network.
The remote devices do not communicate directly with each other, they communicate to the AP.

## Slide 32: Wireless LAN Typical Multicell Topology
Access Point
Wireless Clients
LAN Backbone
Wireless
“Cell”
Channel 1
Channel 6
A
B
C
D
Notes: <number>
<footer>
<header>
<date/time>
If a single cell does not provide enough coverage, then any number of cells can be added to extend the range. This is known as an Extended Service Area.
The cells usually have 10-15% of overlap to allow the remotes to roam without losing RF connections, and provides maximum coverage with minimum cost. For the Direct Sequence all APs are manually set to the a frequency. For the Frequency Hopping system, the hopping pattern is, by default, automatically selected.
You can select channels that are on non-overlapping, non-interfering frequencies on DS, or on FH, different hopping patterns, and the overlap is not critical, as long as it has full coverage areas. The clients will chose the best AP based upon the association processed discussed earlier.

## Slide 33: IEEE 802.11 PHY Layer
Three Modulation Methods
  Infrared Pulse Position Modulation (300-428 Ghz)
  Direct Sequence Spread Spectrum (DHSS) 2.4 Ghz
  Frequency Hopping Spread Spectrum (FHSS) 2.4 Ghz
DSSS and FHSS Actually Operate at 2.4-2.4835 Ghz In the U.S. Channel Bandwidth = 22 Mhz and 1 Mhz respectively
2.4 Ghz Band - Unlicensed Band For Industrial, Scientific, and Medical (ISM) Use
Data Rates of 1 Mbps and 2 Mbps For All Three PHYs and 11 Mbps DSSS now possible (IEEE 802.11b)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: IEEE 802.11 MAC Layer Services
Data Transfer
  Uses CSMA/CA as media access scheme
Association
  Establishment of links between clients and APs
Authentication/Privacy
  Wired Equivalent Privacy (WEP) Specifies Shared Key between client and AP
  WEP specifies 40 bit or 128 bit RC4 encryption
Power Management
Notes: <number>
<footer>
<header>
<date/time>
Must use collision avoidance because 802.11 operates in half duplex mode and a transmitting station can not listen when transmitting.

## Slide 35: IEEE 802.11 Roaming Implementation
Steps to Association:
AP sends Probe Response
Client evaluates AP
response, selects best AP.
Client sends association
request to selected AP (A).
AP A confirms association
and registers client.
Access
Point
A
Access
Point
B
Initial connection to an Access Point
Client sends probe
Client sends authentication
request to selected AP (A).
AP A confirms authentication
and registers client.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: IEEE 802.11- Standards Status
Although Standards Based, No Guarantees Of Vendor Interoperability
No AP to AP Coordination For Roaming
No 802.11 Conformance Test Suite…see University of New Hampshire web site
Notes: <number>
<footer>
<header>
<date/time>
The University of New Hampshire has been most active with interoperability testing. Tests show that client to Access Point interoperability exists to a large degree. AP to AP

## Slide 37: IEEE 802.11 Evolution
Spec. Description Est. Data Rate Act. Data Rate Frequency
802.11 Most widely deployed 2 Mbps 1.6 Mbps 2.4GHz
802.11b ratified 9/99 11 Mbps 5.5 Mbps 2.4GHz
802.11a In development 54 Mbps 25 Mbps 5GHz
HiperLAN Developed by European 24 Mbps 11 Mbps 5GHz

## Slide 38: W.E.C.A.-Promote “One Wireless Thing”
Same Wireless LAN Technology for:
  Enterprise
  Small Office
  Home
  Public Access
Create the Wi-Fi Brand.
www.wirelessethernet.org
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: Bluetooth
Wireless PAN (Personal Area Network)
Founded by Bluetooth SIG (members-Ericsson, IBM, Intel, Nokia, Toshiba)
Open standard for short-range transmission between digital devices
Up to 720Kbps (range 10 to 100 meters)
Intended for wireless peripheral connections
2.4Ghz, ISM band

## Slide 40: Q & A

## Slide 41: Wireless Andrew- Deployment Issues & Challenges
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Wireless Andrew
Project Overview

## Slide 43: Carnegie Mellon Background
Private research university (R1)
50+ buildings on 100+ acre campus
Half of buildings are on contiguous main campus
Early adopters in use of distributed computing and networks (Andrew Project)

## Slide 44: Background -- 1994
Dozens of Mobile, Wearable, and Wireless Computing Projects
Multidisciplinary Collaboration Spanning Several Campus Buildings
More than $20M in Research Funding
No Comprehensive Network-- Each Research Project Left to Fend for Itself
Notes: <number>
<footer>
<header>
<date/time>

## Slide 45: Vision -- 1994
Establish Common Research Network
NSF Grant - $550,000 over 2 years
Build an Experimental, High-Speed, Wireless Network
  Support research projects in wireless communication and mobile computing.

## Slide 46: Implementation -- 1995-1998
No Standard Existed for Wireless LANs
  Evaluation + Selection: ATT/Lucent 915Mhz
Deployed network in 5 campus buildings
Enable use by approximately 150 users
Research Network = Limited Support

## Slide 47: Background -- 1998
Successful Wireless Research Network
Growing use of Laptops
Need for Wireless Production Network
Wireless LAN Standard 802.11 Adopted by IEEE
Lucent Grant to Support Campus-Wide Deployment (400 Access Points/cards)

## Slide 48: Implementation -- 1998-2000
Deploy Network Campuswide
  30+ Buildings (2.8M sq ft) + Outdoor Areas
Use by Virtually Anyone on Campus
Provide Support Equivalent to Wired Network
Lucent’s WaveLAN Product - 2.4GHz, IEEE 802.11 Compliant

## Slide 49: Deployment Issues & Challenges

## Slide 50: Key Components- Wireless LAN
Access Point - network device that links wireless stations to the wired network -- $900/unit
Wireless NIC cards- EISA bus or PC card -radio transceivers for the end users -- $795/card
$595/card
$275/card
$125/card
Notes: <number>
<footer>
<header>
<date/time>

## Slide 51
For every Access Point in a building, we need:
110 vac plug
Data cable capable of supporting a 10BaseT connection
Since most of the Access Points end up above ceilings or other out of the way places, new dedicated cables needed to be installed.
Avg. cost per installed
AP $1.9K (Cost of AP- $.9K)
Wireless doesn’t necessarily mean Without Wires
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: Design factors to consider
Interference
Mobility – Roaming
Coverage vs Capacity
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53
Examples of potential interference sources in the
2.4GHz ISM band (IEEE 802.11)
Microwave ovens
2.4GHz Cordless phones
Bluetooth
Other 802.11 LAN devices
Other 2.4GHz LAN devices
How do you regulate these on your campus?
Can you? Should you?
Interference
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: Other complicating factors
Mobility complicates wireless designs.
Wireless design is as much Art as Science.
The wireless industry is evolving their products to support campus environments (but they are still behind the wired side of networking).
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: Keys to Design Success (for CMU)
We developed new approaches to building-wide wireless design with the vendor.
Colorized coverage maps
Design review meetings
Designed for coverage (not for capacity)
Based on our experiences, the vendor improved their design tools.

## Slide 57: Wireless Andrew Infrastructure
Standards-Based Wireless LAN in all Academic and Administrative Buildings
Comprehensive Coverage with Roaming Enabled (Mobility is Seamless)
Wireless LAN is Connected to the Campus Backbone and Internet
Supporting 600-1000 Users
Add’l Info available at URL:
http://www.cmu.edu/computing/wireless

## Slide 59: Where are we now?
We cover 30+ buildings (to date)- 350 APs
We cover over 2.8 M sq. ft. of office/lab/classroom space
We cover roughly 99% of the academic campus.
We have 1400+ users
We have upgraded our network to the IEEE 802.11(b) standard (11Mbps)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: Wireless Campus by June
Academic and Administrative Buildings
Residence Halls, Parking, etc

## Slide 61: How Much?? $$$, coverage
Average cost of wireless: <$1K for AP, <$1K for power/data install, + wired network infrastructure costs+design labor costs.
Avg pwr/data install schedule– 8 locations / wk
Avg AP installs - 8 per day
AP to sq.ft. density: depends on building construction and arch concerns, ex: older construction 25 A.P.s cover 228Ksq.ft., newer construction 12 A.P.s cover 210Ksq.ft.
Best coverage 17.5Ksqft/AP, Worst 3.4Ksqft/AP
Your mileage WILL VARY!!!

## Slide 62: Wireless Andrew Issues/Futures
Coverage vs capacity – Why not both?
“Airspace policy” and interference –Bluetooth,…
Keeping up with demand- scaling issues
Security-Authentication
Next Gen 802.11(a) –5Ghz Issues:
Fork-lift upgrade? Ease of transition?

## Slide 63: Wireless Andrew Configurations
Workstations/OS
  Windows 95, 98, NT
  Macintoshes
  Linux (CMU “Andrew” version)
  Windows CE
Applications
  data files
  Internet/Intranet
  email
  Web
  centralized calendaring

## Slide 64: Uses of wireless infrastructure
Untethered access to campus network:
Follow-on project - Handheld Andrew:
enhancing usability of palm and HPCs
with access to campus network –
Researcher’s “Field of Dreams”

## Slide 65: Handheld Andrew
Project Overview

## Slide 66: Project Goals
Further CMU’s longstanding anytime, anyone, anywhere computing concept
Integrate handheld devices with our computing and communications infrastructure
In particular, leverage wireless infrastructure

## Slide 67: Project Goals, continued
Extend computing and communications beyond desktop
Replace synchronized access with online wireless
Enable handheld devices as full peers on network
Result: Effective use of handheld devices as personal, group, and internet information managers

## Slide 68: Existing Infrastructure
802.11 DS campuswide
Authentication via Kerberos
  Currently K4, moving to K5
Directory via LDAP
  Mixed now, but moving to pure LDAP

## Slide 69: Existing Infrastructure
Mail via IMAP
Calendar via CorporateTime
Notification via Zephyr (developed at MIT as part of Project Athena)

## Slide 70: Technical Goals
Integrate handheld devices into existing infrastructure
  802.11, Kerberos, LDAP, IMAP
Specific applications: mail, calendar, notification
Demonstrate value of overall environment

## Slide 71: Platform Selection Criteria
General purpose
Robust development environment
Successful in market
802.11 DS support
Contenders: Palm, Psion, Windows CE

## Slide 72: Applications
Mail: Pocket Outlook
Calendar: Web/CorporateTime
Notification: Zephyr

## Slide 73: Supporting Services
Authentication: Kerberos 4, Kerberos 5, and Active Directory
Printing: lpr  klpr
Software management: investigating needs (push vs pull, full backup/restore, state recording and restoration) and modes (media, direct vs PC-mediated)

## Slide 74: Handheld Andrew
Early Uses

## Slide 75: General Use
Heavy use by students, faculty and staff
Mostly used for basic communication (email, zephyr, web browsing)
Other “more interesting” uses, ones we hadn’t envisioned or tested for
Very high convenience factor associated with ‘anytime, anywhere’ network access

## Slide 76: General Issues
Competition for attention in meetings
Increasingly used in lieu of traditional network (at least for some of us)
Mobility & scaling (single subnet now)
Only cost to user is card purchase
  promote use, recognize costs, upgrade service
Bottom line – As supplement to the wired network, huge success

## Slide 77: Academic Interest
Support lab style use in classrooms
  All classrooms w/ projection, video, network, etc; not all students w/ computer
Enhance communication outside class
Increase interaction between instructor and students in large courses
Support student software development projects on mobile computers

## Slide 78: Academic Projects – Wireless
Four classes in Business Administration program – “Virtual Cluster” experiment
  Department proposed laptop ownership; but was rejected at university level.
  Challenge: find a way to supplement rather than require laptop ownership
  Solution was 30 laptops w/ wireless, checked out in the 10 minute window between classes and used in traditional classroom. And it worked….

## Slide 79: Virtual Cluster Evaluation
Student survey (didn’t meet-met-exceed):
  Checkout (0%-19%-81%); in (0%-14%-86%)
  Hours (24%-52%-24%)
  Visio (6%-50%-44%)
  Email (5%-35%-60%)
  Web (5%-29%-66%)
  File/print (0%-56%-44%)
95% used in class, 57% for every class; 67% used outside class

## Slide 80: Virtual Cluster Evaluation (2)
Faculty feedback (most active: Software Analysis & Design; used CASE tool in class)
  “It was a good pilot. Students were engaged.”
  Early bandwidth issues resolved by week 3
  “Didn’t try to police them. They know I don’t relecture so if they miss it, it’s too bad.”
  Intent is to repeat (and expand) next year
    “I’ll get more creative” - more sophisticated exercises; collaborative work or exchanging work across teams

## Slide 81: Academic Projects – Wireless + Handheld
Wireless + Handheld - Vendor Grants
  Modern Chemistry – Lecture course, 100 students; concept test delivered using Pebbles software (research project)
  Rapid Prototyping and Design – Software project course; student groups developed applications for handhelds
  Information Systems – System design project course; utilize web-based communication tool for teams

## Slide 82: Handheld Class Use Evaluation
Student survey (both classes)
  20% used daily, another 48% few x/week
  75% used concept test, 46% web, 43% email, 40% games (<10% other uses)
  91% classroom, 48% study area, 37% lounge, 25% cluster; 25% dining, + outside
  43% believe that handhelds will eventually be used widely in courses; 39% believe will be useful outside but not in class; 18% not useful at university

## Slide 83: Handheld Use Evaluation (2)
Of 91% who used in the classroom:
  12% - neither positive or negative impact
  22% - impact was exclusively positive
  66% - characterized impact as both + and -positive and negative
For the students using concept tests:
  96% agree/strongly agree: concept tests are a useful part of the lecture
  65% a/sa: liked handhelds for concept tests because others couldn’t see response
  61% yes: should use next year

## Slide 84: Academic Issues
Can be a distraction; no reasonable way to “shut off” the network access
  Mandate only for class (where do notes fit)?
Something else for students to worry about
Bottom line – Students neutral to positive; faculty go with student assessment. Big issue is whether we can/should support it or stop it. Are we just an MP3/browser/ email reader away from seeing 90% adoption rate?

## Slide 85: Handheld Andrew

## Slide 86: Q & A

## Slide 87: Acknowledgements
Lucent
Cisco
Computer World
TechWeb
Bluetooth SIG
Metricom
Carnegie Mellon University
In the development of these materials

## Slide 88: Wireless Andrew- Deployment Issues & Challenges
Notes: <number>
<footer>
<header>
<date/time>