## Slide 1: eBusiness Technology
Michael I. Shamos, Ph.D., J.D.
Co-Director, Institute for eCommerce
Carnegie Mellon University
Pittsburgh, Pennsylvania USA
email homepage

## Slide 2: Why Technology?
Electronic commerce is not “electronic” without technology
Business models can only be implemented if the technology is feasible
Technology determines the range of possible business models
The technology component of this course is a survey of technologies applicable to eCommerce

## Slide 3: What is Commerce?
Middle French, from Latin commercium, from com- (together)+ merc- (merchandise) (1537) “The exchange or buying and selling of commodities on a large scale involving transportation from place to place.”
Buying and selling ( transactions )
Large scale (  scalability )
Transportation ( supply chain )
NEED TECHNOLOGY
TO SUPPORT
ALL OF THESE

## Slide 4: What is Electronic Commerce?
Remote business transactions mediated electronically
online shopping (staples.com, buyersindex.com)
product recommendations (brandwise.com)
online stock trading (Schwab)
electronic auctions (eBay)
business-to-business transactions (e.g. procurement) (Seacat, Ariba)
cyber-intermediaries (freemarkets.com, instill.com)
electronic data delivery (Corbis images, MP3)
online services (cargo tracking, greeting cards)
postage (stamps.com, E-Stamp.com)

## Slide 5: The Electronic Marketplace
BUYER
LOCATES
GOODS
NEGOTIATION
PAYMENT
SALE
DELIVERY
POST-SALE
SERVICE
SELECTION
OF GOODS
SEARCH ENGINE
SHOPPING BOT
AGGREGATOR
ON-LINE CATALOG
AUTOMATED AGENTS
TRACKING AGENT
ON-LINE HELP
INTERNET TELEPHONY
CUSTOMER PREFERENCES
BARGAINING STRATEGIES
PRICE SENSITIVITIES
CREDIT/PAYMENT INFORMATION
ON-LINE PROBLEM REPORTS
FOLLOW-ON SALES OPPORTUNITIES
SOME TECHNOLOGIES USED:
SOME INFORMATION GATHERED:
BROWSING BEHAVIOR
DELIVERY REQUIREMENTS
E-PAYMENT SYSTEMS
CONFIGURATOR
RECOMMENDER AGENT
TRANSACTION PROCESSOR
DATA INTERCHANGE
CRYPTOGRAPHY
BROWSER SHARING
MARKET BASKET
INTERNET
PERSONAL DATA
CUSTOMER SATISFACTION
SEARCH BEHAVIOR
EFFECTIVENESS OF PROMOTIONS

## Slide 6: The Internet

## Slide 7: The Internet
How does the Internet connect everyone?
How messages move on the Internet
What are IP addresses and domain names?
Is it reliable enough for a business to depend on?

## Slide 8: Ecommerce Statistics
Web traffic doubles every 98 days (Korea: 92)
  The number 1 becomes 4 billion in 8 years
  The paradox of exponential growth
Ecommerce activity doubles every year
  U.S. (1999) $130 billion
    B2B exceed B2C by a factor of 6; will go up to 14
  Does not include
    foreign exchange ($2T/day), interbank ($2T/day), securities ($100B/day)
  By 2003, global ecommerce $3.2T, 10% of current world economic product

## Slide 9
0
10,000,000
20,000,000
30,000,000
40,000,000
50,000,000
60,000,000
70,000,000
80,000,000
Jan-95
Jan-96
Jan-97
Jan-98
Jan-99
Jan-00
SOURCE: NGI
Adjusted old survey data
Internet Host Count 1995-2000
FEBRUARY 2000
72,400,000
New survey data
HOST = DOMAIN NAME
Notes: <number>
<footer>
<header>
<date/time>
3

## Slide 10
Projected
Historical
SOURCE: NGI
Projected Internet Host Count
1 BILLION
AUG. 2005
100 MILLION
JAN. 2001
10 MILLION
JAN. 1996
1 MILLION
JUL. 1992
Notes: <number>
<footer>
<header>
<date/time>
4

## Slide 11: Bandwidth Review
Bit (b) = a unit of information, 0 or 1
  10 bits convey 1024 different messages
  20 bits convey > 1 million
  30 bits > 1 billion messages
Bandwidth of a communication channel = number of bits per second it transmits
THERE IS NEVER ENOUGH BANDWIDTH
All channels have limited bandwidth
Transmitting 1 MB at 56K bps takes 143 sec.
  At 56K, 1 GB takes 40 hours; at 7Mbps 19 minutes;
  at 1 Gbps 8 seconds; at 1 Tbps .01 seconds)

## Slide 12: BANDWIDTH APPLICATION TECHNOLOGY
Streaming Video + Voice
Browsing, Audio
E-mail, FTP
Paging
Video Conferencing, Multimedia
Telnet
ISDN
FDDI
T3/E3
T1/E1
New Modem
Wireless WAN
Old Modem
4.8
19.2
56K
128K
T3 = 44.7 Mb
OC3 = 155 Mb
In Kbps
Virtual Reality, Medical Imaging
1 gigabit
ADSL
Full-motion HDTV
Gigabit
Ethernet
Copper
Fiber
Experimental
1 terabit
All U.S. telephone conversations simultaneously
T1 = 1.544 Mb
DSL ~ 7 Mb
OC12 = 622 Mb
Human speech = 30 bps
BANDWIDTH LIST
CABLE
CABLE 10-38Mb

## Slide 13: Dense Wave-Division Multiplexing
0
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
200
400
600
800
1,000
1,200
1,400
OC-48
OC-192
OC-192, 2
OC-48, 40
OC-192, 16
OC-48, 96
OC-192, 32
OC-192, 48
OC-192, 80
OC-192, 128
1.7 Gb
565Mb
135Mb
Single
Fiber
Capacity
(Gigabits/sec)
1 Terabit =

## Slide 14
LINK

## Slide 15: Internet Backbone
Just like a subway system -- lines interconnect
AT&T CERFnet

## Slide 16: Structure of the Internet
Europe
Japan
Backbone 1
Backbone 2
Backbone 3
Backbone 4, 5, N
Australia
Regional A
Regional B
NAP
NAP
NAP
NAP
SOURCE: CISCO SYSTEMS
MAPS
UUNET MAP

## Slide 17: Internet Backbone Structure
Level 1 (interconnect level, NAPs)
  billions of pages per day
Level 2 (national backbone, MAE, FIX)
  Federal Internet eXchange Points
Peering
  (Agreement to connect & share routing info)
Level 3 (regional providers, state level)
Level 4 (local ISP)
Level 5 (companies, individuals)

## Slide 18: Network Access Points (NAP)
Where Tier 1 networks interconnect
  Chicago (Ameritech)
  MAE West, Pac Bell
  New York NAP (Sprint)
  MAE East (MSF), CIX
  Minneapolis
  Seattle
NAP Connection Process
Tier 2 MAEs (Metropolitan Area Ethernets):
  Houston, Dallas, LA, Big East (ICS)
Exchange Point information
European Exchange Points

## Slide 19: eCommerce is 24/365
MAE East Aggregate Input Traffic: Tuesday, Nov. 23, 1999
Low: 1180 Mbps
4:15 a.m. EDT
Peak: 2260 Mbps
4:00 p.m. EDT
Traffic through
a major Network
Access Point
(NAP)
24-hour cycle
Megabits/second

## Slide 20: Satellite Access (InterSatCom)
GEOSYNCHRONOUS
ORBIT = 22,000 MILES
LATENCY = 1/4 SEC.

## Slide 21: World Internet Population 9/99
World Total 201 MILLION
Africa 2 million
Asia/Pacific 34 million
Europe 47 million
Middle East 1 million
Canada & USA 112 million
Latin America 5 million
SOURCE: NUA INTERNET SURVEYS

## Slide 22: Web Availability Requirements
Beta Test
Most commercial
systems
Mission-critical
systems
Real-time
Carrier-quality
systems
PERMISSIBLE DOWNTIME
REQUIRED UPTIME

## Slide 23: Plain Old Telephone System (POTS)
Communication
requires a series
of dedicated lines
from point A to B
A
B
Capacity is tied
up for the entire
call even if no
one is talking
Each person can
talk to one other
person at a time
This network is
CIRCUIT-SWITCHED
Also true of
cellular phones
If one link fails,
communication
is lost

## Slide 24: Network Topologies
More than two computers causes complications:
Each machine on a network must have a unique address
If machine 2 sends a message to machine 4, what tells 1, 3 and 5 to ignore it, but 4 to listen?
Ethernet protocol. Demo.
1
2
3
4
5
LAN BUS TOPOLOGY
LAN = LOCAL AREA
NETWORK

## Slide 25: IP (Internet Protocol) Routing
Router A can send
the packet either way
Machine 35 wants to send a
packet to Machine 249.
Routers determine the path
the packet will take.
Routers
A
B
Machine
1.35
Machine
3.249
NETWORK 4 &
IT’S ROUTER
Machine
2.16
4.1
5.9
ROUTING STATISTICS
NUMBER OF ROUTES

## Slide 26: Routers
NORTEL
CISCO
3COM

## Slide 27: Packet Switching (TCP/IP)
TCP = TRANSMISSION
CONTROL
PROTOCOL
(Breaks messages into packets
and reassembles them)
IP = INTERNET
PROTOCOL
(Moves packets around
the Internet)
SOURCE: J. DECEMBER
DEMO

## Slide 28: Internet Performance
The Internet is heavily instrumented
Its performance is constantly monitored
Internet traffic report
AT&T network status

## Slide 29: Client/Server Architecture
Fundamental Internet structure
Client requests service; server provides it
Data exchanged only through real-time messages
Server may become a client to a different server
Server 2
responds
to client 1
The Internet
Client 1 requests
service from server 2
1
2
3
Client 2 requests
service from server 3
Server 3 responds
to client 2

## Slide 30: IP Addresses
Machines on the Internet need an addressing scheme (or couldn’t receive packets!)
Each machine has a 32-bit address assigned by the Internet Corporation for Assigned Names and Numbers (ICANN).
In the U.S., American Registry for Internet Numbers (ARIN)
In Europe, Réseaux IP Européens (RIPE)
Addresses are written in dotted decimal notation:
128 . 2 . 218 . 2
10000000 00000010 11011010 00000010
Current max number of IP addresses = 232 ~ 4,000,000,000

## Slide 31: Domain Names
IP addresses are inconvenient to remember 128.2.218.2 v. euro.ecom.cmu.edu (fully qualified)
Domain names are alphanumeric aliases for IP addresses. They form a tree structure of FQDNs:
ROOT
.GOV .COM .MIL .NET .EDU .ORG .IT
CMU PITT MIT
AMAZON MCKINSEY YAHOO
GSIA CS ECOM HEINZ
YEN EURO DOLLAR PESO
207.237.113.94
128.2.218.2
208.216.182.15
128.2.218.4

## Slide 32: Converting Domain Names to IP Addresses
IP addresses track topology (physical location).
Domain names track administrative responsibility.
There’s no conversion formula. Has to be looked up!
DNS (Domain Name System) is a distributed database of names
Network servers maintain tables of domain names.
IP addresses are obtained by resolvers that communicate with nameservers on the net
DNS at CMU

## Slide 33: DNS Resolution of “abc.foo.com”
What is the IP address
of abc.foo.com?
SOURCE: CISCO SYSTEMS
client
Local DNS
Resolver
Try .com
Root DNS
.com DNS
Try foo.com
foo.com DNS
abc.foo.com is 202.168.14.12
+ Cache
202.168.14.12

## Slide 34: URL: Uniform Resource Locator
URL identifies a specific resource on a server in a domain
URL tells what protocol to use to access the resource
URL format:
http://euro.ecom.cmu.edu/program/courses/index.shtml
protocol://domain_name/path_name

## Slide 35: Other URL Protocols
https: (secure, encrypted HTTP)
ftp: (file transfer protocol)
mailto: (email)
telnet: (remote login)
news: (obtain Usenet news)
irc: (Internet Relay Chat)
finger: (obtain information about a user)
gopher: (indexes of text files)
archie: (ftp databases)

## Slide 36: Browser
Implements HTTP (HyperText Transfer Protocol)
  Displays web pages
  Access authentication
  Caching, freshness control
Font mapping, e.g. Unicode
Compression, decompression
Handles multimedia, manages plug-ins
Interprets scripts
Executes Java applets
Maintains cache, history
Manipulates cookies

## Slide 37: Summary
Internet connects everyone
Makes eCommerce possible
Packet-switched, based on short packets
Survivable, expandable
No competing technology

## Slide 38
Q
A
&