## Slide 1: Introduction to Networking: Protocol Stacks
Peter Steenkiste
School of Computer Science
Carnegie Mellon University
http://www.cs.cmu.edu/~prs

## Slide 2: Outline
Protocol stacks.
Network technologies.
The Internet protocol.
Transport protocols.
Quality of service.
Networking research at Carnegie Mellon.

## Slide 3: Example: Web
User clicks on URL.
Web browser sends a message to the web server.
Server retrieves file specified in request and sends it as a message to the browser.
Browser interprets the file and displays it on the browser.
Simple.
Browser
Server

## Slide 4: But Many Things Happen Under the Covers
The browser and client have to speak a common language (protocol).
  E.g. the server must be able to understand the request
The network can lose packets, so the hosts must be able to recover lost packets.
  Requires another protocol
The network does not consist of a single network but of multiple diverse networks.
  Local area networks, ISPs, home access networks, …
Different networks must carry packets using very diverse technologies.
  Fiber, twisted pair, wireless, satellite, ...

## Slide 5: What Makes Networking Hard?
Application
Operating System
Network Interface
Computer
Links
Router Hardware
Router Software
(many protocols)
Bridge HW/SW
Application
Operating System
Computer
Network Interface

## Slide 6: A Layer Network Model
The Open Systems Interconnection (OSI) Model.
Application
Presentation
Session
Transport
Network
Data link
Physical
1
2
3
4
5
6
7
Network
Data link
Physical
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 7: OSI Functions
(1) Physical: transmission of a bit stream.
(2) Data link: flow control, framing, error detection.
(3) Network: switching and routing.
(4) Transport: reliable end to end delivery.
(5) Session: managing logical connections.
(6) Presentation: data transformations.
(7) Application: specific uses, e.g. mail, file transfer, telnet, network management.
Multiplexing takes place in multiple layers

## Slide 8: OSI Motivation
Each layer provides services to the layer above, using services provided by the layer below.
Each layer encapsulates/encodes/fragments data from the layer above.
Interoperability two ways:
  higher level protocols (e.g. TCP/IP, Appletalk) can run on multiple lower layers
  multiple higher level protocols can share a single physical network
Interfaces naturally creates independent modules.
  layers can be implemented and modified in isolation
  often not true in practice

## Slide 9: Example Revisited
Browser
Server
Data link
Data link
HTTP
Session
Session
Sockets
Transport
Transport
TCP
Network
Network
Network
Network
IP
Data link
Data link
Physical
Physical
Physical
Physical

## Slide 10: Limitations of the Layered Model
Some layers are not always cleanly separated.
  Inter-layer dependencies in implementations for performance reasons
  Some dependencies in the standards (header checksums)
Higher layers not always well defined.
  Session, presentation, application layers
Lower layers have “sublayers”.
  Sublayers well defined in the standards
Interfaces are not really standardized.
  It would be hard to mix and match layers from independent implementations
  Many cross-layer assumptions, e.g. buffer management

## Slide 11: The Internet Protocol Suite
Application
Presentation
Session
Transport
Network
Data link
Physical
UDP
TCP
Data Link
Physical
Applications
Presentation
Session
The Hourglass Model

## Slide 12: Relevant Standardization Bodies
ITU-TS (formerly CCITT) - Telecommunications Sector of the International Telecommunications Union.
  government representatives (PTTs/State Department)
  responsible for international “recommendations”
T1 - telecom committee reporting to American National Standards Institute.
  T1/ANSI formulate US positions
  interpret/adapt ITU standards for US use
  represents US in ISO
ISO - International Standards Organization.
  covers a broad range of topics

## Slide 13: More Bodies
IEEE - Institute of Electrical and Electronics Engineers.
  responsible for many LAN physical layer and datalink layer standards
IETF - Internet Engineering Task Force.
  standards for network layer and “higher”
  standardization based on working documents (Internet drafts) and proposed standards (Request for Comments)
  very “open” standards organization
ATM Forum.
  voting membership mostly manufacturers
  comparatively rapid evolution of recommendations

## Slide 14: Introduction to Networking: Network Technologies
Peter Steenkiste
School of Computer Science
Carnegie Mellon University
http://www.cs.cmu.edu/~prs

## Slide 15: Outline Network Technologies
Network architecture.
Core network technologies.
LANs.
Networks to the home.
Wireless.

## Slide 16: An Internetwork
Network
Network
Network
Network
Network
Network
Network
Network
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host

## Slide 17: Internet Service Providers
Provide Internet services to customers.
  Primary task is providing connectivity between networks
ISPs can provide service on multiple scales.
  Local: e.g. aggregate the traffic of smaller businesses
  Regional: next level of aggregation
  National and International
End-point travel may be handled by several ISPs on its way to its destination.
  Work its way up a hierarchy (local, …)
  Transfer between ISPs at the same level
    e.g. source ISP does not destination

## Slide 18: Access Networks
Support communication between hosts in the same local area or provide access path to the wide-area networks (ISPs).
  Administratively and technology-wise typically quite different from ISPs
Technology exploits the smaller physical distances and high concentration of hosts.
  Coordination is easier if propagation delays are low
  High concentration of hosts can simplify wiring and protocols
Access networks often combine a group of host that are part of the same organization.
  Impact on administration, security, charging policies, ..

## Slide 19: Network Access Points NAPs
Locations where major ISP connect their networks so they can easily exchange traffic.
  Equipment is often co-located
Often located in major metropolitan area so it can also provide network access to a large number of customers.
Administrative arrangements between ISPs are often bilateral in nature.
  ISPs A and B agree to support certain routes and certain amounts of traffic for each other
  Router set up has to match these agreements

## Slide 20: Core Network
Core networks are switch-based.
Switches are high-end routers.
  Connected by the “fattest” pipes that are technically feasible and commercially available
Links consist of single-mode optical fiber.
  Often use wavelength division multiplexing to send multiple channels (colors) over the fiber
  The rate of single channel matches the highest port speed of electronic switches (e.g. 622 Mbs, 2.4 Gbs)
Routing through the backbone is primarily driven by policies and not so much by efficiency.
  Business arrangements and other policies
  More on this later

## Slide 21: Router Architecture
Takes in packets in one interface and has to forward them to an output interface based on the address.
  A big intersection
  Same idea for bridges, switches, routers: address look up differs
Control processor manages the switch and executes higher level protocols.
  E.g. routing, management, ..
The switch fabric directs the traffic to the right output port.
The input and output ports deal with transmission and reception of packets.
Switch
Fabric
Input
Port
Output
Port
Output
Port
Input
Port
Output
Port
Input
Port
Output
Port
Input
Port
Control
Processor

## Slide 22: Access Networks
Local area networks (LAN).
  Broadcast based
  Switch based
Access from the home.
Wireless networks.

## Slide 23: Ethernet IEEE 802.3
Broadcast technology
Everybody “hears” the packet but only receiver accepts it.
  Except for broadcast and multicast packets
Carrier-sense multiple access with collision detection (CSMA/CD).
  Host sense for signal on cable before they transmit
  Hosts check for “collisions”, multiple packets that are on the wire at the same time
  In case of contention, hosts wait for random amount of time to (re)transmit
host
host
host
host
host
host
host
host
Hub

## Slide 24: Bridges and Switches
Bridge keeps track of the source address of every packet on every link.
  uses this information to learn what segment hosts are on
Forwards packets only on segment of destination host.
  Behaves like a switch
  Broadcast packets are still forwarded everywhere
  Increases aggregate bandwidth of the network.
Extreme case: one host per segment - Ethernet switch
host
host
host
host
host
host
host
host
host
host
host
host
Bridge

## Slide 25: IEEE 802 Networks: MAC in the LAN and MAN
Common addressing at MAC level
  Based on 48 bit IEEE addresses
802.3 (Ethernet)
802.5 (Token ring), FDDI.
  Token-based media access control
802.6 (Distributed queue dual bus).
  Reservation-based access control
ATM.
Fast Ethernet: 100 Mbit/second.
Gigabit Ethernet: 1000 Mbit/second.

## Slide 26: Why Ethernet?
Easy to manage.
  You plug in the host and it basically works
  No configuration at the datalink layer
Broadcast-based.
  In part explains the easy management
  Some of the LAN protocols (e.g. ARP) rely on broadcast
    Networking would be harder without ARP
  Not having natural broadcast capabilities adds a lot of complexity to a LAN
    Example: ATM
Drawbacks.
  Broadcast-based: limits bandwidth since each packets consumes the bandwidth of the entire network
  But Ethernet switches reduce impact of this problem

## Slide 27: Physical Layer in the LAN
Medium Transmit/receive Distance Comment
Copper 1000BASE-CX 25 m machine room use
Twisted pair 1000BASE-T 100 m not yet defined; cost?
Goal:4 pairs of UTP5
MM fiber 62 m 1000BASE-SX 260 m
1000BASE-LX 500 m
MM fiber 50 m 1000BASE-SX 525 m
1000BASE-LX 550 m
SM fiber 1000BASE-LX 5000 m
Twisted pair 100BASE-T 100 m 2p of UTP5/2-4p of UTP3
MM fiber 100BASE-SX 2000m

## Slide 28: Example LAN Configuration
Floor 3
Floor 1
Floor 2
Floor 4
10 or 100 Mbit/second connectivity to the desk top using switch or hubs in wiring closets.
100 or 1000 Mbit/second switch fabric between wiring closets or floors.
Management simplified by having wiring based on star topology with wiring closet in the center.
Network manager can manage capacity in two ways:
  speed of individual links
  hub/bridge/switch tradeoff

## Slide 29: Connectivity to the Home
Modems.
ISDN.
DSL.
Cable modem.

## Slide 30: Modems
Modem offers a bit stream.
  Aggressive signal processing has dramatically increased the available throughput - beats the Nyquist limit!
SLIP: Serial Line IP.
  Protocol to sent IP packets with minimum framing
  Lacks authentication, error detection, non-IP support, ..
PPP: Point-to-Point Packets.
  Better framing, error control, and testing support
  Can negotiate choice of higher layer protocols, IP address
  Can support unreliable and reliable transmission
Home
PC
Modem
Bank
Telephone
Network

## Slide 31: Integrated Services Digital Network (ISDN)
ISDN integrates voice and data services.
Provides a set of bit pipes that can be used for voice, data, signaling.
  Implemented by using time multiplexing
Basic rate ISDN offers to 64Kbs data bit pipes and one 16 Kbs signaling channel.
Home
PC
ISDN
Exchange
Telephone
Network
Public
Branch
Exchange
Phone
LAN

## Slide 32: Digital Subscriber Line
Squeeze more bandwidth out of the telephone line using advanced signal processing.
Asymmetric digital subscriber line (ADSL).
  More “download” bandwidth, e.g. video on demand or web surfing
  Example: T1 incoming path, 64 Kbs outgoing path
(Symmetric) digital subscriber line (DSL).
  Same bandwidth both ways, e.g. 768 Kbs
Home
PC
ADSL
Network
Unit
Telephone
Network
ADSL
Subscription
Unit
Phone

## Slide 33: Cable Modem
Use cable infrastructure for data service.
  Inherently has more bandwidth
The last mile is a shared infrastructure that was designed for broadcasting.
  Meaning: the bandwidth is shared by users
  Example: 27 Mbs shared incoming path; 768 Kbs common outgoing path
Fiber
Infrastructure

## Slide 34: Comparison
Modems use “worst case” technology.
  Has to fit within a voice channel so encoding suboptimal
ISDN can be more aggressive.
  But it is old technology by now
DSL is highly optimized for the transmission medium.
  Although there are some constraints on distance
Cablemodem uses a transmission medium that has inherently a higher bandwidth, but the network architecture will limit throughput.
  Designed for broadcasting, not for point-point connections

## Slide 35: Wireless Access Networks
Use a basestation that functions as an edge router in the wired infrastructure.
IEEE 802.11 wireless networks.
  Are becoming very popular in LANs
Cellular digital packet data (CDPD).
  Shares spectrum with cellular telephone network
  Datagrams are sent over idle channels
  Speeds of 10s of Kbit/second of shared bandwidth
Low-altitude satellites.
  Only at ~750 km, in circular (polar) orbit
  Can be viewed a cellular with cells moving
  Eg, www.iridium.com, www.teledesic.com

## Slide 36: Cells
A cell corresponds to the area covered by a “base station”.
Limiting the power avoids interference between cells.
  Frequency reuse
Use of different frequencies between adjacent cells can reduce interference.
Performance typically drops if there are too many users in the cell.
  Limited number of channels
Mobile users require support for handoff.

## Slide 37: Wireless LANs: 802.11
Basically wireless Ethernet in each cell.
  Sender cannot detect collision, so collision avoidance only
  Positive ack after correct reception
Communication goes through a basestation.
  Connected to the wired network
Also supports other operating modes, e.g. point coordination function.
  Basestation controls the bandwidth
  Can send to specific stations and invite a station to transmit
  Contention period for new stations to request bandwidth
Cells rarely cleanly separated.
  Transmitter consumes bandwidth in multiple cells
  11 frequencies helps management

## Slide 38: Mobility Support
Basestations periodically invite new stations to join them.
Mobile stations listen for invite messages and basestations and select one.
  Typically based on signal strength
  Has to be willing to leave old station, but avoid quick changes

## Slide 39: Introduction to Networking: The Internet Protocol - IP
Peter Steenkiste
School of Computer Science
Carnegie Mellon University
http://www.cs.cmu.edu/~prs

## Slide 40: Outline
The Internet.
IP addressing.
Routing.
Domain Name System.
The Internet protocol.
IPv6.

## Slide 41: Internetworking
Ethernet
Packets
over SONET
ATM
ATM
Mixed
Ethernet
Mixed
Ethernet
FDDI
802.x
Host
Host
Host
Host
Host
Host

## Slide 42: Internetworking Issues
Naming and addressing.
  how to structure the name and address space
Packet forwarding and routing.
  given a packet with an address, how do we get there
Fragmentation.
  traversing networks with different maximum packet sizes
Control.
  coordinating IP-level activities in different networks

## Slide 43: Traditional Addressing in IP v4
Each host has an internet address.
  Example: 128.2.209.19
Addresses are hierarchical.
  address contains hint about location
Original design: 4 classes of subnets.
IP address space used to be assigned by the Internet Assigned Numbers Authority (IANA).
  See http://www.iana.org
type
network
host
A 0 7 24
B 10 14 16
C 110 21 8
D 1110 28

## Slide 44: Motivation for Address Structure
Hierarchical structure gives a hint about the location that can be used to simplify routing.
  Compare with postal addresses
  But what happens when your machine moves?
Can assign subnet address spaces that are appropriate for the size of the organizations.
  A small number of large spaces
  Many smaller spaces
  But what happens when your organization grows?
Class D corresponds to multicast.
  Flat address structure

## Slide 45: IP Addressing: Problems
IANA was running out of class C addresses.
  Class-based addressing does not use space efficiently
Routing tables in the network core grow too fast as a result of the success of the Internet.
  Too many networks!
Running out of IP address space: too many hosts.
  32-bit address is not sufficient on the long run
Combination of solutions:
  Classless Inter-Domain Routing (CIDR)
  Dynamic address assignment
  Network Address translation (NAT)
  IPv6 with 128 bit address

## Slide 46: Short-term Solutions to Address Space Crunch
Dynamic assignment of IP addresses.
  Assign an IP address for duration that it is needed only
  Example: dial up connections
  Is supported by the Dynamic Host Configuration Protocol (DHCP)
Use of private address spaces.
  Many large organizations have hosts that do not need direct access to the network
    Only talk to other host in the organization, or
    Can use application level gateways to talk to hosts outside of the organization
  IANA set aside blocks of address space for use inside such organizations
  Uses Network Address Translation (NAT) boxes (later)

## Slide 47: Classless Inter-Domain Routing (CIDR)
Use address space more efficiently by relaxing the strict address structure.
  length of network address is variable
  Size of network can be made to fit size of organization
Have internet service providers hand out blocks of addresses to their customers.
  Reduces the size of the address tables
There are many exceptions to CIDR.
  Existing organizations, organizations with multiple ISPs, …
  But overall it has been very successful

## Slide 48: What Does Routing Do?
Routing protocol specifies how routers jointly collect information about the network.
  Routing protocols must be standardized
Routing algorithm uses network information to select appropriate routes and to set up the routing table.
The data forwarding engine performs route lookup in the routing table.
  through which interface should a packet be forwarded?
Route
Lookup
Routing
Protocol
Routing
Algorithms
Routing protocol
Other routers

## Slide 49: Packet Forwarding based on Network Identifier
AN 2
ISP 2
ISP 1
ISP 3
AN 4
AN 1
AN 5
AN 3
Host
Host
Host
Host
Host
Host
Net.Host
Net ID
Net ID
Net ID
Net ID
Next
Next
Next
Next
Forwarding Table

## Slide 50: Routing Requirements
Scales to large numbers of nodes.
  asymptotic properties matter
Robust in the presence of failures.
  Centralized algorithms unacceptable because they form a single point of failure
  small errors should not result in disasters
Adapts to changes in the network.
  link or node errors
  load sensitive routing
Selects high quality paths.
  Small number of hops, low load, ..

## Slide 51: Taxonomy
Static versus adaptive (load sensitive).
  Does the route depend only on static topology information or also on the load conditions
Hop-by-hop versus source routing.
  Routers determined one hop at a time or preplanned
Precomputed versus on demand.
  Routes are looked up in a precomputed table or are calculated for each packet/connection request
Centralized versus distributed.
  Where are how are routing decisions made
Link state versus distance vector.
  Two commonly used routing mechanisms

## Slide 52: Dykstra’s Shortest Path Algorithm
F
A
D
E
C
3
2
2
5
3
4
4
3
1
2
B
2, F
3, F
5, E
6, E
3, F
6, E
5, E
3, F
5, E
6, E
6, B
6, B
6, E
6, B
2, F

## Slide 53: Link State Routing
Each node collects information about the network topology and link costs.
  Nodes periodically sends information about its immediate topology to all other nodes using flooding
    information includes neighbors and link costs
  a time-to-live field is used to expire old information
Nodes execute Dijkstra’s algorithm locally.
  Build local forwarding table
Amount of state information limits scalability.
  The entire network topology is broadcasted over the network
  Each node has to store the entire network topology

## Slide 54: Flooding Algorithm
The goal is to distribute information without knowing the topology.
  Important for routing information
The node sends the packet to all its neighbors.
Each node drops incoming packets that are old or duplicate.
  Requires sequence numbers
New incoming packets are forwarded on all outgoing links, other than the one the packet came in on.

## Slide 55: Distance Vector Routing
Each node knows its neighbors and the cost of getting to the neighbors.
Each node keeps a routing table
  destination + cost + outgoing link
Each node sends the (destination + cost) vector to its neighbor.
  incoming updates are used to execute one iteration of Dijkstra’s algorithm (Bellman-Ford algorithm)
  note that cost can sometimes increase: have to accept the higher cost from nodes that are on shortest path
When are updates sent?
  whenever information changes: fast propagation
  periodically: provides robustness against node failure

## Slide 56: Common Properties
Distributed algorithms.
  can survive node failure
  (lack of) reachability information continues to propagate
  but can result in temporary problems (e.g. routing loops)
Mechanisms to eliminate old information.
  increases stability
  reduces life time of errors
Redundancy.
  makes the system more robust
“Soft” state.
  state that is periodically updated
  can survive node failures
    after a short interruption of service

## Slide 57: Hierarchical Routing
Two level routing based on intra-domain and inter-domain routing to improve scalability.
Matches the structure of the address space (next lecture).
Driven in part by business/management concerns.
  Local network information is kept internal
  Agreements with specific service providers at boundaries
Host
Host
Host
Host
Host
Host

## Slide 58: Intra- versus Inter-domain Routing
Only concerns itself with routing inside the autonomous system.
  Between two hosts in the AS
  Between host and boundary router
  Between two boundary routers
Does not know about the structure of the world outside the AS.
  Boundary routers represent the connectivity to the outside world
Only concerns itself with routing between boundary routers.
  Oblivious to the internal structure of the networks
Inter-router links can be physical or virtual.
  Physical = single link
  Virtual = path consisting of sequence of links
Relies on intra-domain routing for packet transport between boundary routers.
  For virtual links
Intra-domain
Inter-domain

## Slide 59: Examples
Routing Information Protocol (RIP).
  shortest-hop distance vector protocol for networks
  intradomain protocol
Open Shortest Path First (OSPF).
  authentication, load balancing, multiple levels
  intra-domain protocol
Border Gateway Protocol (BGP).
  advertises complete paths
  inter-domain protocol
ATM PNNI protocol: multi-level hierarchical link state routing.
  load sensitive

## Slide 60: Multicast
Packets sent by a sender are received by more than one receiver.
  Network replicates the packet
  Limits the communication overhead on the sender, making it possible to send to a large number of receivers
  Potentially reduces bandwidth consumption in the network
Many issues/challenges.
  How (receiver) multicast group membership managed?
  How do we route packets?
  How do routers forward multicast packets?

## Slide 61: Multicast Routing
“Union” of point-to-point paths.
  combine message over shared links
Optimizations possible but difficult if the receivers are not known.
  model used in internet
R
R
R
R
R
R
R
R
S

## Slide 62: Group Management
Management strategy depends on usage.
  how quickly does membership change?
  restrictions on membership
  size of the group
Internet: focus on large groups that can change rapidly and with little control over membership.
  distributed algorithm (scalability, again)
  receiver-initiated management (scalability, again)
  sender does not have list of receivers (scalability, again)
Internet Group Management Protocol (IGMP).
  Routers jointly keep track of membership
  Relies on multicast (e.g. Ethernet) in leaf networks
  Protocol defines how receivers contact routers to join a group

## Slide 63: Hop-by-Hop Packet Forwarding in the Internet
Ethernet
WAN
Mixed
Ethernet
Host
Host
7
..
3
2
1
Route lookup
returns
next hop IP address
Route lookup
returns
outgoing interface

## Slide 64: Translation
Name -> (IP) destination address
  name look up: cache + server
Destination address -> next hop address
  look up in routing table
IP address -> physical address
  address resolution protocol (ARP)
Criteria
  scalability: should work for large networks
  correctness: the right answer in a dynamic environment
  robustness: can survive failures
  performance: caching

## Slide 65: Domain Name System
Translate “names” into IP addresses.
  Also: adding new names, changing the name-address mapping, delete names, supporting short cuts, and security
  Main challenge is scale: large number of hosts
DNS uses a hierarchical naming scheme:
  hawaii.cmcl.cs.cmu.edu
Main idea: a separate authority for the name y.z... manages the name space x.y.z...
  The CMCL lab manages x.cmcl.cs.cmu.edu
  Computer science manages x.cs.cmu.edu
  CMU manages x.cmu.edu
Naming authority is distributed.
  Example: InterNIC for .com, ...

## Slide 66: DNS Server
A DNS server is responsible for maintaining the name-address mapping in a specific domain.
  E.g. cs.cmu.edu
The network manager can add, remove, or change mappings.
Computers can send requests to the server to translate a name into an address.
  But how do you find the server?
  Recursively contact the parent in the hierarchical name space
Caching is used to speed up the lookup of frequently used names.
cs.cmu.edu
hawaii.cs.cmu.edu
Other DNS servers
128.17.4.174

## Slide 67: Name Lookup Example Recursive Queries
a.cs.cmu.edu
cs.cmu.edu
Root server
ucb.edu
cs.ucb.edu
c.cs.ucb.edu
c.cs.ucb.edu

## Slide 68: ARP: Address Resolution Protocol
Discover physical address given an internet address.
Broadcast request to nodes on local network.
  destination will respond with MACaddress
  destination saves internet + physical address of requesting node
Each node keeps cache to limit overhead.
  time out old entries
Non-broadcast LANs often use ARP server.
  NBMA ARP (NARP) for non-broadcast, multi-access networks
B
C
A
a
b
c

## Slide 69: IPv4 Protocol Functions
Highest layer that is not end to end.
Connectionless best-effort packet delivery.
Header shows what functions are provided.
V/HL
TOS
Length
ID
Flags/Offset
TTL
Prot.
H. Checksum
Source IP address
Destination IP address
Options..

## Slide 70: Multiplexing and Demultiplexing
Protocol field specifies which transport protocol (layer 4) should interpret the packet.
  Protocol identifiers are controlled by IANA
This form of multiplexing and demultiplexing happens at each layer.
  Logical Link Control (LLC) header in datalink layer (layer 2)
IP
TCP
IP
TCP

## Slide 71: Time to live
Goal: drop packets that are stuck in an infinite loop in the network.
  Can happen because of route inconsistencies
Decrement TTL field in each hop and drop packet if it reaches 0.
  field is initialized by sender
  the router that drops the packet notifies the sender
Used as basis for trace tools.
  send sequence of packets with TTL set to 1, 2, 3, .. until the destination is reached
  sequence of ICMP replies identifies current route

## Slide 72: Fragmentation
Different networks have a different maximum transfer unit (MTU).
A problem can occur if packet is routed onto network with a smaller MTU.
  e.g. FDDI (4500B) onto Ethernet (1500B)
Solution: break packet into smaller fragments.
  each fragment has identifier and sequence number
Destination reassembles packet before handing it up in the stack.
  alternative would be to reassemble when entering network with larger MTU
Sender can disable fragmentation using flag.

## Slide 73: Fragmentation Example
Header
Data
Header
Data
Data
Data
Header
Header
Offset
Identifier
Flags

## Slide 74: ICMP
IP Header
Internet Control Message Protocol.
Report errors to sender.
  redirect
  expired packets
  fragmentation problems
Also used as the basis for tracing and information retrieval.
Type
Code
Checksum
ICMP Data

## Slide 75: IP v6
“Next generation” IP.
Most urgent issue: increasing address space.
  128 bit addresses
Simplified header for faster processing.
Many other changes.
Support for guaranteed services: priority and flow id
Options handled as “next header”
  reduces overhead of handling options
V/Pr
Flow label
Length
Next
Hop L
Source IP address
Destination IP address

## Slide 76: IPv6 Addressing
128 bit addresses with complex structure.
Examples: format for local configuration, geographical addressing, IPv4 backwards compatible, ..
Provider-based unicast addressing extends the format used in IPv4 with CIDR.
Registry
010
Provider
Host
Sub
Net
Subscriber

## Slide 77: Migration from IPv4 to IPv6
Interoperability with IP v4 is necessary for gradual deployment.
Two mechanisms:
  dual stack operation: IP v6 nodes support both address types
  tunneling: tunnel IP v6 packets through IP v4 clouds
Unfortunately there is little motivation for any one organization to move to IP v6.
  the challenge is the existing hosts (using IPv4 addresses)
  little benefit unless one can consistently use IPv6
    can no longer talk to IPv4 nodes
  stretching address space through address translation seems to work reasonably well

## Slide 78: Some Tools
Ping: check whether a host exists and measure the roundtrip time.
  Floodping: send as fast as you can - not very friendly
Traceroute: find the path to a host.
  Based on ICMP, as described earlier
Pathchar: more recent tool that tries to measure the bandwidth of each link on the path to a host.
  Beats on the network pretty heavily
nslookup: uses DNS to find IP address of host.