## Slide 1: Introduction to Networking: Transport protocols
Peter Steenkiste
School of Computer Science
Carnegie Mellon University
http://www.cs.cmu.edu/~prs

## Slide 2: Outline
Transport protocols.
UDP.
TCP.

## Slide 3: Transport protocols
Lowest level end-to-end protocol.
  Header generated by sender is interpreted only by the destination
Wide range of functions:
  Multiplexing/ demultiplexing for multiple applications
  Connection establishment
  Various types of error control
  End-to-end flow control
  Congestion control
7
6
5
7
6
5
Transport
IP
Datalink
Physical
Transport
IP
Datalink
Physical
IP
router
2
2
1
1

## Slide 4: User Datagram Protocol
Addressing used for (de)multiplexing.
  port numbers = connection/application endpoint
End-end reliability through optional end-to-end checksum.
  protects against any data corruption errors between source and destination (links, switches/routers, bus)
  does not protect against packet loss, duplication or reordering
  checksum is very simple
Source Port
Dest. Port
Length
D. Checksum

## Slide 5: Using UDP
Non-standard protocols can be implemented on top of UDP.
  Non-standard = non-TCP in practice
  use the addressing provided by UDP
  implement their own reliability, flow control, ordering, congestion control
Examples:
  remote procedure calls
  multimedia
  distributed computing communication libraries
  look at some examples later

## Slide 6: Transmission Control Protocol
Service: fully reliable byte stream.
Connection establishment and tear down.
Sequence numbers.
Reliability.
End-end flow control.
Congestion avoidance.
TCP extensions
Source Port
Dest. Port
Sequence Number
Acknowledgment
HL/Flags
Window
D. Checksum
Urgent Pointer
Options..

## Slide 7: High-Level TCP Characteristics
Connection-oriented reliable byte-stream protocol.
  Used for file transfers, telnet, web access, ….
Two way connections.
  control information for one direction piggy-backed on data flow in other direction
  header fields fall in three classes: general, forward flow, opposite flow
Protocol has evolved over time and will continue to do so.
  uses options to change the protocol
  backward compatibility is what makes it TCP

## Slide 8: Connection management
Time
Open
Data
Close
Sender
Receiver
syn
syn/ack
ack
fin
ack
fin
ack
Establish
Initial
Sequence
Numbers

## Slide 9: Sequence Number Space
Each byte in byte stream is numbered.
  32 bit value
  wraps around
  initial values selected at start up time
Each packet has a sequence number.
  indicates where it fits in the byte stream
Detects lost, duplicate or out of order packets.
  Recovers to offer reliable in-order byte streaming
packet 8
packet 9
packet 10
packet 11

## Slide 10: Reliability
Checksum guarantees end-end data integrity.
Sequence numbers detect packet sequencing problems:
  duplicate: ignore
  reordered: reorder or drop
  lost: retransmit
Lost packets detected by sender.
  uses time out to detect lack of acknowledgment
  requires reliable roundtrip time estimate
Retransmission requires that sender keeps copy of the data until ack is received.
  performance issue

## Slide 11: When to Send a Packet?
End-to-end flow control.
  avoid buffer overflow on receiver
  receiver advertizes a window size
Congestion control.
  estimates amount of data that can be in network
  implemented using the congestion window, slow start, and fast retransmit/recovery mechanisms
Efficiency considerations.
  try to send large packets (if possible)
    more efficient in the network and on end points
  piggybacking of acks

## Slide 12: End-to-End Flow Control
Receiver advertises how much data it can receive.
  backed up with real buffer space
  point in sequence space
Acknowledgement indicates that data was received correctly.
  sender can delete copy of message
  but data still consumes buffer space on receiver
Window update indicates that data was consumed and that buffer space was freed up.
  sender can send more data
acknowledged
sent
to be sent
outside window

## Slide 13: Window Size versus Throughput
Sender
Receiver
Time
Throughput =
Window Size
Roundtrip Time
RTT

## Slide 14: Congestion
Congestion: the load placed on the network is higher than the capacity of the network.
  Behavior on short time scales (a few roundtrip times)
Increased load can result in lower throughput, large delays.
  multihop nets: heavy traffic  long queues  lost packets, retransmits
  Ethernet: high demand  many collisions
  compare with highways: too much traffic slows down throughput
Load
Throughput

## Slide 15: TCP Congestion Avoidance
Congestion avoidance limits how fast TCP can send data.
  Implemented using a congestion window that limits how much data can be in the network
    independent from flow control window
  transmission is limited by minimum of the two windows
  window grows in response to acknowledgement
Packet loss is seen as sign of congestion.
  multiplicative decrease of the congestion window
  have to cut back fast since cost of congestion is high
How do you detect when more bandwidth becomes available?
  gradually increment congestion window (probing)
  results in oscillation around congestion window size!

## Slide 16: Adaptation with Binary Feedback
Network stability requires multiplicative decreases and additive increases in the transmission rate.
Congestion is a dangerous condition -> back off quickly
Unused bandwidth is undesirable but not dangerous -> probe carefully
Time
Rate

## Slide 17: TCP Fairness Issues
Multiple TCP flows sharing the same bottleneck link do not necessarily get the same bandwidth.
  Factors such as roundtrip time, small differences in timeouts, and start time, … affect how bandwidth is shared
  The bandwidth ratio typically does stabilize
Modifying the congestion control implementation changes the aggressiveness of TCP and will change how much bandwidth a source gets.
  Affects “fairness” relative to other flows
  Changing timeouts, dropping or adding features, ..
Users can grab more bandwidth by using parallel flows.
  Each flow gets a share of the bandwidth to the user gets more bandwidth than users who use only a single flow

## Slide 18: Other Transport Protocols
Some applications need a form of reliability, congestion avoidance, or flow control different from that of TCP.
  May not need a 100% reliable transport
  Timeouts or slow down for congestion avoidance may introduce unacceptable delays
Other transport protocols are often implemented in user space on top of UDP.
  Use the addressing provided by UDP
Examples: Multimedia.

## Slide 19: Playback of Audio/Video
Source attaches a timestamp to each sample.
Receiver uses the timestamp to playback the sample at the right time.
The playback point corresponds to the delay in the replay relative to the generation of the data.
  Packets that arrive too late have no value and are ignored
  Packets that arrive too early have to be buffered
Source
Playback

## Slide 20: Transport Protocol Properties
Reliability.
  Some lost data is typically acceptable (impact depends on the type of encodingencoding)
  Timeouts typically result in unacceptable delay, and there is often not enough time to retransmit data (live transfers)
Congestion control.
  Nature of the flow fundamentally limits its bandwidth
  reduction of rate in response to congestion should not be done by sending samples slower but by reduce data size
    E.g. change frame rate or frame size
Flow control.
  Samples should be paced at the natural rate of the data
  Sending too slow --> underflow and missed deadlines
  Sending too fast --> buffer overflow and lost data

## Slide 21: Adaptive Video Streaming
Source
Playback
Feedback
Receiver reports dropped packets.
Sender reduces frame size if loss rate is too high.
  Also uses probing to detect additional bandwidth
Similar to TCP, except that lost data is typically not retransmitted.

## Slide 22: Real-Time Transport Protocol RTP (RFC 1889)
Supports the transport of data with real-time characteristics.
Provides the formatting and synchronization information for the data transfer.
  Data encoding used, timestamps for synchronization, loss rates for used by congestion control protocol, sequence numbers for ordering, ...
RTP does not guarantee timely data delivery.
  guarantees have to be provided by lower level protocols
The protocol has two parts.
  Real-time Transport Protocol: carry data
  Real-Time Control protocol: monitor quality, exchange information about participants, ..

## Slide 23: Introduction to Networking: Quality of Service
Peter Steenkiste
School of Computer Science
Carnegie Mellon University
http://www.cs.cmu.edu/~prs

## Slide 24: Outline
What is quality of service?
How do you provide it?
Two Internet proposals: IntServ and DiffServ
Practical issues.

## Slide 25: What is QoS? An Application View
Current Internet supports best effort packet delivery only.
  sufficient for most applications
  but some applications require or can benefit from a “higher” level of service
“Higher” quality of service typically means that bounds are provided for one or more performance parameters.
  Bandwidth: fast data transfers, video
  Delay, jitter: telephony
  Packet loss, bit error rate: update services

## Slide 26: What is QoS? A Network Manager View
Link sharing: multiple organizations share a link.
  each pays for certain % and expects service accordingly
Service providers want to offer different types of services to different users.
  Gold, silver, bronze
Managers want to place limits on how much bandwidth is used by certain traffic classes.
  Distribute bandwidth over Web, video, audio, ...
Link
CMU
Pitt

## Slide 27: QoS Analogy: Surface Mail
The defaults if “first class mail”.
  Usually gets there within a few days
  Sufficient for most letters
Many “guaranteed” mail delivery services: next day, 2-day delivery, next day am, …..
  Provide more faster and more predictable service at a higher cost
  Providers differentiate their services: target specific markets with specific requirements and budgets
Why don’t we do the same thing in networks?

## Slide 28: QoS Requirements and Challenges
Good technical solutions.
  Can offer appropriate types of guarantees (complexity)
  Scale to large numbers of flows and users
What are the usage models for networks with QoS guarantees.
  How do we develop applications for such networks?
  How can we get (uneducated) users to use such networks appropriately?
Define appropriate business models that make economic sense.
  What will a contract for network services with QoS look like and will anybody sign it?
  Does it match the technology solutions?

## Slide 29: How to Provide QoS?
Admission control limits number of users.
  You cannot provide guarantees if there are too many users sharing the same set of resources (bandwidth)
  For example, telephone networks - busy tone
  This implies that your request for service can be rejected
Traffic enforcement limits how much traffic users can inject based on predefined limits.
  Make sure user respects the traffic contract
  Data outside of contract can be dropped (before entering the network!) or can be sent at a lower priority
Scheduling support in the routers guarantee that users get their share of the bandwidth.
  Again based on pre-negotiated bounds

## Slide 30: QoS Framework
G
H
F
E
C
B
J
I
H
Admission
Control
A
D
Traffic
Enforcement
Packet
Scheduling

## Slide 31: QOS Admission Control
Client submits request.
  description of traffic source
  service requested from network
  can include desirable and acceptable levels of service
Traffic descriptors.
  Specifies a traffic service class
  set of parameters describing service or traffic
Network checks whether the request can be satisfied and accepts or rejects the request.
  May have to check with the routers in the network
  May have to reserve resource on every router along the path that was selected for the flow
    using a signaling protocol

## Slide 32: How Do We Distinguish Between Flows?
For every packet we must be able to determine what flow (or user) it belongs to.
  First step towards giving it appropriate service
Packet classifier takes as input the packet header and generates a flow identifier.
  The classifier has to be initialized, for example as part of admissions control
Packet
Classifier
Flow Identifier
Source, destination
IP addresses,
netmasks, and ports
protocol identifier

## Slide 33: Weighted Fair Queueing WFQ
Distributed bandwidth to flows according to some agreed upon distribution.
  Routers are given a set of weights during signaling
WFQ can support bandwidth reservations.
  Adjust the weights so that guaranteed flows get their bandwidth
  Other flows share bandwidth according to some sharing formula (e.g. equally)
  Weights have to be adjusted when flows leave and enter
10
15
25
10
10
10
10
10
8.33
8.33
8.33
8.33
8.33
8.33

## Slide 34: Enforcement - Example
We have to limit the traffic that each user can inject in the network.
  Has to stay within agreed upon bounds
How do we do this for bursty traffic.
  Averaging interval is important: seconds, hours, …
Token bucket supports enforcement for bursty traffic: limits a long term average rate and a burst rate.
rate r
size b

## Slide 35: A Short History of Internet QoS
Lots of initial research in the late 80s and early 90s.
  Often takes a telecommunications view of the network
ATM QoS and Integrated services were developed based on these results.
  Focus still on per-flow, hard QoS
In the last 5 years, the focus has shifted to differentiated services.
  Focus is on QoS for flow aggregates, e.g. all the flows belonging to one customer
  The immediate user is really the network manager

## Slide 36: Service Model of a Network
Set of services supported by that network.
  Provide a coherent offering that satisfies a wide range of users
Multiple types of services.
  mathematical guarantees
  predictive services
  best effort
Examples:
  ATM: constant bit rate, variable bit rate, unreliable bit rate, available bit rate
  IETF Integrated services (IntServ): best effort, controlled load, guaranteed service
  IETF Differentiated services (DiffServ): defines set of mechanisms, not services

## Slide 37: IETF IntServ
Focus on per-flow QoS.
  Support specific applications such as video streaming
  Based on mathematical guarantees
Many concerns.
  Complexity?
  Scalability?
  Business model?
  Charging?
Link Sharing
Guaranteed
Best Effort
BW, delay
Guarantee
Controlled
Load
Fair Share
Traditional

## Slide 38: Charging for Network Service
Flat charge: you pay a flat fee, independent from usage.
  Garbage pick up (?)
Usage charging: you pay for what you use.
  Water, electricity, ...
Practice: you pay for the thickness of the pipe.
  Is equal to potential use or peak use
  Also needed: bilateral agreements between ISPs to deal with cross ISP traffic
A lot of the early work on QoS would require usage based charging, if deployed.
  E.g., pay on a per connection basis
  Concerns for increased complexity and cost

## Slide 39: Differentiated Services: Motivation and Design
Do fine grain enforcement only at the edge of the network.
  Typically slower links at edge
  E.g. mail sorting in post offices
Label packets with a type field.
  E.g. a priority stamp
The core of the network uses only the type field for QoS management.
  Small number of types with well defined behavior
  Can be handled fast
Example: expedited service versus best effort.
Evolution rather than revolution.
Traffic
metering
and shaping

## Slide 40: DiffServ Charging Models Examples
Customer buys into a specific class.
  Bronze, gold, silver
Customer gets service in a number of classes and sorts traffic according to priority.
  IP telephony and president get expedited service
  Others get best effort
  Sorting is based on classification
Add a “speed up” button to the browser.
  Impatient users can switch to a higher class (as a higher cost)
  Finest grain user control
A
B
C
D

## Slide 41: Resource Reservation Protocol (RSVP)
Signaling protocol that establishes connections in the Internet.
  IntServ, DiffServ
Main goal: establish “state” in each of the routers so they “know” how they should treat flows.
  State = packet classifier parameters, bandwidth reservation, ..
  Uses periodic refresh to deal with failures and recovery
  Based on receiver initiated operation (like multicast)
A
B
C
D

## Slide 42: Policy Issues
Any QoS solution must include mechanisms for implementing a range of policies.
  Who gets to use what services?
  ISP: payment drives service
  In other environment, administrative policies are needed
One components is to use a directory service for policy management.
  Managers can enter policies
  Network entities can retrieve the policies they need
Policy
Manager
Network

## Slide 43: Common Open Policy Service (COPS) Protocol
Routers have a “Policy Enforcement Point”.
  Is responsible for enforcing policies when a request for resources is handled
  Example: RSVP router performing policy based admission control
COPS defines the interaction between the PEP and the policy server.
  PEP issues policy request through an RPC
  Interaction is based on long-term session that can have state at both ends
    asynchronous streaming of information to PEP
    caching information on the PEP
Policy
Server
Data
Forwarding
RSVP
PEP

## Slide 44: Introduction to Networking Networking Research at CMU Peter Steenkiste School of Computer Science Carnegie Mellon University http://www.cs.cmu.edu/~prs

## Slide 45: Outline
Network quality of service.
  Darwin: customizable network quality of service
  Libra: scalable electronic services
Network traffic reporting.
Wireless, mobile, and ad hoc networking.
  Monarch: mobile and ad hoc networking
  Bandwidth management on wireless links
  Wireless Andrew
High performance networking.
  Gigabit Nectar and Credit Net
  Next Generation Internet.

## Slide 46: Networking Faculty
David Johnson - Monarch.
  Mobile IP for IP v4 and v6
  routing protocols for ad hoc networks
Hui Zhang.
  Hierarchical scheduling and core-stateless QoS
  multicast research
  video distribution
Peter Steenkiste.
  High performance networking
  Application-oriented QoS
  Network monitoring
  Wireless bandwidth management

## Slide 47: Motivation
Implement interface that supports both monitoring and adaptation of network resources.
Network reports on expected performance so services can adapt pro-actively.
  Reduce or increase bandwidth, move to different cell
  Leverage the Remos Quorum project
Control the network resources to deliver the performance the services need.
  Selective use of reservations can improve predictability
  Leverage the Darwin Quorum project

## Slide 48: Darwin Motivation: Applications versus Networks
Enhanced
Video
Conferencing
Emergency
Response
Video
Conferencing
Process
Optimization
Distributed
Simulation
Internet
Embedded
environment
Enterprise
network
A
B
e
d
F
C
E
D
Archival
Storage
G
Compute
Servers
a
b
c
Applications want
predictable high quality
service, where quality
is an application and
user-specific concept
The network is
a set of diverse
generic resources
that is shared by
competing and
cooperating users

## Slide 49: An Architecture for User-oriented QoS
Distance
Learning
User
User
Schedulers guarantee
network properties
for traffic flows
Delegates manage
the user’s network
resources at runtime
Resource Brokers
perform global
resource allocation
on behalf of the user
Resource
Broker
Resource
Broker

## Slide 50: Resource Brokers Perform Global Resource Allocation
Map high-level user request onto a set of resources using domain knowledge.
  Request includes cost constraints and QoS metrics
  E.g. 1.5 Mbs for MPEG-1 video
  Generate alternate mappings, e.g. use compression or not
Optimize quality of service or cost.
  Select “the best” mapping option
  Tradeoffs across resource types
  Negotiate with user about options
Domain
Knowledge
Optimization
High-level
User
Request
Low-level
Resource
Specification
Global
Resource
Information
Resource
Discovery

## Slide 51: What is (Application-level) Network Quality of Service?
Application-level QoS is inherently a vague concept.
  What is the quality of service of a distance learning application?
  Service and user specific
If we want to optimize QoS automatically, we must be able to quantify QoS.
Frame Rate > 20
Frame Size > 60K
Response Time < 300
Cost < 8
QoS = (3 x FR + 1/RT)
Bandwidth?
?
?
?
?
Application QoS is
1- Minimum acceptable service level specified as a set of constraints that must be met
2- QoS expression to be maximized - or cost function to be minimized

## Slide 52: Darwin Hierarchical Scheduling
Scheduling must supports efficient, customizable, hierarchical resource sharing.
  efficient = controlled dynamic sharing, besides hard guarantees
  customizable = many policies
  hierarchical = flows + flow aggregates
Divide and conquer.
  independent traffic management policy control in each subtree
  dynamic control over who gets excess bandwidth
Hierarchical Fair Service Curve (H-FSC) algorithm supports wide range of sharing policies.
155 Mbps
40 Mbps
60 Mbps
10 Mbps
30 Mbps
100 Mbps
55 Mbps
Controlled
Load Service
Value Added Service Provider 1
Distributed
Simulation
seminar
video
ECE
U.Pitt
WEB
Video
Audio
Control
Bitway Provider
Campus
seminar
audio
CMU
Guaranteed
Service
Value Added Service Provider 2
SCS
Best-effort
Service
FTP
Telnet

## Slide 53: Base-line Case: No Hierarchy
Audio/Video
FFT
File Transfer
Adversary (UDP)
10 Mbps
1 Mbps
3 Mbps
1Mbps
5 Mbps
Link
Separate reservations.
A/V guarantee met
FTP throughput
  1.7 Mbps
FFT finish time
  29 second
UDP
A/V
FTP
FFT
Router 1
Router 2
Router 3

## Slide 54: Link-sharing at Root Node

## Slide 55: Test Case: Two Levels of Resource Hierarchy
10 Mbps
1 Mbps
3 Mbps
1Mbps
5 Mbps
7 Mbps
Audio/Video
File Transfer
Adversary (UDP)
FFT
Link
Same amount of total resource reserved
A/V guarantee met
FTP throughput
  4 Mbps
  factor of 2.4 improvement
FFT finish time
  27 second
  slightly faster
FFT
TCP
29 sec
1.7 Mbs
Flat
27 sec
4 Mbs
Hier
A/V
FTP
FFT
UDP
Mesh
Router 1
Router 2
Router 3

## Slide 56: Link-sharing at Root Node

## Slide 57: Link-sharing at Interior Application Node

## Slide 58: Delegates Manage Resources at Runtime on Behalf of the User
Motivation: service quality is sensitive to how resources are managed at runtime.
Code insertion is a very flexible method of adding “domain expertise” to the network.
  Set of parameters is too restrictive and too static
  “Applets in reverse”: user extends network functionality
Executing delegates on the router results in fast response times.
  Immediate access to relevant information
  Eliminate roundtrip delay to endpoints
  Active networking in the control path

## Slide 59: Delegate Implementation
Delegates implemented as Java code segments.
  RCI implemented as native class
  Supported for NetBSD and FreeBSD routers, Cairn
  Beagle installs delegates and verifies execution requirements and authorization
Clean programming model.
  Delegates are associated with nodes in the resource tree
  Scheduler: isolation in data plane
  Delegates: isolation of control
Safety considerations.
  Rely on Java sandboxing
  Use of PCC with Fox project
Delegate
Execution Env.
Hierarchical
Resource Tree
Link
Pitt
CMU
App 1
Flow 1

## Slide 60: Control/Data Delegate Coordination
Control delegate manages the level of compression in a transcoder that is deployed as a data delegate.
  JPEG hardware encoder in this example
The use of a control delegate results in a fast response to bandwidth changes.
R1
R2
m1
m5
m6
CMU
Cairn
Transcoder
Bottleneck
R3
R4
R5
San Diego
m2

## Slide 61: Adaptive Compression Combines Xena, Scheduler, Delegates
Resource broker selects JPEG and transparently inserts transcoder to deal with video type mismatch.
  trades computational for communication resources
Delegate dynamically adapts JPEG encoding level to match available bandwidth.
  quick application-specific response
Hierarchical scheduler supports cooperative bandwidth sharing between video and bursty simulation data streams.
  combines sharing and isolation

## Slide 62: Virtual Private Network Service using Darwin
ISIEPC
UCL
CMU
DARPA2
MIT
UCLAPC
LBLPC
PARCPC
A
C
D
E
F
ISIPC
B
Link sharing
Virtualization of
router resources
G
Hierarchical
scheduler:
per-VPN resources
and QoS
Delegates: per-VPN
control plane protocols
Beagle:
establishes VPN

## Slide 63: Scalable Advanced Services based on Coordinated Active Components
Core networking services.
  Active core-stateless QoS
Middleware services.
  Support for end-to-end non-functional requirements
  Load balancing based on request contents
  Active distributed monitoring
User-level services.
  Virtual private network service with QoS support
  Proxy runtime environment for mobile hosts
  Scalable video distribution
Choice of services emphasizes distribution, composability, and end-to-end requirements.
Integrate Darwin in ABONE and expand API.
  Ideally combine with other execution environment

## Slide 64: Portable Networked Applications Must be Network-aware
Application adapts to network conditions in an application-specific way.
  Video streaming: match frame rate or size to available bandwidth
  Image database: select images with different resolutions
  Storage access: select the fastest server
  Distributed computing: change degree of parallelism
Collecting network information is a hard problem.
  The network can be very large
  Users need different types of information
  Different network technologies require different data collection methods
  Network operators are often reluctant to release network information

## Slide 65: Remos: A Traffic Report for the Internet
API that allows applications to collect explicit information on network connectivity.
Application specifies the nodes and network information that are of interest.
Network returns the best available information in a network-independent format.
  Simplified “virtual” topology
Remos has been built and released to users.
  BBN: adaptation in QuO/Corba
  U of Texas, Georgia T.: distributed computing
  CMU: video streaming, ..
User
Remos
Query
Network
Information

## Slide 66: Scalable Remos Architecture
Design goals.
  Scalability: deal with large networks and queries.
  Diversity: wide range of technologies and use.
  Privacy: operators limit access to internal info.
Appl 1
Appl 2
Modeler
LAN
Collector
SNMP
Master
Collector
ETH
WAN
CMU
A.ETH
B.ETH
C.CMU
D.CMU
EDGE.ETH
EDGE.CMU
LAN
Collector
SNMP
WAN
Collector
Benchmarks
Data collectors
collect
information
for individual
subnets
Master collector
breaks up
application requests
and merges results

## Slide 67: Runtime Adaptation using Remos
Airshed air pollution modeling application periodically uses Remos to collect network information and adapt.
  Automatically avoids busy links and nodes
Improves efficiency under a wider range of conditions
0
200
400
600
800
1000
1200
1400
1600
1800
2000
Dedicated
Non
interfering
Traffic 1
Traffic 2
Fixed
Adaptive
Time (sec)
aspen
timberline
maui
m-4
m-5
m-6
m-1
m-2
m-3
m-7
m-8

## Slide 68: Next Generation Internet Goals
Dramatically increase network performance.
  Both application-level and aggregate performance
  Involves scalability along a number of dimensions
Invite the development of a new generation of distributed applications.
  Telepresence, virtualized reality, ….
Develop network support for this class of applications and networks.
  Network management and provisioning
  OS and architecture support for high-speed networks
  Quality of service support for diverse set of services

## Slide 69: CMU NGI Topology
400
500
742
1138
353
107
159
512
619
Wean Hall
Cyert Hall
Mellon Institute
Carnegie Museum
Smith Hall
Building C
Hamburg
Qwest POP
Single mode GE
Multi mode GE
3COM
3900
3COM
3900
3COM
3900
3COM
9300L
3COM
9300S
100 Mbs E
Wean Hall

## Slide 70: Applications
Interactive video.
  Distributed lectures, video conferencing, …
Playback video.
  Adaptive video retrieval for Informedia
Telepresence applications.
  CMU robotics institute
Distributed computing.
  Earth quake simulation, …
Other applications that can benefit from explicit network support?

## Slide 71
stereo color cameras
pan-tilt
LCD monitor
XR4000
robot
3 channels of wireless video
• two from robot to network
• one from network to robot
wireless 2 way
audio / video link
Carnegie Museum
400 MHz PC with
• 2 video receivers, 1 transmitter
• 3 ASPRO realtime JPEG cards
• gigabit Ethernet card
• sound card
• radio ethernet
Transmission
Server
Carnegie Mellon
color camera
400 MHz PC with
• 3 ASPRO realtime JPEG cards
• gigabit Ethernet card
• sound card
Gigabit Network
Control
Server
System Overview:
Telepresence
Initiative - Demo #2
Two way audio and 3D video
from a wireless mobile
museum robot over Gigabit
Ethernet
Crystal Eyes
3D glasses
Telepresence
Application

## Slide 72: Virtualized Reality
Combine real/live elements of a scene with virtual elements.
  E.g. super impose images, maps, ...
  View from different angles
Capture scene with multiple cameras from multiple angles and extract 3D information.
  Lots of bandwidth for video
  Lots of cycles for online processing
Use 3D information to reconstruct new scene.
  View from different angles
  Add artificial elements

## Slide 73
PDP Monitor
composite
Gigabit Ethernet Switch
Pentium II 450MHz
Gigabit Ethernet NIC
Fast Ethernet NIC
1000BASE-SX (up to 1Gbps)
100BASE-T (up to 100Mbps)
Video D/A
CPU
UDP Trans. S/w
PCI Bus
PCI Bus (up to 133MBps)
MPEG H/w Encoder
MPEG H/w Encoder
MPEG H/w Encoder
MPEG H/w Encoder
(X12)
Camera (X48)
CPU#1
CPU#2
S-Video
MPEG S/w Decoder
Dual Pentium II 450MHz
(X12)
up to 4Mbps
Prototype System

## Slide 74: Platform for Networking Research
Support for QoS in high-speed environment.
  Per-flow, hard-guarantee models
  Class based, weak-guarantee models
Edge-driven control of network on multiple time scales.
  Networks with primitive internal capabilities
    extreme case: optical networks
  Integrate control, management, and provisioning
Testbed for service development and deployment.
  Build on top of Darwin
Evaluation using rich application mix.

## Slide 75: Mobile IP
Communicate with mobile hosts using their home IP address.
  should be transparent to applications and higher level protocols
  minimize changes to host and router software
Each area has a home agent and foreign agent that managing packet forwarding.
  binding = (IP address, foreign agent address)
  binding includes time stamp
Try to short circuit the home location by going directly to the foreign agent.
  cache bindings in the appropriate places
  protocol to update/invalidate caches
  security considerations

## Slide 76: Mobile IP in IPv4
Registration process
  mobile host registers with home and foreign agent
  cache bindings: address, care-of-address
Tunneling is used to forward packets between agents.
Supporting mobility
  invalidating old caches explicitly or in a lazy fashion
Many variants and optimizations possible.
  Mobile host can be its own foreign agent, e.g. can get local addresses
  Source can redirect packet directly to foreign agent
Source
Home
Agent
Foreign
Agent 1
Foreign
Agent 2

## Slide 77: Ad Hoc Networking
Build a network on the fly without the benefit of an established infrastructure.
  Building site, hotel room, …
Basic idea is that hosts function as routers and forward packets for each other.
  Mobility of hosts, signal propagation effects, battery power, load conditions, .. make routing very complicated
Proposal: Dynamic Source Routing (DSR).
  Hosts maintain a cache of source routes that are discovered through a route discovery protocol
  Routes are updates dynamically as the network changes

## Slide 78: Wireless Networks are Fundamentally Different
Challenge: a wireless link is a pipe of variable thickness that interferes with adjacent pipes.
  Wireless networks suffer from high, variable error rates.
Fundamentally different from a wired link, which is a fixed-bandwidth isolated pipe
  Requires fundamental changes in scheduling algorithms, monitoring support, ...
Wireless bandwidth is a critical resource so it should be managed carefully.
  Feedback so users can fully utilize their bandwidth
  Control so critical applications can be protected
Realizing a two-way communication channel is especially important!

## Slide 79: How Do We Manage a Variable Bandwidth Pipe?
Today’s packet schedulers were designed to manage fixed-bandwidth pipes.
We need a fundamentally different model for managing wireless bandwidth
  Reservations can fail when bandwidth disappears
  Priorities and preferred bandwidth allocations can change with the available bandwidth
  Location dependent errors raise questions of efficiency and fairness
Proposed solution: add per-flow parameter that indicates how important it is that this flow maintains fidelity in the presence of errors.
  As error environment gets worse, flows with high “power factor” become more important.

## Slide 80: Example: Class-based Reservations
Three classes of flows:
  Audio: low bandwidth, high power factor
  Video: high bandwidth, low power factor
  Data: in between
As error environment degrades, audio will maintain its fidelity the longest by using more “ether time”.
Power factor can also be used to optimize efficiency.
See Infocom 2000 for details
A
D
V
0%
A
D
V
35%
A
D
V
A
D
A
D
V
70%
A
D
V
Effort/Outcome
E
O
E
O
E
O
Errors
Errors

## Slide 81: Traffic Reporting in a Wireless LAN
Bandwidth characterization must include used bandwidth and error rates.
  Information is location dependent
  Cannot always be obtained accurately
Bandwidth is affected by traffic in adjacent cells.
  Typically not reported by management tools
  Again, result is location dependent
Must explicitly consider the physical location of the wireless host.
  IP address is not enough, as in wired networks
  Effects of mobility

## Slide 82: Wireless Andrew
802.11 based wireless infrastructure on Carnegie Mellon Campus.
  Based on Lucent wavelan cards
Provides ubiquitous connectivity to campus community.
  Fairly widely used by students, faculty and staff
Provides unique environment for experimentation in networking.
  Large scale wireless networks
  Aura project on “distraction free computing”