## Slide 1: Introduction to the Internet
Marvin A. Sirbu
Engineering and Public Policy
and
Industrial Administration
Carnegie Mellon University
sirbu@cmu.edu
http://www.ini.cmu.edu/~sirbu/MarvinSirbu.html

## Slide 2: Outline
The Internet: a packet network based on the TCP/IP protocol suite
Internet industry structure
Strategic Competition: NAPs, GigaPOPs and Multihoming
Datagrams and Virtual Circuits: The Internet and ATM
Intranets: from Frame Relay to Virtual Private IP networks

## Slide 3: The Internet
30 years ago the DoD began funding research in computer networks
ARPANET inaugurated in 1969
  emphasis on Remote Job Entry
Has evolved today to encompass:
  > 1,000,000 interconnected networks
  >200 countries
  13 million domains
  more than 10 petabytes (1016) per month over multiple backbones

## Slide 4: Some Definitions
An internet: A network of networks of computer hosts able to seamlessly communicate - usually through the Internet Protocol (IP) and services
Intranet: An internet within an organization
The Internet: More than 100,000 internets which are linked through public Internet Service Providers for the exchange of traffic
Extranet: A closed network for a corporation and its trading partners.

## Slide 5: The Enterprise Intranet
Outside World
Every machine transparently connected to every other
Notes: The local campus network
When your computer is connected, you will have established a link first of all to the local campus network and will be in a position to make use of the local communal computing facilities. You can log on to other computers such as the library’s catalog, or the local campus information service. You can also move files between your computer and other computers on the local network, and you can use electronic mail.
You also have access to the powerful computing facilities of our large, centrally-provided computers.
Name some of the local central computers.
To make use of one of these machines, you will need to first register as a user. When you have your userid and password, i.e. when you have your account, you can logon and use the applications and services on that machine.
Mention same some of the facilities available on the local machines.
But being ‘on the network’, means much more than simply accessing local computing facilities. You are also connected, through the local area network to JANET - the UK’s Joint Academic Network.

## Slide 6: Internet Philosophy
Peer to Peer Network
  every Host able to communicate with every other host
End-to-end design principle
  Assume end systems are smart
  Maximize functionality in the end systems
    “stupid networks”
Internet Protocol provides “glue” for running over a variety of subnetwork types
Network merely carries packets. Services are provided by applications running on Hosts
Rough consensus and running code

## Slide 7: Internet Architecture
APPLICATION
Web
Browsing
Video Server
Voice
Dial-up
Electronic Mail
Financial Services
ATM
Frame Relay
Satellite
Wireless
LANs
SMDS
IP
Cable Modem Access
Private Lines
ADSL
DWDM
SONET

## Slide 8: Benefits of the Internet Philosophy
New services are provided by servers at the edges of the network
  Anybody can invent a new service
    WWW
    Napster
    …
Minimizing functionality in the routers has allowed throughputs to scale by five orders of magnitude since the development of IP
  56 kbps  10 Gbps

## Slide 9: TCP/IP
Subnetwork B
Subnetwork A
Internet Protocol
Transmission Control
Protocol
Unacknowledged
Datagram Protocol
Telnet
FTP
HTTP
Time of Day
Internet Control
Message Protocol
• • •
SMTP

## Slide 10: A Network of Networks
Q: Who Manages the Internet?
A: No One
The Internet is a collection of independently operated and managed networks that agree to exchange traffic using open standards

## Slide 11: Internet: Directly Reaching 90,000,000+ Computers
Notes: The world from your desktop
Title: The World from your desktop
  ‘The world’ = world of resources to which the interconnected computers on national and international networks give access.
  This matrix of networks we can refer to as ‘the network’. If your computer is connected to the local network, which then connects to the national academic network, you can be said to be ‘on the network’. And if you are ‘on the network’, this world of network resources is open to you.
Aims of presentation
  to show a sample of what that world might offer you
  to enable you to begin exploring it for yourself
There is a handout to help you get started
  a starting point for your network explorations
  pick one up before you leave

## Slide 12: Internet Hosts
Source: http://www.netsizer.com/

## Slide 13: Worldwide Internet Users
World Total (millions) | 360
Africa | 3.1
Asia/Pacific | 89.
Europe | 94
Middle East | 2.4
Canada and US | 157
Latin America | 13
Source: http://www.nua.ie/surveys/how_many_online/
July, 2000
Notes: Notes

## Slide 14: US Internet User Trends
US has 50% of total Internet population

## Slide 15: Online and Networked Homes
0.0
10.0
20.0
30.0
40.0
50.0
60.0
70.0
1998
1999
2000
2001
2002
2003
2004
Units in Millions
Homes On Line
Multi PC Homes
Home Networks
Source: Frost & Sullivan, Sep. 1999

## Slide 16: European Internet Usage

## Slide 17: Internet Use Outside of the U.S.

## Slide 18: Organization of the Internet Industry

## Slide 19: Internet Industry Structure
1. Customer (CUS)
2. Local Area Transport Provider (LAT)
3. Internet Access Provider (IAP)
4. Wide Area Transport Provider (WAT)
5. Internet Service Provider (ISP)

## Slide 20: Internet Industry Value Added Chain
Internet Access Provider (IAP)
(retail services, e.g. local access)
-sales & marketing, customer
service, billing
-modem pools, servers
-leased access services
Internet Service Provider (ISP)
(wholesale services, e.g., Internet
backbone providers
-IP routers, exchange points
-wide area transit
-peering and settlements
Local Access Facilities Provider
(LAT)
(e.g. local telco, wireless, CATV)
local access, switching, and
transport facilities
Wide Area Facilities Provider
(WAT)
(e.g., long distance carrier)
-wide area switching and transport
facilities
-fiber, WDM, SONET, ATM
Customer

## Slide 21: Internet Tiered Architecture
IAP
IAP
LAT
ISP Backbone Provider
ISP Backbone Provider
IAP
LAT
NAP
NAP
Private
Peering
IAP
LAT

## Slide 22: Tiered Internet Industry Structure
6000+ North American Internet Access Providers (IAPs)
  regional or national
  provide Internet access to end user customers
  dialup or leased line
  Customers of ISP Backbones
40-50 Tier 1 ISPs
  National or International
  Interconnect with other ISPs at Network Access Points (NAPs)
    Public NAPs or private bilateral peering points
  Exchange traffic without settlements

## Slide 23: Vertical Integration
Various forms of vertical integration
  LAT-IAP-WAT-ISP AT&T, WorldCom, Sprint
  LAT-IAP ILECs
  WAT-ISP Williams, Level 3
  IAP-ISP CAIS

## Slide 24: Commercial IP Services
R
R
R
R
R
R
ISP
IXC
Early ISPs leased circuits from IXC to interconnect routers
Today Largest Backbone ISPs are also IXCs

## Slide 25: ISPs Provide More Than Packet Transport
Adjuncts to Basic Service
  Domain Name Servers (DNS)
  email servers
High speed access and wholesale service
Hosting
  web servers
  application servers
Content Delivery Support
  caching servers
Web Design
Customer network design and management consulting
Proprietary Content

## Slide 26: ISPs Provide More than Access: Analysis of 3816 ISPs by S. Greenstein
Notes: 10

## Slide 27: Web Hosting Market Forecast
Source: DB Alex Brown

## Slide 28: ISP Strategy
IP transport is a commodity
  newest networks have lowest costs per bit-mile
Differentiate basic network service
  Quality of Service
  Multicasting
Differentiate by moving up the value added chain
  bundle IP transport with unique services
    application hosting
    management of customer Virtual Private Networks
    content

## Slide 29: Growth of North American ISPs
Source: Boardwatch

## Slide 30: Internet Backbone Market Shares
Source: Internet Week, 6/26/00

## Slide 31: Internet Service Providers to Enterprise Market
Source: Cahners In-Stat based as of 6/99

## Slide 32: UUNET

## Slide 33: Qwest Backbone

## Slide 34: Level 3 Fiber Backbone

## Slide 35: Williams Communications
Source: Web Week 10/27/97, p. 34

## Slide 36: The Enron Network

## Slide 37: AT&T IP Backbone

## Slide 38: IBM GlobalNet (now ATT Business Communications)

## Slide 39: Backbone Observations
If you live in Montana or North Dakota you are far from any backbone node
  Many smaller cities and states are poorly served
New fiber networks are greatly increasing available capacity
Source: Communication News, Feb 2000, p. 12

## Slide 40: Growth in Undersea Fiber

## Slide 41: Will There Be a Fiber Glut?
Source: Barrons, 9/9/00

## Slide 42: Internet Service Economics
Users typically pay flat rate to IAP based on access port speed
  IAPs are not restricted to published tariffs; prices are often negotiable
IAPs pay an ISP for transit to other ISPs and their customers
ISPs peer with each other at public or private Network Access Points (NAPs) and typically do not pay settlements to each other
As with most communications systems, last mile (last 100 meters?) costs dominate
  CMU spends ten times as much to provision and maintain its LAN as it does for Internet services

## Slide 43: ISP Tariffs
Access Rate $/month
Dial-up 22
Dedicated 56 Kbps 444
Dedicated T1 1,543
10 Mbps 7,706
DS3 (45 Mbps) 32,312
Significant economies of scale
Source: Internet Week 10/3/97, p.41

## Slide 44: ISP Pricing: T1 Access
Great variation in pricing and bundled services
Source: Boardwatch, 1999

## Slide 45: IP Value Added Services
Few users are sophisticated enough to buy raw packet transport with no support.
Support is expensive
  Full consulting support can double the monthly rate

## Slide 46: Emergence of Usage Based Tariffs
AT&T Managed “Burstable” DS3 Service
Compare to $25,000 for non-burstable DS3

## Slide 47: The Marginal Cost of Internet Usage
Based on AT&T’s Managed Burstable DS3 service
$605/Mbps
$.23/gigabit or 0.09¢/minute for a 64 kbps phone call
Source: http://www.att.com/abs/serviceguide/docs/mis_sg.doc 5/23/00

## Slide 48: ISP Performance Variation
Source: Boardwatch

## Slide 49: Summary
The Internet industry is:
  hierarchically structured
  extremely competitive at IAP layer, less so at ISP layer
  barriers to entry for IAPs are small
  ISPs are integrated wide area transport providers
ISPs are rapidly moving up value added chain
  web hosting and design
  network design
  differentiated services

## Slide 50: Internet as a Network of Networks
NAPs
MultiHoming
GigaPOPs

## Slide 51: Competitive Strategy
Porter’s theory of competitive strategy
Increase your customer’s switching costs
Force your suppliers to compete
Firm
suppliers
customers

## Slide 52: How the ISP Ties the Customer
Pricing
  long term contracts and volume discounts
Provide proprietary services
  virtual private networks,
    incompatible security
Provide better performance to customers who are entirely on network
How Does the ISP Customer Resist Tying?
  Demand standards-based services
  Second sourcing

## Slide 53: NAPs
Prior to 1992 there was one default backbone ISP that everyone connected to: NSFnet
When the NSFnet was decommissioned, the NSF created public NAPs where competitive ISPs could interconnect
  New York
  Chicago
  San Francisco
MFS Fiber systems (now part of Worldcom) created several Metropolitan Area Exchanges (MAE-East, MAE-West)

## Slide 54: Public and Private Peering
IAP
IAP
LAT
ISP Backbone Provider
ISP Backbone Provider
IAP
LAT
NAP
NAP
Private
Peering
IAP
LAT

## Slide 55: Network Interconnection
Source: Boardwatch

## Slide 56: NAPs
Earliest NAPs were a simple Ethernet cable
Each ISP connected a router to the cable
NAP at Layer 2 (subnet layer)
Bilateral agreements on terms of traffic exchange

## Slide 57: NAPs
Interconnect today using
  LAN switching
    FDDI, 100BaseT (100 Mbps)
  ATM switch
    up to OC12 (620 Mbps)
Example: MAE West ATM switch traffic
Source: www.mae.net/atm/

## Slide 58: NAPs
No ISP carries more than 30% of network traffic
  inter-organizational and consumer traffic likely to traverse one or more NAPs
Peering points can be bottlenecks
  higher packet loss at peering points than in ISP backbones
  incentive for multi-location firms to concentrate traffic with one ISP

## Slide 59: Public versus Private Peering
Interconnection at a NAP does not guarantee settlement-free peering
  smaller IAPs pay ISPs for Transit
  Peering: accept traffic for your customers and your customers customers
  Transit: accept traffic for any destination
Increasingly, ISPs make bilateral private peering arrangements
  more difficult for an ISP to determine who is sending it traffic at a multilateral NAP

## Slide 60: Public and Private Peering
Carnegie
Mellon
Source: Data Communications Magazine
October, 1999
Number of
Connections to
the 30 ISPs
surveyed

## Slide 61: Hot Potato Routing
IAP A
ISP Backbone Provider #2
ISP Backbone Provider #1
NAP
NAP
IAP B
Asymmetric routing
Handoff packet as quickly as possible
Bit miles carried may be unequal if one ISP has more web farms and other has more end users
Cold potato routing?

## Slide 62: Example Traffic: AboveNet to PacBell ATM NAP
30 minute average samples over one week ending 2/24/00
Traffic from NAP
Traffic to NAP
OC3 (155 Mbps) Interface

## Slide 63: Evolution of NAPs
First generation NAPs run by carriers
  MCI: the MAEs
  ILECs: NSF NAPs
ISPs concerned that NAP operator in a position to learn too much about traffic
New entrants building “neutral” NAPS
  Equinix
  PAIX
Provide web server farm space adjacent to NAP for good connectivity to major backbones.

## Slide 64: Equinix Growth Projections & Plans
30+ Global locations Over Next 4 Years
San Jose, Ashburn, Newark 1Q00, Chicago, LA, Dallas 2Q’00
Source: http://www.nanog.org/mtg-0002/equinix.html

## Slide 65: Solutions to NAP Performance Problems
Multihoming
  Customer purchases direct access to multiple backbone ISPs
  Requires significantly greater customer expertise to manage routing
  Poses significant problems for route aggregation
ISP Backbone Provider
ISP Backbone Provider
NAP
NAP

## Slide 66: IP Address Assignment
Recall that there are 4 types of IP addresses for different size networks
In early days, network numbers assigned by IANA* to organizations for the asking
  If you had more than 255 hosts, you needed a class B address good for 64000 hosts
As Internet grew
  Class B addresses became scarce
  Routing tables grew in size
==>
“Classless InterDomain Routing” (CIDR)
Currently handled by American Registry for Internet Numbers (ARIN)

## Slide 67: CIDR Addressing
Length of network address is variable and specified using a netmask
Address 204.194.28.40 with mask 255.255.255.128 means 25 bits of network number and 7 bits of host
Can merge a group of adjacent class C addresses to form a larger network, or break up a class B into multiple networks
In routers, if adjacently numbered networks are served by the same router, need only store the common prefix + mask in the router table
  substantially reduced growth rate of router tables

## Slide 68: Changing ISP Means Changing IP Address
ISP A
Customer
190.10.80.0 to
190.10.87.255
190.10.0.0/16
175.25.0.0/16
190.10.80.0/21
Customer
175.25.96.0 to
175.25.103.255
190.10.0.0/16
175.25.0.0/16
175.25.96.0/21
Internet
Internet
Customer served by ISP A
Customer switches to ISP B
ISP B
ISP A
ISP B

## Slide 69: CIDR and Route Aggregation
To maximize ability to use common prefixes, networks served by a ISP A should have adjacent network numbers
  ISP B can then have one router table entry for the common prefix of ISP A’s customers.
Requires network numbers to be assigned by ISP
  dialup customers are dynamically assigned an IP address on each call

## Slide 70: CIDR Address Allocation
Service provider hands out network addresseS to its customers from a large block assigned to it
Routing entries for the ISPs customers can be merged in many cases
  Packets should be forwarded to that ISP which will then forward them to the customer
  Only the destination ISP has to distinguish between its customers
  Recursive for IAPs and their customers
ISP A
Cust
Cust
Cust
ISP B
IAP 1
IAP 3
IAP 2

## Slide 71: Changing ISPs
Changing ISP requires customer to change IP addresses on all machines or break common prefix
  Can be costly if addresses were statically defined
    Use Dynamic Host Control Protocol (DHCP) for centrally assigning IP addresses to machines
Multihoming breaks route aggregation
  requires “portable” network number assigned by ARIN

## Slide 72: GigaPOPs
Gigabit Point of Presence
Shared Multihoming

## Slide 73: GigaPOPs Share Access to Backbone ISPs
LAT
GigaPOP
ISP Backbone Provider
ISP Backbone Provider
NAP
NAP
GigaPOP

## Slide 74: What Is A GigaPOP?
Multiple sites agree to aggregate to a central location and share high-speed access from there, instead of each maintaining direct links to multiple networks
Share costs through sharing infrastructure
Share ISP expenses
Essentially statistical multiplexing of expensive high-speed resources
  at any given time much more bandwidth is available to each institution than each could afford without sharing
Share engineering and management expertise
More clout with vendors

## Slide 76: InterNap: A Private GigaPOP Operator
Source: InterNap

## Slide 77: GigaPOPs Reduce NAP Usage
Source: InterNap

## Slide 78: GigaPOPs Can Route Traffic Over Lowest Cost Backbone
LAT
GigaPOP
ISP Backbone Provider #2
ISP Backbone Provider #1
NAP
NAP
GigaPOP
XYZ-West
XYZ-East
GigaPOP operator routes XYZ intra-company traffic over lowest cost backbone
Forces price competition among ISPs

## Slide 79: GigaPOP Business Model
Paying customer of backbone networks, not a peer
Operate at layer 3 (IP layer)
  NAPs operate at layer 2 (subnet layer)
Able to select backbone to minimize NAP usage
GigaPOP operator has choice of backbones for traffic between two GigaPOPs
  force price competition among backbone providers
  if price equal, choose to minimize latency
  reduces backbone to commodity IP transport provider
    reduces ISP’s cost by eliminating uncompensated peering
Ideal location for server farms
GigaPOP customer outsources management of multihome routing

## Slide 80: GigaPOP
GigaPOP acquires portable IP address space from ARIN
  assigns addresses to customers
Customer’s IP address needn’t change if traffic is shifted among backbone providers
Is a GigaPOP a virtual IAP?
  a point not a network
Or, a true IAP?
  distributed GigaPOP

## Slide 81
Source: UCAR

## Slide 82: Summary of Strategic Competition
The Internet is a Network of Networks
ISPs both compete and cooperate
ISP goal
  capture the customer and increase his switching costs
Customer goal
  resist capture, force price competition among providers
Strategic role of NAPs, Multihoming, and GigaPOPs

## Slide 83: ALTERNATIVE PARADIGMS
Connection Oriented (CO) vs Connectionless (CL)
or
Virtual Circuits vs Datagrams

## Slide 84: TWO WAYS OF THINKING ABOUT A NETWORK
1) The network is like a perfect telephone wire. First you set up the call. Then packets put in come out the other side, in order and without any errors
2) Handing a packet to the network is like putting a message in a bottle and tossing it into the river. Most of the time, it will get downstream. Some messages will be lost, and the bottles may arrive out of order.

## Slide 85: Datagrams versus Virtual Circuits
Datagrams
  every packet has the full address of the destination
  each packet is routed through the network independently
    packets may arrive out of order
  network has no expectations about future packets
    packet switches are stateless

## Slide 86: Datagram (CL) Routing
Host
Host
PS
PS
PS
PS
Host
P
P
P

## Slide 87: Datagrams versus Virtual Circuits
Datagrams
  every packet has the full address of the destination
  each packet is routed through the network independently
    packets may arrive out of order
  network has no expectations about future packets
    packet switches are stateless
Virtual Circuits
  a setup packet carrying full address of destination sets up a “connection” between origin and destination
    data packets identified by short Connection ID
  switches maintain per-connection routing tables
  packets follow fixed path
  Resource Reservation and Admission Control (Call blocking)

## Slide 88: OVERHEAD COMPARISONS
Datagram Network
Address
Data
Address
Data
Virtual Circuit Network
Address
Setup
ID
Data
ID
Data
ID
Clear

## Slide 89: VIRTUAL CIRCUIT ROUTING e.g. X.25
9
PS3
PS4
DTE
DTE
DTE
b
a
c
a
b
a
b
c
b
c
7
27
5
7
33
13
Routing table for packet switch # 1
Link # in LCN Link # out LCN
a 5 b 7
a 7 c 27
Routing table for packet switch # 2
Link # in LCN Link # out LCN
a 7 b 13
X.25
PS1
PS2

## Slide 90: Examples of CO vs CL protocols
Virtual Circuit Datagram
X.25 Internet Protocol (IP)
Frame Relay IPX (Novell)
ATM Appletalk
MPLS XNS

## Slide 91: CONNECTION ORIENTED (CO) (VIRTUAL CIRCUITS)
Clearly distinguishable lifetime
Three party agreement
Negotiation
  parameter values
  collect calls
Connection identifiers
Data sequencing
Flow control

## Slide 92: CONNECTIONLESS (CL) (DATAGRAM)
Everything in one packet and one interaction
Data unit independence
Two party agreement
No negotiation

## Slide 93: COMPARISON OF CO vs CL
Connection Oriented
  Guaranteed quality of service
  Can reserve resources
  Accountability
  Traffic Engineering
Connectionless
  Broadcast capability
  Ease of gateway construction
  Robust under gateway failure
  Less delay

## Slide 94: Why Is This Debate Important?
Mirrors the debates today over
  Frame Relay and ATM versus IP
  How to provide Quality of Service within IP
Modern IP networks are often built on top of a Virtual Circuit network
  Frame Relay
  ATM
  MPLS (future)

## Slide 95: IP over ATM over SONET over DWDM over Fiber
DWDM Optical
Network
ATM
ATM
ATM
ATM
IP Router
IP Router
IP Router
IP Router
IP Router
ATM
IP

## Slide 96: IP, ATM, SONET and WDM Interplay
IP
ATM
SONET
WDM
  Four possibilities will co-exist for awhile
    IP provides the common architecture for all applications
    ATM is efficient and reliable for core backbone and traffic engineering
    SONET provides reliability, restoration and provisioning
    WDM provides transmission cost efficiency

## Slide 97: Internet Subnet Layers
DWDM/Fiber
SONET
ATM
AAL5
PPP
SONET
ATM
AAL5
Snap
LLC
SONET
ATM
AAL5
SONET
PPP
OIF
(future)
IP Layer
Ethernet
Copper
or Fiber
PPP
AAL: ATM Adaptation Layer DWDM: Dense Wavelength Division Multiplexing
OIF: Optical Interconnect Forum PPP: Point to Point Protocol
LLC: Logical Link Control layer

## Slide 98: Why an ATM Layer?
Advantages
  ATM infrastructure provides circuit emulation services for POTS
  Support multiple Virtual Private IP Networks (VPNs) sharing the same ATM infrastructure
  Full mesh of ATM PVCs means fewer router hops, less latency
Disadvantages
  “Cell tax” -- cell header overhead
  manage two different technologies
  IP routing protocols don’t scale well in large full mesh networks

## Slide 99: Collapsing the Layers
IP
Frame Relay
ATM
SONET
WDM
Legacy
IP/WDM Future
WDM
TCP
TCP
IP
Application
Application
Future networks will reduce the number of layers
Substantial equipment savings
Lightweight layer on top of WDM for link monitoring
Restoration via rerouting of traffic at IP layer
Guaranteed circuits provisioned using MPLS

## Slide 100: Corporate Networks

## Slide 101: Corporate Data Networks
1975 1980 1985 1990 1995 2000
BISYNC
Networks
SNA
Networks
LAN
Internetworks
Mesh/Ring Network
Multiple Protocols
Host & Workstation
Mixed Addressing
Large Amounts of Data
56,000 to 100 Mbps
Mesh Network
One Dominant Protocol
Multi-Host
Application Independent
Large Screens
Query-Response
9,600 - 56,000 bps
Star Network
Single Protocol
Single Host
Small screens
Query/Response
1200 - 9600 bps

## Slide 102: Corporate Data Networks: Transport Facilities
1975 1980 1985 1990 1995 2000
Private Analog
Circuits
Private T1
Networks
Public
Broadband
Networks
BISYNC
Networks
SNA
Networks
LAN
Internetworks

## Slide 103: Private Net with TDM and Routers
Router
MUX
FEP
MUX
MUX
MUX
Router
Router
Router
token ring
3174
3174
token ring
3174
FEP
Terminals
Terminals
Host
Host

## Slide 104: Integrated Internetwork

## Slide 105: Leased Line Based Intranet
High Speed Serial Line Card
CSU/DSU
co
co
Router
Router
Router
CO
CO
CO
POP
POP
POP
CSU/DSU
CSU/DSU
CSU/DSU
CSU/DSU
CSU/DSU
Channel Service Unit/
Data Service Unit
POP
Point of Presence of Inter-
exchange carrier
CO
Central Office
Leased line service
configuration

## Slide 106: FRAME RELAY
A connection-oriented service
  uses low overhead channel numbers
Provides error detection (FCS) but no error correction
  responsibility of higher layers
Frames data using modified LAPD protocol
Used largely for Permanent Virtual Circuits
  leased line replacement for
    internal networks
    access to Internet
Current services at up to 45 Mbps, though most usage is at DS1 rate (1.5 Mbps) and below.

## Slide 107: Savings with Frame Relay
Frame Relay service
configuration
co
co
Router
Router
Router
CO
CO
CO
POP
POP
POP
CSU/DSU
CSU/DSU
CSU/DSU
Source of Savings
Fewer ports on the router
Fewer CSU/DSU
Single higher speed access circuit
Can purchase only fractional T1 Committed Information Rate CIR to get T1 latency

## Slide 108: Frame Relay Pricing
Port Charge based on access speed
Source: Communications News, May, 1998, p. 53

## Slide 109: Monthly Charge for Committed Information Rate (CIR)
PVC Charge. Price is Simplex (one way)
  distance independent

## Slide 110: Public Data Network Pricing is Distance Insensitive

## Slide 111: Frame Relay Services Dominated IP Until Recently
Source: Data Communications, 12/97
($ millions)

## Slide 112: Savings with Internet Service
ISP service
configuration
Source of Savings
Fewer ports on the router
Fewer CSU/DSU
Single higher speed access circuit
Buy T1 access link for low latency but pay less than T1 leased line price
co
co
Router
Router
Router
CO
CO
CO
POP
POP
POP
CSU/DSU
CSU/DSU
CSU/DSU

## Slide 113: Difference Between Frame Relay and Internet
Frame Relay is a layer 2 service
  can carry multiprotcol layer 3 traffic
    TCP/IP
    IPX
    Appletalk
IP is a layer 3 service
  must standardize on IP or use Protocol Encapsulation
  e.g. Point to Point Tunneling Protocol (PPTP)

## Slide 114: Protocol Encapsulation
An alternative to multiprotocol routing is encapsulation of one internet packet type in another
Appletalk internet packets (DDP) are encapsulated into DoD IP packets
Can now be carried across a TCP/IP network
Gateway strips IP and
forwards AppleTalk
Gateway wraps
AppleTalk in IP
IP (UDP)
Apple DDP
Apple DDP

## Slide 115: Using IP As a Subnet for Appletalk
Apple DDP
Router/
Gateway
IP (UDP)
Apple DDP
TCP/IP Network
Apple DDP
Router/
Gateway
Gateway makes entire TCP-IP internet appear as a single large Appletalk subnet
Gateway maps Appletalk addresses to TCP-IP "subnet" addresses

## Slide 116: Using Appletalk as a Subnet for IP
Macintosh "talking" IP
IP
Apple DDP
IP
Gateway strips AppleTalk,
forwards IP
Gateway wraps IP
in AppleTalk
Mac application creates IP packet and encapsulates it in Appletalk internet (DDP) packet
Router/Gateway strips Appletalk forwards IP packet to Internet host.

## Slide 117: Difference Between Frame Relay and Internet
FR a regulated offering of common carriers
ISP unregulated offering
FR provides committed information rate, QoS guarantees
ISP provides no guarantees

## Slide 118: Internet vs Leased Line Pricing
T1 Leased line, NY to San Francisco $8,400 - 12,000/mo
Cost for T1 Internet service in each city
  T1 Intenet access from Uunet $2,312/mo
  T1 line from premises to ISP POP 1,000 - 1,700/mo
Total Cost for T1 Internet NY - SF $6,624 - 8,024/mo
Source: Communications Week 4/21/97 p. 73.

## Slide 119: IP Virtual Private Networks
Business networks
Shared
infrastructure
Business networks
Business networks
Partitioning a shared infra-structure to create a virtual network that provides participants
  Connectivity
  Traffic Isolation
  Access Control
  QoS
  Security.

## Slide 120: Corporate Virtual Networks
Virtual Private Networks
  Use encryption to create secure “tunnel” through public Internet

## Slide 121: Virtual Private Networks
Router Management
Service Level Agreements
  availability
  latency
Use of ATM PVCs to provide guaranteed capacity
Security
Dialup support

## Slide 122: IP over ATM over SONET over DWDM over Fiber
DWDM Optical
Network
ATM
ATM
ATM
ATM
IP Router
IP Router
IP Router
IP Router
IP Router
ATM
IP

## Slide 123: Mananged IP Service
DWDM Optical
Network
ATM
ATM
ATM
ATM
IP Router
IP Router
IP Router
IP Router
ATM
IP
IP Router

## Slide 124: Managed IP Service
Place ISP owned and managed routers on customer’s premise
Link these routers with ATM Virtual Circuits providing committed information rate
Guarantees available capacity between company locations
Company deals only with IP interface to router--never sees ATM
ISP takes responsibility for network availability
  I.e. arranges for redundant access circuits from company premises to ATM switch
Service Level Agreement may specify guaranteed throughput, latency, availability
Premises router encrypts all intra-company traffic for security

## Slide 125: Where to use IP VPNs?
Secure corporate network interconnection
  Centralize processing and control in security gateway (router, firewall, or VPN server at network edge)
  “Part of IP” -- policies applied to every IP packet
  User transparent, supports any IP-based application
Corporate Network
Security
Gateway
Internet
Secure Tunnel
Security
Gateway
Branch Office
Notes: IP VPNs are best viewed as connecting separate networks -- for example, branch office networks -- by providing a tunnel between security gateways.
A security gateway can be a router, a firewall, or a special-purpose VPN server, located at the edge of each network. All packets entering or leaving the network must pass through the security gateway. Thus, the security gateway is an excellent place to centralize policy decisions and to beef up hardware support for the CPU demands imposed by bulk encryption.
By building security into IP at the gateway, it becomes part of a network’s infrastructure. Users don’t need to do anything to enable or use it, and any application protocol carried by IP packets can be protected. Older routers that might be encountered by an IPsec-protected packet just see ordinary IP packets. Only the endpoints of the tunnel -- the security gateways -- need to be IPsec-aware and interoperable.

## Slide 126: Where to use IP VPNs?
IPsec can also securely connect hosts
  Host-to-gateway for secure remote access
  Host-to-host for end-to-end packet protection
Can be more costly and intrusive
  Must install, configure, run IPsec client on every host
  Limited support for roaming hosts
IPsec-Enabled Host
Internet
Secure Transport Mode
IPsec-Enabled Host
Public Host
Notes: IPsec can also be used to connect an individual host to either a security gateway or to another host.
Tunneling from an individual host to a security gateway can be used to support remote access in a manner that looks similar to voluntary PPTP tunnels. IP packets sent by an IPsec host to a protected network are encapsulated and delivered to the security gateway for that network. However, IP packets sent by that host to public destinations are sent directly, without addition of IPsec protocols. Security policies must be configured into the host to differentiate between public and private destinations.
IPsec can also be used to protect IP packets between a pair of hosts, providing end-to-end privacy and message integrity. This configuration is referred to as “transport mode” IPsec. Again, packets sent to public destinations are unaffected by the use of IPsec transport mode to private destinations, as determine by security policy at each host.
But adding IPsec to every host in a network is more intrusive and costly than centralizing IPsec deployment at security gateways. This year, IPsec is being added to Windows 2000 and flavors of UNIX. But until this happens, special IPsec client software must still be separately installed on each host. Security parameters must be configured at each host, typically without automated distribution of centrally-configured policies. And each host must bear the additional packet processing demands imposed by IPsec.
Furthermore, support for roaming hosts is still limited. Standards work is underway to add DHCP assignment of tunnel endpoint IPs, incorporate traditional dial user authentication, and facilitate use of IPsec with Mobile IP.

## Slide 127: Layer 2 (Dial) VPDNs
Treat remote dial access as virtual (point-to-point) links
  Traditional dial-up user authentication (CHAP, PAP)
  Controlled access to corporate network via Internet
  In some cases, data confidentiality
ISP
Subnet
Internet
Corporate
LAN
Enterprise
Access
Server
Workstation,
RAS Server, or
ISP POP
PPTP/L2F/L2TP
Notes: Recognizing the financial benefits of ubiquitous low-cost dial access provided by the public Internet, dial access vendors were the first to develop tunneling protocols.
Cisco approached this challenge by defining its Layer 2 Forwarding Protocol (L2F) as an add-on to ISP access server equipment, a network infrastructure enhancement.
Microsoft designed its Point-to-Point Tunneling Protocol (PPTP) as a feature upgrade to dial-up networking clients and paired remote access servers, a network edge software solution.
Cisco and MS enlisted industry partners, and submitted their respective protocols to the IETF in 1996. Since that time, they have worked together to produce a common hybrid L2 standard for tunneling: the Layer 2 Tunneling Protocol (L2TP). In the interim, virtually every dial access vendor has deployed L2F and/or PPTP.
In the next few slides, we'll look at how each of these protocols enables Virtual Private Dial Networks.
1) All three employ traditional dial authentication (CHAP, PAP, etc).
2) All three allow a tunnel server to enforce access controls at the point where the dial session connects to the corporate network.
3) We'll see that MS PPTP, but not L2F, encrypts payload, and how L2TP will be married with IPsec to address both confidentiality and integrity requirements.

## Slide 128: Layer 3 (IP) VPNs
Encrypts IP data or encapsulates (tunnels) IP packets
Secures IP traffic between gateways, hosts
  IP Security Protocols: ESP and AH
  Internet Key Exchange: ISAKMP and Oakley
ISP
Subnet
Internet
Corporate
LAN
Router, Firewall, or VPN Server
Workstation
or Router
IPsec, IKE
Notes: During the past 3 years, the IETF has been defining extensions to IP in order to make it more secure when private packets transit a shared public network like the Internet.
IP security protocols, collectively referred to as “IPsec”, include the Authentication Header (AH) and Encapsulating Security Payload (ESP). These IP extensions provide the foundation for constructing network layer VPNs.
IPsec depends upon symmetric keys that must be distributed securely and changed frequently. The standard used to automate this process is called the Internet Key Exchange (IKE).
In the next few slides, we'll look at IPsec and IKE work together to enable Virtual Private IP Networks.

## Slide 129: Virtual Private Networks
Router Management
Service Level Agreements
  availability
  latency
Use of ATM PVCs to provide guaranteed capacity
Security
Dialup support

## Slide 130: IP VPN Revenue Forecast

## Slide 131: Summary
Corporate network migration:
  Leased Lines => Frame Relay => IP VPNs
Key issues:
  Quality of Service
    latency, availability, throughput
  Security
Deliver QoS by building IP networks over QoS capable ATM
Deliver security through encapsulation, encryption

## Slide 132: Managed Network Market Evolution
Source:
http://www.webtorials.com/main/vici/presentn/frf-vpn/frf-vpn.pdf