## Slide 1
18-100 Introduction to Electrical and Computer Engineering
Lecture 18
Data Communications

## Slide 2: Outline
Today
Physical Layer
Link Layer
Network Layer
Transport Layer
Application Layer

## Slide 3
Application
Transport
Network
Physical
Link
Physical Layer: A Few Odds and Ends
The messages sent and received by application programs
The end-to-end connection as seen by a programmer
The decision making needed to steer a message from source to destination through an inter-network
The management of the physical channel for communication
The specification for the hardware that enables the signaling between or among devices

## Slide 4: A wire isn’t a just wire anymore!
Everything from the board to the wire adds capacitance, inductance, resistance, etc.
Acts as big RLC filter
https://ww1.microchip.com/downloads/en/Appnotes/VPPD-02901.pdf

## Slide 5: Encoding
Too many ones or zeros in a row are hard to “clock”
  Sender and receiver might time long sequence of high or low voltage differently
Made worst by AC Coupling, e.g. use of capacitance as high-pass noise filter
  Capaciters have charge-discharge curves. They aren’t flat. Rounding, esp. at edges.
Transitions synchronize clocks
Need a coding that guarantees transitions

## Slide 6: Baseline Wander From Capacitance
“AC Coupling” is used for transmission, e.g. a capacitor-like filtering of the low-frequency DC bias leaving only the higher frequency data.
  But, a DC bias can slowly creep in over time. It isn’t completely eliminated
http://docwiki.cisco.com/wiki/Ethernet_Technologies

## Slide 7: Old Solution: Manchester Encoding
0
0
1
1
0 = rising transition
1 = falling transition
1 transitions per bit, but twice as much bandwidth
High-low pattern has good electrical properties
Balanced signal – no net DC voltage.
This allows AC coupled power supply on receiver.
If code had a DC bias, it would be lost in the transformer on the receiver side.

## Slide 8: Challenges To Manchester Encoding
Requires a clock rate of 2x data rate
Just can’t work for higher data rates
The frequency space isn’t high enough
Modern ethernets, e.g. gigabit use specific bit encodings
  Specific bit patterns are encoded in larger patterns to guarantee transitions
  But, not 2x as long

## Slide 9: Outline
Today
Physical Layer
Link Layer
Network Layer
Transport Layer
Application Layer

## Slide 10
Application
Transport
Network
Physical
Link
Link Layer
The messages sent and received by application programs
The end-to-end connection as seen by a programmer
The decision making needed to steer a message from source to destination through an inter-network
The management of the physical channel for communication
The specification for the hardware that enables the signaling between or among devices

## Slide 11
Link Layer Framing is critically important
Preamble
Destination MAC Address
Source MAC Address
DT
Data (Payload)
FCS
NH
TH
1010 1011
Preamble: A sequence of alternating 1 and 0 to alert computer with “11” to indicate the frame is next.
DT: Data Type
FCS: Frame Check Sequence
Using Cyclic Redundancy Code to Check the Fidelity of the Data Sent
Media access control (MAC) address: Hardware address
Framing breaks data into manageable units
Easily identifiable beginning and end
Identify sender and receiver
Carry data
Provide a way to verify the data

## Slide 12: A Lesson In Sharing: Pure Aloha
Circa 1970
Originally developed for terrestrial radio at Univ. of Hawaii, it illustrates the principles of a contention-based MAC protocol on any broadcast media.
Senders transmit whenever they want
If any two transmission over lap – even by one bit, they are garbled. This is called a collision.
  Unlike I2C, collisions destroy both frames.
  The distance makes it impossible for them to align. The bit time would need to be too long.
Collisions are detected by listening and verifying checksum.
Garbled frames are resent after a random delay.
Resent frames may also collide.
Resending frames does, of course, waste the channel

## Slide 13: A Lesson In Sharing: Pure Aloha
A
B
C
D
E

## Slide 14: A Lesson in Sharing: Slotted Aloha
Circa 1972
Stations agree on slot boundaries. These might be maintained by a special station that produces a timing signal.
Tolerance needs to be built in for timing signal’s transmission latency
Send only at beginning of slot.
This reduces the window of vulnerability to a single frame’s transmission time (1 slot)
Of course, if contention is low and collision is not likely, it will increase average transmission latency.

## Slide 15: Quick History: Slotted Aloha
A
B
C
D
E
tic
tic
tic
tic
tic
tic
tic
tic
tic
tic
tic
tic
tic

## Slide 16: Carrier Sense Multiple Access (CSMA)
What if, instead of using slots, we just “listen” first, and only transmit if no one else is?
This means that collisions would only occur in the event that two messages sent concurrently crosses paths after being started
The vulnerability to collisions is related to the latency
  More soon

## Slide 17: CSMA/CD
Another level of sophistication is the addition of collision detection.
Stations listen while transmitting
If a station hears something different than what it is sending, it immediate stops
What it hears is different from what it sends, if another transmission garbles the original.
Additionally, if any station detects a collision, it sends a jamming signal to make sure that the colliding signals don’t cancel each other out, preventing detection after attenuation.
This reduces the time wasted in the event of a collision sending already garbled packets.
IEEE 802.3 (including Ethernet) protocols are use CSMA/CD.

## Slide 18: Minimum Frame Size for CSMA/CD
Because of latency, collisions cannot be detected immediately. This signal from one transmitter much reach the other transmitter.
In practice, this imposes a minimum size on the length of a frame. The frame must be long enough to permit a collision to be detected.
If the frame is too short, it will be gone before the signal from one transmitter reaches another.
The frames will be corrupted as the “cross in the mail”
But neither sender will be able to detect it, until the whole frame has been sent, which defeats the purpose.

## Slide 19: Minimum Frame Size for CSMA/CD
The frame needs to be sufficiently long to require more than a round-trip time for transmission.
We must consider the bit-rate of the channel as well as its length to determine the round trip time.
The frame must require more than this round-trip time for transmission.
B bits/second
S seconds
B*S bit time
B*S
Sender1
Sender2
Sender2 detects the Collision almost immediately
Sender 1 must wait for its frame to (almost) make it to Sender2, when the collision occurs, and then for the energy from Sender2’s frame to make it back, before detecting the collision.

## Slide 20: Aside: “Ether” Net
Circa 1973
Robert Metcalf’s Memo @ Xerox PARC
Presented at 1976 National Computer Conference
CSMA/CD
3 Mbps
Key improvement of satellite based Aloha Net
  Backoff was exponential random, not just random
  More load = more retries = more delay
http://www.ieee802.org/3/ethernet_diag.html

## Slide 21: Aside: Ethernet Evolution Milestones
1988: Twisted Pair (Among other cabling)
1995: 100Mbps
  10 years after 1st standard
1997: Full duplex
1998: Gigabit (1000Mbps)
2002: 10 Gps (10,000Mbps)
2010: 40Gps and 100Gps standards
2017: 400Gps
https://en.wikipedia.org/wiki/Twisted_pair

## Slide 22: Gigabit Ethernet: Frame Size Challenge
Detecting Collision requires a frame size = RTT bit distance
  Without this a collision cannot be “heard” by the sender
As data rate increases
  Either minimum frame sizes increases
  Or maximum segment length decreases
Prior solutions cut network length
  20m wouldn’t quite cut it for gigabit ethernet

## Slide 23: Gigabit Ethernet Frame: Solution, Part 1
Add “extension” bits to make small frames larger
http://docwiki.cisco.com/wiki/Ethernet_Technologies

## Slide 24: Gigabit Ethernet Frame: Solution, Part 2
http://docwiki.cisco.com/wiki/Ethernet_Technologies
Allow a “burst” of frames
An extension in only required after the first one, so it is compliant
The IFG is filled with bits, so the carrier is never quiet.

## Slide 25
Addressing in Wired LANS: Ethernet Example
Each device connected to the network has a unique identification number given by the manufactory:
Media access control (MAC) address
Local Area Network (LAN)
1a:2b:3c:4d:5e:6f
Six 2-digit hex numbers
(Six 8-bit binary numbers)
On a PC: Example
MAC Address on a Printer
MAC address is also called as :
hardware address
physical address
machine address

## Slide 26
Sending a Message in Wired LANS
Wired Local Area Network (LAN)
MAC Address Data
1a:2b:3c:4d:5e:6f
1a:2b:3c:4d:5e:6f
A
Computer A sends a document to the printer to print via local network.

## Slide 27
Broadcast to Everyone on the LAN
Local Area Network (LAN)
MAC Address Data
1a:2b:3c:4d:5e:6f
1a:2b:3c:4d:5e:6f
A
It actually is broadcasted to all the devices connected to the network.

## Slide 28
Message Acceptance
Local Area Network (LAN)
MAC Address Data
1a:2b:3c:4d:5e:6f
1a:2b:3c:4d:5e:6f
A
MAC address is used to have destination device accept the document and all other devices reject.

## Slide 29
Message Collision
Local Area Network (LAN)
1a:2b:3c:4d:5e:6f
A
On this network, only one message is allowed at a time. Otherwise a “collision” happens. During a message on the network, others have to wait.

## Slide 30
Managing Collison with Switches
Switches can forward messages from one network leg to another without flooding the whole network.
For example, learning switches pay attention to the location of each station when it transmits and learn its location
  Then they send messages destined for that host to only the associated leg.
  Flooding to all legs only happens if the location of the host is unknown.
The internal design of the “switch fabric” can be very complex with shared memory, buffers, locking, etc.
  Different designs have different performance characteristics.
A
Local Area Network (LAN)
aa:aa:aa:aa:aa:aa
bb:bb:bb:bb:bb:bb
128.20.21.2
aa:aa:aa:aa:aa:aa Data
bb:bb:bb:bb:bb:bb Data
Switch

## Slide 31: Internally Buffered Crossbar Switches (IBCS)
One common baseline switch fabric architecture
N ports require N2 connections
Buffers can be placed in various locations to manage contention and avoid dropping messages due to collision
  Input queues
  Output queues
  Each point of connection
Output
Ports
Input
Ports

## Slide 32
Difference Between Hub and Switch
Local Area Network (LAN)
Hub links devices together with Ethernet cables.
Still a collision domain.
A switch forwards message only to the destination MAC address.
Can avoid collisions in many cases

## Slide 33: Outline
Today
Physical Layer
Link Layer
Network Layer
Transport Layer
Application Layer

## Slide 34
Application
Transport
Network
Physical
Link
The Network Layer
The decision making needed to steer a message from source to destination through an inter-network

## Slide 35
Computer Network: Internet
The Internet is a computer network
Interconnects billions of computing devices referred to as hosts or end systems.
Kurose & Ross, “Computer Networking”
Server
Internet Service Provider (ISP)
End systems connected by a network of communication links, such as coaxial cable, copper wire, optical fiber, and radio.
Transmission rate of a link measures in bits/second. E.g. Fiber: ~1Tbits/second.
Routers and switches forward messages towards their ultimate destination.
End systems access internet through ISPs (Internet Service Providers).

## Slide 36: The Network Layer: Addressing
Hierarchical addressing
  Venerable IPv4 addresses: 32-bits: Network# + Host Number
  IPv6 addresses: 128-bits and more structured
  Host number translated to LAN station ID, e.g by ARP between IPv4 and 802.11
Routing selects path to take from one network to another, often on a hop-by-hop basis
  Does this packet belong on one of my LANs? If so ARP and deliver
    If not, send upstream (or to a peer, or…)
This provides for an order of magnitude more hosts

## Slide 37: Network Layer: Addressing
http://www.tcpipguide.com/free/t_IPv6GlobalUnicastAddressFormat-4.htm
https://medium.com/hd-pro/cidr-addressing-and-subnet-masking-on-ip-networks-part-i-3054e3fbb0a1

## Slide 38: The Network Layer: Address Assignment
Old school: Go to system administrator and trade MAC address for IP address
Today: DHCP server automates this. Broadcast of request with MAC is answered with assigned IP
  Assigned IP is leased and needs to be renewed
  Assigned IP can be from dynamic pool
  Assigned IP can also be according to a pre-configured rule, such as to give a server a well-known address
  DHCP can also communicate other configuration information
DHCP isn’t technically part of the link layer.
  It is an Application Layer Service that supports it.

## Slide 39
Routing Among Networks
A
B

## Slide 40
Routing Among Networks
A
B

## Slide 41
Routing Among Networks
A
B

## Slide 42
Routing Among Networks
A
B

## Slide 43
Routing Among Networks
A
B
1
2
3
4

## Slide 44
A
B
Routing Among Networks
1
2
3
4

## Slide 45
Packet Switching: Store-and-Forward Transmission
Store-and-forward transmission:
Classically, a packet switch must receive the entire packet before it can begin to transit the first bit of the pack onto the outbound link.
Modern switches can actually begin after receiving and processing only the needed portions of the header
Switch
Time for the switch to receive the entire packet:
bits in each packet
transmission rate (bits per second)
Time for the switch to forward the entire packet after receiving:
Total switch delay:
Total switch delay for N links:

## Slide 46
Packet Switching: Queuing Delays and Packet Loss
Each packet switch has multiple links attached to it. For each attached link, the packet switch has an output buffer (also called output queue), which stores packets that the router is about to send into that link.
Packet Loss: When output buffer is full, either the arriving packet or one of the already-queued packet will be dropped.
Queuing Delay: Output link is busy for transmitting an arriving packet.

## Slide 47
Queuing Delay
Packet arrival rate: Number of packets arriving per second
a
Traffic intensity
Queueing delay = 0
Queueing delay diverges…
Link transmission rate (bits per second)

## Slide 48: Outline
Today
Physical Layer
Link Layer
Network Layer
Transport Layer
Application Layer

## Slide 49
Application
Transport
Network
Physical
Link
The Transport Layer
The messages sent and received by application programs
The end-to-end connection as seen by a programmer
The decision making needed to steer a message from source to destination through an inter-network
The management of the physical channel for communication
The specification for the hardware that enables the signaling between or among devices

## Slide 50: Transport Layer: Meaningful Endpoints
Hosts don’t communication – various aspects of software systems do
  Consider how many different sessions your Web browser has with servers. Now add for your IM sessions, upgrades-in-progress, music streaming, etc.
Endpoints enable the establishment of sessions
  Classic model is <<IP:port>:<IP:port>>
  Client: Ephemeral port
  Host: Well-known port

## Slide 51: Transport Layer: Meaningful Paradigm
Character of communication
  Reliable/session-oriented, e.g. TCP
  Unreliable/datagram, e.g. UDP
  Etc.
The transport layer exists once we have the ability to establish communication from end-point to end-point with well-understood properties

## Slide 52: Transport Layer: User Datagram Protocol (UDP)
Reminder: Port numbers in addition to IP addresses
Best effort = Unreliable
  Messages can be lost or reordered
  Message corruption is assumed to be detected at the link layer
Message oriented. Max message size
Simple
Used for timely updates, e.g. send audio or video for teleconferencing

## Slide 53: Background: Reliable Protocol vs Reliable Media The Two Armies Parable
“Attack at dawn”?
Red army in the hills, but divided.
Blue army in the valley.
Red army can defeat blue army, but only if the two elements coordinate an attack at the same time, otherwise it will be defeated
All communication is by messenger (in the challenging environment of war)

## Slide 54: Transport Layer: Reliable Protocols
Keeps trying to send data until it succeeds or times out
Used acknowledgements to determine that it does not need to resent
Buffers to ensure in-order delivery, which allows head-of-line blocking
Messages are assumed to be correct or undelivered via checksums at link layer
  “Byzantine Failures” are possible, occur commonly at Internet scale, but infrequent enough to be (mostly) ignored. Maybe.
Can’t guarantee delivery.
  At best can trade timeliness for delivery

## Slide 55: Transport layer: Stop-And-Wait Protocols
Send a message. Wait one fully network latency for it to get to the recipient. Wait for the recipient to process it. Wait another full network latency to send back the acknowledgement
  In one round-trip time (RTT), only one message is sent.
  RTT sec * bits/sec = total bits we can send in that time.
  Size of message is what we actually sent. Rest of time is wasted waiting.

## Slide 56: Transport layer: Sliding Window
Buffer enough data on sender to keep sending for the entire RTT.
Treat sending buffer as circular: As ACKs come back, “slide window” to buffer new data, releasing old data and keep sending.
If ACK doesn’t come back in time, resend data.
  Head-of-line blocking is possible
Keep buffer an receiver in sync with sender to buffer, releasing segments up the stack in order.
Requires segments, segment numbers

## Slide 57: Transport Layer: Sliding Window
seq. numbers
LAR
LFS
Acknowledged packets
Packets not acknowledged yet
  LAR (last ACK received)
  LFS (last frame sent)

## Slide 58: Transport layer: Sliding Window, Cont.
Receiver
Sender
…
…
Sent & Acked
Sent Not Acked
OK to Send
Not Usable
…
…
Max acceptable
Receiver window
Max ACK received
Next seqnum
Received & Acked
Acceptable Packet
Not Usable
Sender window
Next expected
Credit:
Hui Zhang

## Slide 59: Transport Layer: Transmission Control Protocol (TCP)
Reminder: Port numbers in addition to IP addresses
Used for transmissions that need to be correct, but not timely
  Streaming audio or video, e.g. recorded movies
  Bulk data transfer, e.g. uploads or downloads
Requires overhead of establishing a session to maintain shared state between sender and receiver to coordinate.
Different schemes for ACKs
  Delayed ACKs, Cumulative ACKs, Selective ACKs

## Slide 60: Transport Layer: Transmission Control Protocol (TCP)
Congestion Control
  Packet loss can be due to many types of failure, including congestion
  If congestion, desire is to slow down.
  Slowing down can be achieved by shrinking window, which leaves network time unused
  TCP has different strategies it can use to determine when to slow down and how to speed back up.
3-Way Handshake: SYN, SYN-ACK, ACK-SYN
  Establishes session, negotiates window sizes and other options, e.g. SACK, window sizes, etc.

## Slide 61: Application Layer: Purposeful Communication
Defined by the messaging we, as programs, bake into our applications, shaped by our applications,
  e.g. client-server interactions, peer-to-peer interactions, etc.
E.g.
  HTTP: PUT, GET, POST, etc
  E.g DNS: queries, responses, updates, etc.
  MIME, VOIP protocols, etc.
  Application protocols exist when applications can communicate

## Slide 62
Computer Network: Summary: Layered Structure

## Slide 63
Application
Transport
Network
Physical
Link
Application Layer
The messages sent and received by application programs
The end-to-end connection as seen by a programmer
The decision making needed to steer a message from source to destination through an inter-network
The management of the physical channel for communication
The specification for the hardware that enables the signaling between or among devices

## Slide 64: Hyper Text Transport Protocol (HTTP)
Unique name for a file: URL (Universal Resource Locator)
Example URL: http://www.cmu.edu:80/index.html
Clients use prefix (http://www.cmu.edu:80) to infer:
  What kind (protocol) of server to contact (HTTP)
  Where the server is (www.cmu.edu)
  What port it is listening on (80)
Servers use suffix (/index.html) to:
  Determine if request is for static or dynamic content.
    No hard and fast rules for this
    One convention: executables reside in cgi-bin directory
  Find file on file system
    Initial “/” in suffix denotes home directory for requested content.
    Minimal suffix is “/”, which server expands to configured default filename (usually, index.html)

## Slide 65: HTTP Requests
HTTP request is a request line, followed by zero or more request headers
Request line: <method> <uri> <version>
  <method> is one of GET, POST, OPTIONS, HEAD, PUT, DELETE, or TRACE
  <uri> is typically URL for proxies, URL suffix for servers
    A URL is a type of URI (Uniform Resource Identifier)
    See http://www.ietf.org/rfc/rfc2396.txt
  <version> is HTTP version of request (HTTP/1.0 or HTTP/1.1)
Request headers: <header name>: <header data>
  Provide additional information to the server
Notes: Request header examples: brand name of the browser, domain name of the origin server

## Slide 66: HTTP Responses
HTTP response is a response line followed by zero or more response headers, possibly followed by content, with blank line (“\r\n”) separating headers from content.
Response line:
<version> <status code> <status msg>
  <version> is HTTP version of the response
  <status code> is numeric status
  <status msg> is corresponding English text
    200 OK Request was handled without error
    301 Moved Provide alternate URL
    404 Not found Server couldn’t find the file
Response headers: <header name>: <header data>
  Provide additional information about response
  Content-Type: MIME type of content in response body
  Content-Length: Length of content in response body

## Slide 67: Example HTTP Transaction
whaleshark> telnet www.cmu.edu 80 Client: open connection to server
Trying 128.2.42.52... Telnet prints 3 lines to terminal
Connected to WWW-CMU-PROD-VIP.ANDREW.cmu.edu.
Escape character is '^]'.
GET /index.shtml HTTP/1.1 Client: request line
Host: www.cmu.edu Client: required HTTP/1.1 header
Client: blank line terminates headers
HTTP/1.1 200 OK Server: response line
Date: Wed, 05 Nov 2014 17:37:26 GMT Server: followed by 4 response headers
Server: Apache/1.3.42 (Unix)
Transfer-Encoding: chunked
Content-Type: text/html; charset=...
Server: empty line terminates headers
1000 Server: begin response body
<html ..> Server: first line of HTML content
…
</html>
0 Server: end response body
Connection closed by foreign host. Server: close connection

## Slide 68: Domain Name System
Old school
  Let “The Keeper of All Things” know about a hostname:IP assignment in your organization
  The Keeper updates a “hosts” text file with the information
  Periodically download this file to keep your system up to date
  Obvious scalability problems, but /etc/hosts still exists vestigially and for special cases
Today
  Domain Name System (DNS) is a distributed data base that delegates assignments for information to the responsible domains and can direct queries to the servers associated with those domains.
  Uses caching for efficiency.
  We’ll talk about it later in detail
DNS isn’t technically part of the network layer.
  It is an Application Layer Service that supports it.

## Slide 69: DNS Example
https://clouddocs.f5.com/training/community/dns/html/class4/module1/lab4.html

## Slide 70
Application
Transport
Network
Physical
Link
Wrapping Up
The messages sent and received by application programs
The end-to-end connection as seen by a programmer
The decision making needed to steer a message from source to destination through an inter-network
The management of the physical channel for communication
The specification for the hardware that enables the signaling between or among devices

## Slide 71
Computer Network: Summary: Layered Structure
http://books.gigatux.nl/mirror/snortids/0596006616/snortids-CHP-2-SECT-2.html

## Slide 72: End-To-End Argument
“Functions placed at low levels of a system may be redundant or of little value when compared with the cost of providing them at that low level.”
“Low-level mechanisms to support these functions are justified only as performance enhancements.”
  Unless there is a reason, do it at a higher layer: One might not need to do it at all.
Error Detection Example: Link Layer or Transport layer?
  Probably link layer: Who wants bad data? Why pass it up?
Error Correction Example: Link Layer or Transport layer?
  Probably transport layer: Late may be of no value. Redundancy may be too costly.
  But, then there are very high error channels that wouldn’t be viable without forward error correction, e.g. redundancy baked in
Encryption Example: Link Layer or Transport Layer?
  Probably transport layer: May not be needed + “Person In The Middle”, i.e. the messengers that can se it along the way.

## Slide 73: Enjoy Carnival!
See you Tuesday!