# Stress analysis of truss_structure_final

### Author: Nicholas Selman, Richard Pantaleo, Jason Calaiaro

### Company: RNJ Solutions

### Date: 5.7.2007

- Introduction

- File Information

- Materials

- Load & Restraint Information

- Study Property

- Contact

- Stress Results

- Strain Results

- Displacement Results

- Deformation Results

- Design Check Results

- Appendix

## 1. Introduction

Summarize the FEM analysis on truss_structure_final

### Note:

Do not base your design decisions solely on the data presented in this report. Use this information in conjunction with experimental data and practical experience. Field testing is mandatory to validate your final design. COSMOSWorks helps you reduce your time-to-market by reducing but not eliminating field tests.

## 2. File Information

| Model name: | truss_structure_final |
| --- | --- |
| Model location: | C:\Users\Nick\Documents\CMU\2006-2007\Stress Analysis\Design Project\truss_structure_final.SLDPRT |
| Results location: | C:\Program Files\SolidWorks\COSMOS\work |
| Study name: | Study 2 (-Default-) |

## 3. Materials

| No. | Part Name | Material | Mass | Volume |
| --- | --- | --- | --- | --- |
| 1 | truss_structure_final | 1060 Alloy | 0.317661 kg | 0.000117652 m^3 |

## 4. Load & Restraint Information

| Restraint Restraint-1 <truss_structure_final> | on 4 Edge(s) fixed. |  |
| --- | --- | --- |
| Description: |  |

| Load Force-1 <truss_structure_final> | on 1 Edge(s) apply force 1 lb normal to reference plane with respect to selected reference Edge< 1 > using uniform distribution | Sequential Loading |
| --- | --- | --- |
| Description: |  |

## 5. Study Property

| Mesh Information Mesh Type: | Solid mesh |
| --- | --- |
| Mesher Used: | Standard |
| Automatic Transition: | Off |
| Smooth Surface: | On |
| Jacobian Check: | 4 Points |
| Element Size: | 0.19297 in |
| Tolerance: | 0.0096487 in |
| Quality: | High |
| Number of elements: | 39508 |
| Number of nodes: | 89382 |

| Solver Information Quality: | High |
| --- | --- |
| Solver Type: | FFEPlus |
| Option: | Include Thermal Effects |
| Thermal Option: | Input Temperature |
| Thermal Option: | Reference Temperature at zero strain: 298 Kelvin |

## 6. Contact

### Contact state: Touching faces - Bonded

## 7. Stress Results

| Name | Type | Min | Location | Max | Location |
| --- | --- | --- | --- | --- | --- |
| Plot1 | VON: von Mises stress | 218.929 N/m^2; . Node: 32816; . | (-2.71673 in,; . 0.015625 in,; . 4.74219 in); . | 2.12239e+007 N/m^2; . Node: 6287; . | (-6 in,; . 4.09375 in,; . 12.75 in); . |

truss_structure_final-Study 2-Stress-Plot1 JPEG

; .

## 8. Strain Results

| Name | Type | Min | Location | Max | Location |
| --- | --- | --- | --- | --- | --- |
| Plot1 | ESTRN: Equivalent strain | 2.13076e-009 ; . Element: 33634; . | (-2.71573 in,; . 0.015625 in,; . 4.78906 in); . | 0.000156667 ; . Element: 22153; . | (-5.99219 in,; . 4.10937 in,; . 12.7031 in); . |

truss_structure_final-Study 2-Strain-Plot1 JPEG

; .

## 9. Displacement Results

| Name | Type | Min | Location | Max | Location |
| --- | --- | --- | --- | --- | --- |
| Plot1 | URES: Resultant displacement | 0 m; . Node: 5429; . | (-6 in,; . 0 in,; . 5.03125 in); . | 0.000251184 m; . Node: 11557; . | (-28 in,; . 9.125 in,; . 12.75 in); . |

truss_structure_final-Study 2-Displacement-Plot1 JPEG

; .

## 10. Deformation Results

| Plot No. | Scale Factor |
| --- | --- |
| 1 | 288.23 |

truss_structure_final-Study 2-Deformation-Plot1 JPEG

; .

## 11. Design Check Results

truss_structure_final-Study 2-Design Check-Plot1 JPEG

; .

## 12. Appendix

| Material name: | 1060 Alloy |
| --- | --- |
| Description: |  |
| Material Source: | Library files |
| Material Library Name: | cosmos materials |
| Material Model Type: | Linear Elastic Isotropic |

| Property Name | Value | Units | Value Type |
| --- | --- | --- | --- |
| Elastic modulus | 6.9e+010 | N/m^2 | Constant |
| Poisson's ratio | 0.33 | NA | Constant |
| Shear modulus | 2.7e+010 | N/m^2 | Constant |
| Mass density | 2700 | kg/m^3 | Constant |
| Tensile strength | 6.8936e+007 | N/m^2 | Constant |
| Yield strength | 2.7574e+007 | N/m^2 | Constant |
| Thermal expansion coefficient | 2.4e-005 | /Kelvin | Constant |
| Thermal conductivity | 200 | W/(m.K) | Constant |
| Specific heat | 900 | J/(kg.K) | Constant |
| Hardening factor (0.0-1.0; 0.0=isotropic; 1.0=kinematic) | 0.85 | NA | Constant |